## Slide 1: Outline of today’s session
What is a binary code?
Where it is used?
Classification of binary codes
Various binary codes
Problems

## Slide 2: What is a binary code?
The group of symbols is called as a code. The digital data is represented, stored and transmitted as group of binary bits.
This group is also called as binary code.
It is a coding system using the binary digits 0 and 1 to represent a letter, digit, or other character in a computer or other electronic device.

## Slide 3: Where it is used?
Binary codes are suitable for the computer applications.
Binary codes are suitable for the digital communications.
Binary codes make the analysis and designing of digital circuits if we use the binary codes.
Since only 0 & 1 are being used, implementation becomes easy.

## Slide 4: Classification of binary codes

## Slide 5: Weighted Codes
Weighted binary codes are those binary codes which obey the positional weight principle.
Each position of the number represents a specific weight.
Several systems of the codes are used to express the decimal digits 0 through 9.
In these codes, each decimal digit is represented by a group of four bits.

## Slide 6: Binary coded Decimal(BCD)
BCD is a 4-bit binary code representation of a decimal digit which uses four bits to represent the 10 decimal digits of 0 to 9.
The weights are 8,4,2,1.
There are six invalid code words: 1010, 1011, 1100, 1101,1110, 1111

## Slide 7: Other BCD codes

## Slide 8: Conversion Vs Coding

## Slide 9: Non weighted codes
Non-weighted or un-weighted codes are those codes in which the digit value does not depend upon their position i.e., each digit position within the number is not assigned fixed value.
Examples of non-weighted codes are:
  Un-weighted BCD code
  Gray code
  Excess-3 code

## Slide 10: Gray code
Developed by Frank Gray.
It is also called cyclic or mirror code or minimum error code or unit distance code
Each code word differs in only one bit from its neighbor code word.
But in binary, the number of bits that change from one binary value to next value varies

## Slide 11: How is Gray reflective?

## Slide 12: Excess-3 code
The Excess-3 code is also called as XS-3 code.
It is non-weighted code used to express decimal numbers.
The Excess-3 code words are derived from the 8421 BCD code words adding (0011)2 or (3)10 to each code word in 8421.
The excess-3 codes are obtained as follows :

## Slide 13: BCD Excess 3

## Slide 14: Sequential code
A code is said to be sequential when two subsequent codes, seen as numbers in binary representation, differ by one.
This greatly aids mathematical manipulation of data.
The 8421 and Excess-3 codes are sequential, whereas the 2421 and 5211 codes are not.

## Slide 15: Reflective code
A code is reflective when the code is self complementing.
In other words, when the code for 9 is the complement the code for 0, 8 for 1, 7 for 2, 6 for 3 and 5 for 4.
2421BCD, 5421BCD and Excess-3 code are reflective codes.

## Slide 16: Error Detecting and correcting codes
When bits are transmitted over the computer network, they are subject to get corrupted due to interference and network problems.
Error detection is the detection of errors caused by noise or other impairments during transmission from the transmitter to the receiver. Error correction is the detection of errors and reconstruction of the original, error-free data.

## Slide 17: Error detection-Parity
Parity check is done by adding an extra bit, called parity bit to the data to make number of 1s either even in case of even parity, or odd in case of odd parity.
The sender counts the number of 1s in it and adds the parity bit in following way:
  In case of even parity: If number of 1s is even then parity bit value is 0. If number of 1s is odd then parity bit value is 1.
  In case of odd parity: If number of 1s is odd then parity bit value is 0. If number of 1s is even then parity bit value is 1.
On receiving a frame, the receiver counts the number of 1s in it. In case of even parity check, if the count of 1s is even, the data is accepted, otherwise it is rejected. Similar rule is adopted for odd parity check.
Parity check is suitable for single bit error detection only.

## Slide 19: Error Correction-Hamming
Hamming code is a block code that is capable of detecting up to two simultaneous bit errors and correcting single-bit errors.
It is technique developed by R.W. Hamming for error correction.
Hamming codes are used in many applications where such errors are common, including DRAM memory chips and satellite communication hardware.

## Slide 20: ASCII code
The ASCII stands for American Standard Code for Information Interchange.
The ASCII code is an alphanumeric code used for data communication in digital computers.
The ASCII is a 7-bit code capable of representing 27 or 128 number of different characters.
The ASCII code is made up of a three-bit group, which is followed by a four-bit code.

## Slide 21: EBCDIC code
The EBCDIC stands for Extended Binary Coded Decimal Interchange Code.
IBM invented this code to extend the Binary Coded Decimal which existed at that time.
All the IBM computers and peripherals use this code.
It is an 8 bit code and therefore can accommodate 256 characters.

## Slide 22: Problems
Write a BCD code for the weight 84-2-1.
Write the Biquinary code 05-01234.
Note: code comprises both a two-state (bi) and a five-state (quinary) component.
iii. Represent 8620 in (a) BCD (b) 2421
(c) Excess-3 (d) binary
iv. List the ten BCD digits with an even parity in the left-most position. Repeat it with odd parity also.

## Slide 23
THANK YOU