## Slide 1: Outline of today’s session
Exclusive OR operation
Binary to Gray conversion
Gray to Binary conversion
Binary to BCD
BCD to Binary
BCD to Excess 3
Excess3 to BCD
BCD Addition

## Slide 2: Exclusive-OR Operation
“A OR B but NOT both” will give an output at Q
An Ex-OR gate will give an output value of logic “1” ONLY when there are an ODD number of 1's on the inputs.
If the two numbers are equal, the output is “0”.

## Slide 3: Binary ↔ Gray
The M.S.B. of the gray code will be exactly equal to the first bit of the given binary number.
The second bit of the code will be exclusive-OR of the first and second bit of the given binary number, i.e if both the bits are same the result will be 0 and if they are different the result will be 1.
The third bit of gray code will be equal to the exclusive-OR of the second and third bit of the given binary number.
Thus the Binary to gray code conversion goes on.

## Slide 4: Example: Binary ↔ Gray
Convert (11101)2 to Gray
(11101)2= (10011)Gray

## Slide 5: Gray ↔ Binary
The Most Significant Bit (MSB) of the binary code is always equal to the MSB of the given binary number.
Other bits of the output binary code can be obtained by checking gray code bit at that index. If current gray code bit is 0, then copy previous binary code bit, else copy invert of previous binary code bit.

## Slide 6: Example: Gray ↔ Binary
Convert (10011)Gray to Binary
(10011)Gray = (11101)2

## Slide 7: Problems
Convert Binary to Gray.
0011
01001
101011
111000
Convert Gray to Binary.
100111
111001
100110
001110

## Slide 8: Binary ↔ BCD
Step 1 -- Convert the binary number to decimal.
Step 2 -- Convert decimal number to BCD.
Example − Convert (11101)2 to BCD.
Step 1 − Convert to Decimal
Step 2 − Convert to BCD
Result (11101)2 = (00101001)BCD

## Slide 9: BCD ↔Binary
Step 1 -- Convert the BCD number to decimal.
Step 2 -- Convert decimal to binary.
Example − convert (00101001)BCD to Binary.
Step 1 - Convert to Decimal Step 2 - Convert to Binary
Result : (00101001)BCD = (11101)2

## Slide 10: BCD ↔Excess 3
Step 1 -- Convert BCD to decimal.
Step 2 -- Add (3)10 to this decimal number.
Step 3 -- Convert into binary to get excess-3 code.
Example − convert (1001)BCD to Excess-3.
Step 1 − Convert to decimal
(1001)BCD = 910
Step 2 − Add 3 to decimal
(9)10 + (3)10 = (12)10
Step 3 − Convert to Excess-3
(12)10 = (1100)2
Result : (1001)BCD = (1100)XS-3

## Slide 11: Excess 3 ↔ BCD
Step 1: Subtract (0011)2 from each 4 bit of excess-3 digit to obtain the corresponding BCD code.
Example : Convert (10011010)XS-3 to BCD.
Given XS-3 number = 1 0 0 1 1 0 1 0
Subtract (0011)2 = 0 0 1 1 0 0 1 1
-----------------------
BCD = 0 1 1 0 0 1 1 1
Result : (10011010)XS-3 = (01100111)BCD

## Slide 12: Problems
Convert the following binary numbers to BCD:
  101010
  111000
Convert the following BCD numbers to binary:
  1001 0000
  0101 0110
Convert the following BCD numbers to Excess3:
  0100 0101
  1000 0111
Convert the following Excess3 numbers to BCD:
  0101 0110
  0011 0101

## Slide 13: BCD Addition
The rules are given below in three steps:
At first the given number are to be added using the rule of binary.
In second step we have to judge the result of addition.
  The result of addition of two binary number is greater than 9, which is not valid for BCD number.
  The result of addition is less than 9, which is valid for BCD numbers.
If the four bit result of addition is greater than 9 and if a carry bit is present in the result then it is invalid and we have to add 6 whose binary equivalent is (0110)2 to the result of addition. Then the resultant that we would get will be a valid binary coded number.

## Slide 14: Example: BCD Addition
In case 1 the result of addition of two binary number is greater than 9, which is not valid for BCD number.
In case 2 is less than 9, which is valid for BCD numbers.
So, in case 1 the result was (1111)2, which is greater than 9 so we have to add 6 or (0110)2 to it.

## Slide 18: Problems
Perform BCD addition:
13+19
98+89
974+595
3475+1353

## Slide 19
THANK YOU