## Slide 1: UNIT-1: Outcomes
Students will be able to:
Understand number systems.
Convert from one number system to another number system.
Determine r’s and (r-1)’s complement of a number.
Understand complements of numbers, subtraction using complements.
Perform addition and subtraction of signed and unsigned numbers.
Understand Weighted and un-weighted binary codes.

## Slide 2: Outline of today’s session
What is a number system?
Base or radix
Weight of a digit
Types of number systems
  Binary number system
  Decimal number system
  Octal number system
  Hexa decimal number system

## Slide 3: What is a Number System?
A number system is a writing system for expressing numbers.
Set of rules and symbols to represent numbers.
A mathematical notation for representing numbers of a given set, using digits or other symbols in a consistent manner.

## Slide 4: BASE or Radix
A base of a number system or radix defines the range of values that a digit may have.
It also defines the number of different values in the number system.
A number system of base r , has a set of r allowed digits :
{ 0, 1, 2, ….. ,r-1}
A number N with base r is represented as:
(N)r

## Slide 6: Weight of a digit
The weight of the digit in each position is the base of the number system raised to the power of the position number.
The value of the number is than calculated by multiplying the value of the digit in each position by the base raised to the power of that position and then summing the products.

## Slide 9: Types of Number systems
Binary number system
Decimal number system
Octal number system
Hexa decimal number system

## Slide 10: Usage
We use Decimal system
Computers use  Binary system
Digital displays, Unix systems  Octal system
String representation  Hexa decimal system

## Slide 11: BINARY (BASE 2) NUMBER SYSTEM
Digital and computer technology is based on the binary number system,.
Has two states: ON or OFF.
Each bit must be less than 2 which mean it has to be either 0 or 1.
Each bit is weighted based on its position in the sequence (powers of 2) from the Least Significant Bit (LSB) to the Most Significant Bit (MSB).

## Slide 12: What is MSB and LSB?

## Slide 13
Weighing factors (or weights) are in powers of 2.
… 23 22 21 20 . 2-1 2-2 2-3 …
Ex: 1101.1012 = 123 + 122 + 120 + 12-1 + 12-3

## Slide 14: OCTAL (BASE 8) NUMBER SYSTEM
Octal digits: 0, 1, 2, 3, 4, 5, 6, 7.
Weighing factors (or weights) are in powers of 8:
… 83 82 81 80 . 8-1 8-2 8-3 …
Example
56.28 = (5 x 81) + (6 x 80) + (2 x 8-1)

## Slide 15: DECIMAL (BASE 10) SYSTEM
Base or radix is 10 .
Decimal digits = { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Weighing factors (or weights) are in powers of 10:
… 103 102 101 100 . 10-1 10-2 10-3 …
Example, the 9 in the two numbers below has different values:
(7594)10= (7 × 103) + (5 × 102) + (9 × 101) + (4 × 100)
(912)10 = (9 × 102) + (1 × 101) + (2 × 100)

## Slide 16: HEXADECIMAL (BASE 16) NUMBER SYSTEM
Hexadecimal has sixteen values 0 to 15, but to keep all these values in a single column, the 16 values (0 to 15) are written as 0 to F, using the letters A to F to represent numbers 10 to 15.
Hexadecimal digits: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F.
Weighing factors (or weights) are in powers of 16:
… 163 162 161 160 . 16-1 16-2 16-3 …
Example
98.216 = (9 x 161) + (8 x 160) + (2 x 16-1)

## Slide 17: Summary

## Slide 19
THANK YOU