## Slide 1: Outline of today’s session
Need of complements
What is a complement?
Types of complements
Decimal complements
  10’s complement
  9’s complement
Binary complements
  2’s complement
  1’s complement
Unsigned numbers

## Slide 2: Need of complements
In mathematics and computing, the method of complements is implemented so that we can use the same algorithm (hardware) for addition throughout the whole range.
Mainly used for simplifying subtraction. Thus subtraction of any number is implemented by adding its complement.

## Slide 3: What is complement?
Complements are used in the digital computers in order to simplify the subtraction operation and for the logical manipulations.
For each radix-r system (radix r represents base of number system) there are two types of complements:
  Radix complement (or) r’s complement
  Dimnished Radix complement (or) (r-1)’s complement
For example:
r=10, we have 10’s and 9’s complements
r=2, we have 2’s and 1’s complements
r=8, we have 8’s and 7’s complements

## Slide 4: r’s and (r-1)’s complement
r’s complement of a number N, with n digits in base r is calculated as:
(r-1)’s complement of a number N, with n digits in base r is calculated as:
Note:
(r-1)’s complement is obtained by subtracting 1 from r’s complement
(or)
r’s complement is obtained by adding 1 to (r-1)’s complement
(rn-N)
(rn-1)-N

## Slide 5: Decimal System Complements
10's complement : (10n – N)
where n = number of digits in the number.
Ex: 10’s complement of 456:
    =103-456
    =1000-456
    =544
9's complement : (10n –1)-N
where n = number of digits in the number.
Ex: 9’s complement of 456:
    =(103-1)-456
    =(1000-1)-456
    =999-456
    =543

## Slide 6: Direct method to calculate decimal complements
To get 10’s complement of number, scan the number from right to left, subtract the first non-zero digit from 10 and remaining digits from 9.
To get 9’s complement of number, subtract each digit of a number from 9.
Ex: Complement of 12389
  10’s complement : 87611
  9’s complement : 87610

## Slide 7: Binary Subtraction
Note: Subtracting a binary digit from 1 just complements it
1-0=1
1-1=0

## Slide 8: Binary Addition

## Slide 9: Binary System Complements
2's complement : (2n – N)
where n = number of digits in the number.
Ex: 2’s complement of 101:
    =23-101
    =1000-101
    =011
1's complement : (2n –1)-N
where n = number of digits in the number.
Ex: 1’s complement of 101:
    =(23-1)-101
    =(1000-1)-101
    =111-101
    =010
How 23=1000?
24=10000?
25=100000?

## Slide 10: Direct method to calculate binary complements
To get 2’s complement of number, scan the number from right to left, subtract the first non-zero digit i.e., 1 from 2 and remaining digits from 1.
To get 1’s complement of number, change 01 and 10
Ex: Complement of 10101
  2’s complement : 01011
  1’s complement : 01010

## Slide 13: Direct method to calculate complements
To get r’s complement of number, scan the number from right to left, subtract the first non-zero digit from r and remaining digits from r-1.
To get 1’s complement of number, subtract each digit of a number from r-1.

## Slide 14: Some examples…

## Slide 16: Problems
Calculate 10’s and 9’s complements of the following:
  12349876
  00000000
  546700
  012398
Calculate 2’s and 1’s complements of the following:
  1011101
  11001011
  01010
  11110
  1011001
  001100
  000000

## Slide 17: Unsigned Numbers
Unsigned binary numbers are, by definition, positive numbers and thus do not require an arithmetic sign.
An m-bit unsigned number represents all numbers in the range 0 to 2m − 1.
For example, the range of 8-bit unsigned binary numbers is from 0 to 25510 in decimal and from 00 to FF16 in hexadecimal.
Similarly, the range of 16-bit unsigned binary numbers is from 0 to 65,53510 in decimal and from 0000 to FFFF16 in hexadecimal.

## Slide 18
THANK YOU