## Slide 1: Outline of today’s session
Unsigned numbers
Unsigned Binary arithmetic
  Addition
  Subtraction
  Multiplication
Problems

## Slide 2: Unsigned numbers
Unsigned numbers don’t have any sign, these can contain only magnitude of the number. So, representation of unsigned binary numbers are all positive numbers only.
Unsigned binary numbers are, by definition, positive numbers and thus do not require an arithmetic sign.

## Slide 4: Representation of Unsigned Binary Numbers
Since there is no sign bit in this unsigned binary number, so N bit binary number represent its magnitude only.
Zero (0) is also unsigned number. This representation has only one zero (0), which is always positive.
Every number in unsigned number representation has only one unique binary equivalent form, so this is unambiguous representation technique.
The range of unsigned binary number is from 0 to (2n-1).

## Slide 6
Find range of 5 bit unsigned binary numbers. Also, find minimum and maximum value in this range.
The range of unsigned binary number is from 0 to (2n-1).
Therefore, range of 5 bit unsigned binary number is from 0 to (25-1) which is equal from minimum value 0 (i.e., 00000) to maximum value 31 (i.e., 11111).
5 bits: range is 0 to 31

## Slide 7
Represent decimal number 92 in unsigned binary number.
  = (92)10
  = (1x26+0x25+1x24+1x23+1x22+0x21+0x20)10
  = (1011100)2
It’s 7 bit binary magnitude of the decimal number 92.

## Slide 8: Unsigned Arithmetic
Addition
Subtraction(done by complements)
Multiplication

## Slide 9: Unsigned Addition

## Slide 10: Unsigned Addition
0+0 = 0, with no carry, 1+0 = 1, with no carry, 0+1 = 1, with no carry, 1+1 = 0, and you carry a 1

## Slide 11: Unsigned Subtraction

## Slide 12: Unsigned Subtraction(complements)
For unsigned, there is no answer to A−B, because negative numbers cannot be represented. So,
A-B=A+(-B)

## Slide 13: Unsigned Multiplication

## Slide 14: Problems
20+40
50-30
125+34
34-12
Note: convert to binary and perform the operation

## Slide 15
THANK YOU