## Slide 1: Outline of today’s session
Introduction
Methods to represent signed numbers
  Signed magnitude
  Signed Complement
    2’s complement
    1’s complement
Problems

## Slide 2: Introduction
Signed number representations are required to encode negative numbers in binary number systems.
Negative numbers in decimal or any other base are represented by prefixing them with a minus sign ("−").
But in computer hardware, numbers are represented only as sequences of bits, without extra symbols. So various methods are adopted for representing negative numbers.

## Slide 3: How to represent signed numbers?
Signed Binary number representations
1’s complement
2’s complement
Signed magnitude
Complement

## Slide 4: Signed magnitude representation
For n bit binary number, 1 bit is reserved for sign symbol. If the value of sign bit is 0, then the given number will be positive, else if the value of sign bit is 1, then the given number will be negative.
Remaining (n-1) bits represent magnitude of the number. Since magnitude of number zero (0) is always 0, so there can be two representation of number zero (0), positive (+0) and negative (-0), which depends on value of sign bit.
Hence these representations are ambiguous generally because of two representation of number zero (0). Generally sign bit is a most significant bit (MSB) of representation.
The range of Sign-Magnitude form is from
-(2(n-1)-1) to +(2(n-1)-1).

## Slide 5: Signed magnitude representation
The most significant bit of a binary number is used to represent the sign bit. If the sign bit is equal to zero, the signed binary number is positive; otherwise, it is negative. The remaining bits represent the actual number.

## Slide 6: Range of values in signed magnitude
Largest representable magnitude, in this method, is (2n-1-1)
Range of numbers:
-(2n-1-1), … , -1, -0, +0, +1, …, +(2n-1-1)
For example, an 8-bit register, the leftmost bit is a sign bit, which leaves 7 bits to represent the magnitude.
The largest magnitude representable in 7-bits
2(8-1)-1 =127
A signed number has:
  Magnitude (or absolute value)
  Sign (positive or negative)
  Everything has to be in binary (0s and 1s)

## Slide 7: Positive signed binary numbers
Negative signed binary numbers

## Slide 9: Complement representation
Subtraction: A – B = A + (-B) = A + B’
  A negative number is represented with its complement
  Note that B = (B’)’
Two types of complements for each base-r
  (r-1)’s complement
    1’s complement
  r’s complement
    2’s complement

## Slide 10: 1’s complement representation
In one's complement form, a negative number is the 1's complement of its positive number.
In this scheme:
if the binary number 0102 encodes the signed integer 210, then its one's complement, 1012, encodes the inverse: −210.

## Slide 11: Range of values in 1’s complement representation
Range of numbers: - The range of 1’s complement form is from -(2(n-1)-1) to (2(n-1)-1)
-(2n-1-1), … , -1, -0, +0, +1, …, +(2n-1-1)

## Slide 12: 2’s complement representation
In two's complement form, a negative number is the 2's complement of its positive number.
In this scheme:
if the binary number 0102 encodes the signed integer 210, then its two's complement, 1102, encodes the inverse: −210.

## Slide 13: Range of values in 2’s complement representation
Range of numbers: - (2(n-1)) to (2(n-1)-1).
-2n-1, … , -1,+0, +1, …, +(2n-1-1)
Note: There will no -0

## Slide 16: Disadvantage with signed magnitude and 1’s complement
The disadvantage is that there are two notations for 0 in signed magnitude and 1’s complement, which is very inconvenient when the computer wants to test for a 0 result.
  Signed magnitude : +0(0000), -0(1000)
  1’s complement : +0(0000), -0(1111)

## Slide 17: Problems
Represent the following numbers in signed magnitude, 1’s complement and 2’s complement:
-9
-25
-90
-220

## Slide 19
THANK YOU