## Slide 1: UNIT-2
Logic Gates and Boolean Algebra
NOT, AND, OR, universal gates, X-OR and X-NOR gates
Boolean laws and theorems, complement and dual of a logic function
Canonical and standard forms
Two level realization of logic functions using universal gates
Minimizations of logic functions (POS and SOP) using Boolean theorems
K-map (upto four variables), don’t care conditions.

## Slide 2: Outline of today’s session
Introduction- Logic Gate
Types of logic gates
  NOT
  AND
  OR
  NAND
  NOR
  EX-OR
  EX-NOR

## Slide 3: Logic Gates
Logic gates are the basic building blocks of a computer.
It is an electronic circuit having one or more than one input and only one output.
Input and output values are the logical values TRUE and FALSE or ON or OFF.
Digital systems are said to be constructed by using logic gates.
The relationship between the inputs of logic gates and their output is given by the truth table.
A truth table lists all the possible combinations of input variables and the corresponding outputs is called a truth table.

## Slide 4: Types of Gates

## Slide 5: For every logic gate:
Logic Symbol
Boolean Expression
Truth Table

## Slide 6: NOT Gate
NOT gate is also known as Inverter. It has one input A and one output Y.
Its output is always the complement of its input. If the input is 1 then output is 0 and vice versa.
Logic symbol : Truth Table:
Boolean Expression:
Y=A1

## Slide 7: AND Gate
It has n input (n >= 2) and one output.
The output is equal to 1 only if all the inputs are 1.
Logic symbol : Truth Table:
Boolean Expression:
Y=AB

## Slide 8: OR Gate
It has n input (n >= 2) and one output.
The output is equal to 1 if atleast one input is 1.
Logic symbol : Truth Table:
Boolean Expression:
Y=A+B

## Slide 9: NAND Gate
A NOT-AND operation is known as NAND operation.
It has n input (n >= 2) and one output.
Logic symbol : Truth Table:
Boolean Expression:
Y=(AB)1

## Slide 10: Graphic Symbol-NAND

## Slide 11: NOR Gate
A NOT-OR operation is known as NOR operation.
It has n input (n >= 2) and one output.
Logic symbol : Truth Table:
Boolean Expression:
Y=(A+B)1

## Slide 12: Graphic Symbol-NOR

## Slide 14: XOR Gate
XOR or Ex-OR gate is a special type of gate.
The exclusive-OR gate is abbreviated as EX-OR gate or sometime as X-OR gate.
It can be used in the half adder, full adder and subtractor.
It has n input (n >= 2) and one output.
Logic symbol : Truth Table:
Boolean Expression:
Y=A1B+AB1

## Slide 16: XNOR Gate
XNOR gate is a special type of gate.
It can be used in the half adder, full adder and subtractor.
The exclusive-NOR gate is abbreviated as EX-NOR gate or sometime as X-NOR gate.
It has n input (n >= 2) and one output.
Logic symbol : Truth Table:
Boolean Expression:
Y=AB+A1B1

## Slide 18: What is the output?

## Slide 19: What is the output?
X

## Slide 20: What is the output?
Y1
X

## Slide 21: What is the output?
X+Y1
Y1
X

## Slide 22: What is the output?
X+Y1
Y1
Z
X

## Slide 23: What is the output?
X+Y1
Y1
(X+Y1)Z
Z
X

## Slide 24: What is the output?
X+Y1
Y1
(X+Y1)Z
X1
Z1
Z
Y
X

## Slide 25: What is the output?
X+Y1
Y1
(X+Y1)Z
X1
Z1
X1YZ1
Z
Y
X

## Slide 26: What is the output?
X+Y1
Y1
(X+Y1)Z
X1
Z1
X1YZ1
(X+Y1)Z+X1YZ1
Z
Y
X

## Slide 27: What is the output?
F= (X+Y1)Z+X1YZ1

## Slide 28: What is the output?

## Slide 29
THANK YOU