## Slide 1: Outline of today’s session
Universal Gates
  NAND
  NOR
Realization of other gates using Universal gates.

## Slide 2: Universal Gates
Universal gates are the ones which can be used for implementing any gate like AND, OR and NOT, or any combination of these basic gates;
NAND and NOR gates are universal gates. This means any gate operation can be implemented using these gates.
But there are some rules that need to be followed when implementing NAND or NOR based gates

## Slide 3
NAND
NOT
AND
OR
NOR
NOR
NOT
OR
AND
NAND
1
Number of NAND gates
Number of NOR gates
2
3
4
1
2
3
4

## Slide 4: NOT function using NAND
NOT function can be implemented as follows:
(A.A)1 = A1 (Idempotent)
It requires ONE NAND gate.

## Slide 5: AND function using NAND
AND function can be implemented as follows:
    = ((AB)'. (AB)' )'
    = ((AB)')' (Idempotent)
    = (AB) (Involution)
It requires TWO NAND gates.

## Slide 6: OR function using NAND
OR function can be implemented as follows:
  =((AA)'(BB)')'
  = (A'B')' (Idempotent)
  = A''+B'' (DeMorgan)
  = A+B (Involution)
It requires THREE NAND gates.

## Slide 7: NOR function using NAND
NOR function can be implemented as follows:
It requires FOUR NAND gates.
  =[((AA)'(BB)')']'
  = [(A'B')']' (Idempotent)
  = [A''+B'']' (DeMorgan)
  = [A+B]' (Involution)

## Slide 8: EX-OR function using NAND
1.(AB)’
2.(A(AB)’)’=A’+((AB)’)’=A’+AB=(A’+A).(A’+B)=1.(A’+B)=(A’+B)
3.(B(AB)’)’=B’+((AB)’)’=B’+AB=(B’+A).(B’+B)=(A+B’).1=(A+B’)
4. [(A’+B)(A+B’)]’=(A’+B)’+(A+B’)’=(A’)’B’+A’(B’)’=AB’+A’B
Distributive: A+(B*C)=(A+B)*(A+C)
A*(B+C)=(A*B)+(A*C)

## Slide 9: EX-NOR function using NAND

## Slide 10: NOT function using NOR
NOT function can be implemented as follows:
(A+A)1 = A1 (Idempotent)
It requires ONE NOR gate.

## Slide 11: OR function using NOR
OR function can be implemented as follows:
    = ((A+B)')' (Idempotent)
    = (A+B) (Involution)
It requires TWO NOR gates.

## Slide 12: AND function using NOR
AND function can be implemented as follows:
  =((A+A)'(B+B)')'
  = (A'+B')' (Idempotent)
  = A''.B'' (DeMorgan)
  = A.B (Involution)
It requires THREE NOR gates.

## Slide 13: NAND function using NOR
NAND function can be implemented as follows:
It requires FOUR NAND gates.
  =[((A+A)'(B+B)')']'
  = [(A'+B')']' (Idempotent)
  = [A''.B'']' (DeMorgan)
  = [A.B]' (Involution)

## Slide 14: EX-OR function using NOR

## Slide 15: EX-NOR function using NOR

## Slide 16: Any logic with only universal gates
Converting all gates into universal gates.
Drawing a logic diagram and converting.
Using SOP and POS forms.

## Slide 17
THANK YOU