## Slide 1: Outline of today’s session
Boolean Algebra
Boolean Laws
Two valued boolean algebra

## Slide 2: Boolean Algebra
Boolean algebra was invented by George Boole in 1854.
Boolean Algebra is used to analyze and simplify the digital (logic) circuits.
It uses only the binary numbers i.e. 0 and 1.
Also called logical Algebra.
Any complex logic statement can be expressed by a Boolean function.

## Slide 3: Boolean Laws
There are six types of Boolean Laws.
  Commutative Law
  Associative Law
  Distributive Law
  AND Law
  OR Law
  Complement Law

## Slide 4: Commutative law
Any binary operation which satisfies the following expression is referred to as commutative operation.
A.B=B.A
A+B=B+A
Commutative law states that changing the sequence of the variables does not have any effect on the output of a logic circuit.

## Slide 5: Associative law
This law states that the order in which the logic operations are performed is irrelevant as their effect is the same.
(A.B).C=A.(B.C)
(A+B)+C=A+(B+C)

## Slide 6: Distributive law
  Distributive law states the following condition:
  A.(B+C)=A.B+A.C
  A+BC=(A+B).(A+C)
  Example:
  x.(y1+z)= x.y1+x.z
  x+y1z=(x+y1).(x+z)

## Slide 7: AND Laws
  These laws use the AND operation. Therefore they are called as AND laws.
  A.0=0
  A.1=A
  A.A=A (Idempotent Law)
  A.A1=0

## Slide 8: OR Laws
  These laws use the OR operation. Therefore they are called as OR laws.
  A+0=A
  A+1=1
  A+A=A (Idempotent Law)
  A+A1=1

## Slide 9: INVERSION Law
  This law uses the NOT operation. The inversion law states that double inversion of a variable results in the original variable itself.
(A1)1=A

## Slide 10: Two Valued Boolean Algebra
A two valued Boolean Algebra is defined on a set of two elements, B = { 0, 1 }, with rules for the two binary operators + and .
These rules are exactly same as the AND, OR, & NOT operations, respectively.

## Slide 11: Huntington postulates
For the set B = { 0, 1 } and the two binary operators + and . :
Closure: The result of each operation is 1 or 0 of B.
Identity element:
  With respect to +, identity element is 0,
  since 0 + 0 = 0, 0 + 1 = 1 + 0 = 1.
  With respect to . ,identity element is 1, since 1.1=1, 1.0=0.1=0
3. Commutative law
  0 + 1 = 1 + 0 = 1 ( for + )
  0 . 1 = 1 . 0 = 0 ( for . )

## Slide 12
4. Distributive law
a. . is distributive over + : x ( y + z ) = xy + xz
b. + is distributive over . : x + ( y. z) = (x + y) . (x + z)

## Slide 13
5. From the complement table,
  a. x + x' = 1
    since 0 + 0' = 0 + 1 = 1
    1 + 1' = 1 + 0 = 1
  b. x . x' = 0
    since 0 . 0' = 0 . 1 = 0
    1 . 1 ' = 1. 0 = 0
6. Two valued boolean algebra has two distinct elements 1 and 0.

## Slide 14: Theorems and Properties of Boolean Algebra
a. x + x = x
proof:
x + x = ( x + x ) . 1
= ( x + x ) (x + x')
= (x + xx')
= x + 0
= x
b. x . x = x
proof:
x . x = x. x + 0
= x . x + x . x'
= x (x + x')
= x . 1
= x
IDEMPODENT LAW

## Slide 15
a. x + 1 = 1
proof:
x + 1 = 1 . ( x + 1)
= ( x + x' )( x + 1)
= x.x+ x.1+ x‘.x + x'.1
= x + x + 0+ x'
= 1
b. x.0 = 0 by duality
Proof:
x.0 = 0+(x.0)
= (x.x’)+(x.0)
= 0+0
= 0
ANNULMENT LAW

## Slide 16: Absorption Theorem
a. x + xy = x
proof:
x + xy = x.1 + xy
= x (1 + y)
= x ( y + 1 )
= x . 1
= x
b. x ( x + y ) = x

## Slide 17: De morgan’s Theorem
DeMorgan’s First theorem proves that when two (or more) input variables are AND’ed and negated, they are equivalent to the OR of the complements of the individual variables. Thus the equivalent of the NAND function will be a negative-OR function, proving that (A.B)1 = A1+B1.
DeMorgan’s Second theorem proves that when two (or more) input variables are OR’ed and negated, they are equivalent to the AND of the complements of the individual variables. Thus the equivalent of the NOR function is a negative-AND function proving that (A+B) 1 = A1.B1
1. ( xy )' = x' + y'
2. ( x + y )' = x' y'

## Slide 18: Consensus Theorem

## Slide 19: Operator precedence
For evaluating the boolean expression is:
1. First the expressions inside parentheses must be evaluated.
2. Complement ( NOT )
3. AND
4. OR

## Slide 20
THANK YOU