## Slide 1: Outline of today’s session
Revise-Boolean Laws
Boolean Function
Dual of a Boolean function
Complement of a Boolean function
Minimization of Boolean functions

## Slide 2: Boolean Laws
Annulment Law – A term AND´ed with a “0” equals 0 or OR´ed with a “1” will equal 1
  A . 0 = 0 A variable AND’ed with 0 is always equal to 0
  A + 1 = 1 A variable OR’ed with 1 is always equal to 1
Identity Law – A term OR´ed with a “0” or AND´ed with a “1” will always equal that term
  A + 0 = A A variable OR’ed with 0 is always equal to the variable
  A . 1 = A A variable AND’ed with 1 is always equal to the variable
Idempotent Law – An input that is AND´ed or OR´ed with itself is equal to that input
A + A = A A variable OR’ed with itself is always equal to the variable
A . A = A A variable AND’ed with itself is always equal to the variable

## Slide 3: Boolean Laws
Complement Law – A term AND´ed with its complement equals “0” and a term OR´ed with its complement equals “1”
  A . A1 = 0 A variable AND’ed with its complement is always equal to 0
  A + A1 = 1 A variable OR’ed with its complement is always equal to 1
Commutative Law – The order of application of two separate terms is not important
  A . B = B . A The order in which two variables are AND’ed makes no difference
  A + B = B + A The order in which two variables are OR’ed makes no difference
Double Negation Law – A term that is inverted twice is equal to the original term
A = ((A)|)| A double complement of a variable is always equal to the variable

## Slide 4: Boolean Laws
Distributive Law – This law permits the multiplying or factoring out of an expression.
A(B + C) = A.B + A.C (OR Distributive Law)
A + (B.C) = (A + B).(A + C) (AND Distributive Law)
Absorptive Law – This law enables a reduction in a complicated expression to a simpler one by absorbing like terms.
  A + (A.B) = A (OR Absorption Law)
  A(A + B) = A (AND Absorption Law)
Associative Law – This law allows the removal of brackets from an expression and regrouping of the variables.
  A + (B + C) = (A + B) + C = A + B + C (OR Associate Law)
  A(B.C) = (A.B)C = A . B . C (AND Associate Law)

## Slide 5: Boolean Function
A Boolean function is a function that has n variables or entries, so it has 2n possible combinations of the variables.
A Boolean Function is described by an algebraic expression called Boolean expression which consists of binary variables, the constants 0 and 1, and the logic operation symbols.
These functions will assume only 0 or 1 in its output.
An example of a Boolean function is :
f(a,b,c) = ab + c
These functions are implemented with the logic gates.

## Slide 6: Boolean Expressions
A Boolean expression always produces a Boolean value.
A Boolean expression is composed of a combination of the Boolean constants (True or False), Boolean variables and logical connectives.
Each Boolean expression represents a Boolean function.
Example − AB’C is a Boolean expression

## Slide 7
F(a,b,c)=abc+abIcI+aIbcI
Terms:3
abc
abIcI
aIbcI

## Slide 8
F(a,b,c)=abc+abIcI+aIbcI
Terms:4
abc
abIcI
aIbcI
Variables: 3
Has two values

## Slide 9
F(a,b,c)=abc+abIcI+aIbcI
Terms:3
abc
abIcI
aIbcI
Literals: 6
A single variable within a term that may be complemented or not
Variables: 3
Has two values

## Slide 10: Dual of a Boolean function
The dual of a Boolean expression is the expression is obtained by interchanging addition and multiplication and interchanging 0's and 1's.
Example:
The dual of xy + xz is (x + y) · (x + z).

## Slide 11: Complement of a Boolean function
Method 1: Using Duality
  Take the dual of function F.
  Complement each literal in the dual obtained in step 1 to get F1
  Example:
  F(x,y,z)=xy + xz
  Dual of F=Fd= (x + y) · (x + z)
  Complement of F=F1= (x1 + y1) · (x1 + z1)
Method 2: Using De-Morgan’s laws
  Example:
  F(x,y,z)=xy + xz
  F1= (xy + xz) 1
  =(xy) 1 . (xz) 1
  =(x1 + y1) · (x1 + z1)

## Slide 12: Problems
Find the complement of the following Boolean functions:
  F1 = x' yz' + x'y'z
  F2 = x ( y'z' + yz )
Simplify the following using De Morgan’s theorem: [((AB)1 C)1D]1.
Show that (X+Y1+XY) (X+Y1 ) (X1 Y)=0.
Realize the Boolean function using logic gates Y = CD+EF+G.

## Slide 13: Minimizing a Boolean expression using Boolean laws
AB+A(B+C)+B(B+C)
[AB(C + BD)+ AB]C
A1BC+ABC1+ ABC + A1BC1
Use Boolean algebra to simplify the following expression, then draw a logic circuit for the simplified expression: A (B + AB) + AC
Reduce the following Boolean expressions to the indicated number of literals
    A’C’+ABC +AC’ to THREE literals
    ABC1D+A1BD+ABCD to TWO literals
    A’B(D’+CD)+B(A+A’CD) to ONE literals

## Slide 14: GATE Questions
Minimum number of 2 input NAND gates required to implement the function given below is :F=(X1+Y1)(Z+W) [GATE 1988]
The minimum number of 2 input NAND gates required to implement the Boolean function Z = AB’C, assuming that A, B and C are available, is____ [GATE 1998]
For the logic circuit shown in figure, the output Y is equal to:

## Slide 15: GATE Questions
4. For the output F to be 1 in the logic circuit shown, the input combination should be: [GATE 2010]
  a)A = 1, B = 1, C = 0 b) A = 1, B = 0, C = 0
  c) A = 0, B = 1, C = 0 d) A = 0, B = 0, C = 1
5. Evaluate the minimum number of gates required to implement the Boolean function (AB+C) if we have to use only 2-input NOR gates? [GATE 2009]

## Slide 16
THANK YOU