## Slide 1: Outline of today’s session
Minterm, Maxterm
Canonical forms of a Boolean function
  Sum of Minterms
  Product of Maxterms
Expressing a Boolean function in canonical forms.
Conversion between canonical forms
Standard Forms
  Sum of Products form(SoP)
  Product of Sums(PoS)

## Slide 2: Minterm: Product Term
For a boolean function of variables , a product term in which each of the variables appears once, either in its complemented or uncomplemented form is called a minterm.
A variable is complemented for a value of 0 and uncomplemented for a value of 1.
Denoted by mi
For n variables, we have 2n minterms.
Any boolean function can be expressed as “sum of minterms”.

## Slide 3: Maxterm: Sum Term
For a boolean function of variables , a sum term in which each of the variables appears once, either in its complemented or uncomplemented form is called a maxterm.
A variable is complemented for a value of 1 and uncomplemented for a value of 0.
Denoted by Mi
For n variables, we have 2n maxterms.
Any boolean function can be expressed as “product of maxterms”.

## Slide 5: CANONICAL FORMS
For a Boolean expression there are two kinds of canonical forms −
  The sum of minterms (SOM) form
  The product of maxterms (POM) form
Any Boolean function can be expressed as a sum of its 1-minterms( and the inverse of the function can be expressed as a sum of its 0-minterms. Hence,
  F (list of variables) = ∑ (list of 1-minterm indices)and
  F’ (list of variables) = ∑ (list of 0-minterm indices)
Any Boolean function can be expressed as a product of its 0-maxterms and the inverse of the function can be expressed as a product of its 1-maxterms. Hence,
  F (list of variables) = π (list of 0-maxterm indices) and
  F’(list of variables) = π (list of 1-maxterm indices).

## Slide 6: Sum of Minterms
Example:
Let, F(x, y, z) = x’ y’ z’ + x y’ z + x y z’ + x y z
F(x, y, z) = m0 + m5 + m6 + m7
Hence, F(x, y, z) = ∑ (0, 5, 6, 7)
Now we will find the complement of F(x, y, z)
F’(x, y, z) = m1 + m2 + m3 + m4
Hence, F’(x, y, z) == ∑ (1, 2, 3, 4)

## Slide 7: Expressing a Boolean function in SOM form
Method 1:
  Check every term in the function. If a term misses a variable x, it is ANDed with (x+x1).

## Slide 8: Expressing a Boolean function in SOM form
Method 2: Truth Table
  Write the all the 1-minterms i.e., minterms for which F=1, in the truth table.

## Slide 9: Expressing a Boolean function in POM form
Method 1:
  Check every term in the function. If a term misses a variable x, it is ORed with (xx1) and apply DISTRIBUTIVE LAW.

## Slide 10: Expressing a Boolean function in POM form
Method 2: Truth Table
  Write the all the 0-maxterms i.e., maxterms for which F=0, in the truth table.

## Slide 11: Summary of minterms and maxterms
F(A,B,C)= Σ(1,4,7)
F(A,B,C)=Π(0,2,3,5,6)
F1(A,B,C)= Σ (0,2,3,5,6)
F1(A,B,C)= Π (1,4,7)

## Slide 12: Conversion from SoM to PoM form
The SOP function:
F = ∑ A, B, C (0, 2, 3, 5, 7)
= A’ B’ C’ + A B’ C’ + A B’ C + ABC’ + ABC
This is written in POS form by:
Step 1: changing the operational sign to Π
Step 2: writing the missing indexes of the terms, 001, 100 and 110. Now write the sum form for these noted terms.
001 = (A + B + C) 100 = (A + B’ + C’) 110 = (A + B’ + C’)
Writing down the new equation in the form of POS form,
F = Π A, B, C (1, 4, 6)
= (A + B + C) * (A + B’ + C’) * (A + B’ + C’)

## Slide 13: Conversion from PoM to SoM form
The POS function:
F = Π A, B, C (2, 3, 5)
= (A’+B’+C).(A+B’+C’).(A’+B+C’)
This is written in SOP form by:
Step 1: changing the operational sign to Σ
Step 2: writing the missing indexes of the terms, 000, 001, 100, 110, and 111. Now write the product form for these noted terms.
000 = A’ B’ C’ 001 = A’B’C 100 = AB’C’ 110 = ABC’ 111 = ABC
Writing down the new equation in the form of SOP form,
F = Σ A, B, C (0, 1, 4, 6, 7)
= (A’B’C’) + (A’B’C) + (AB’C’) + (ABC’) + (ABC)

## Slide 14: Problems: Canonical Forms
(a+b’+c)(b’+c+d’)(a+b’+c’+d) to PoM
ab’c+a’b’+abc’d to SoM
(u+xw) (x+u1v) to POM
x1 +x(x+y1)(y+z1) to SoM

## Slide 15: Standard Forms
There are two standard forms of representing the Boolean outputs. These are the simplified version of canonical forms.
  Standard SoP (Sum of Products) form
  Standard PoS (Product of Sums) form
The main advantage of standard forms:
  number of inputs applied to logic gates can be minimized.
  Sometimes, there will be reduction in the total number of logic gates required.

## Slide 16: Standard SoP form
In this form, each product term need not contain all literals. So, the product terms may or may not be the min terms.
Therefore, the Standard SoP form is the simplified form of canonical SoP form.
Convert the following Boolean function into Standard SoP form.
f = p’qr + pq’r + pqr’ + pqr
f = p’qr + pq’r + pqr’ + pqr + pqr + pqr
Therefore, the standard SoP form corresponding to given canonical SoP form is f = pq + qr + pr

## Slide 17: Standard PoS form
In this form, each sum term need not contain all literals. So, the sum terms may or may not be the Max terms.
Therefore, the Standard PoS form is the simplified form of canonical PoS form.
Convert the following Boolean function into Standard PoS form.
f = (p+q+r).(p+q+r).(p+q+r′).(p+q+r′).(p+q′+r).(p+q′+r).(p′+q+r)
f = (p+q+rr′).(p+q+rr′).(p+r+qq′).(p+r+qq′).(q+r+pp′)
f = (p+q+0).(p+q+0).(p+r+0).(p+r+0).(q+r+0)
f = (p+q).(p+q).(p+r).(p+r).(q+r)
f = (p+q).(p+r).(q+r)
Therefore, the standard PoS form corresponding to given canonical PoS form is f = (p+q).(p+r).(q+r) This is the dual of the Boolean function, f = pq + qr + pr.

## Slide 18: Standard Forms
Standard forms can be implemented using :
SoPTWO level AND-OR gates/ TWO level NAND gates
PoSTWO level OR-AND gates / TWO level NOR gates

## Slide 19: SoP: AND-OR/NAND implementation

## Slide 20: SoP: AND-OR/NAND implementation

## Slide 21
THANK YOU