## Slide 1: Outline of today’s session
Karnaugh maps
  Rules for grouping
  Two variable k-maps
  Three variable k-maps
  Four variable k-maps
Problems

## Slide 2: What is Karnaugh map?
The Karnaugh map provides a simple and straight-forward method of minimizing Boolean expressions.
With the Karnaugh map Boolean expressions having up to four and even six variables can be simplified.
A Karnaugh map provides a pictorial method of grouping together expressions with common factors and therefore eliminating unwanted variables.
The map is a simple table containing 1s and 0s that can express a truth table.
They are used to simplify S.O.M and P.O.M forms of Boolean function.
One map cell corresponds to a row in the truth table i.e, a minterm or a maxterm in the Boolean expression.

## Slide 3: Requirements
To minimize a boolean function using k-map:
  Boolean function must be expressed in SoM or PoM form.
Minterms results in minimized SoP form.
Maxterms results in minimized PoS form.

## Slide 4: Rules for K-Maps
Each cell with a 1 or 0 must be included in at least one group.
  Groups of 1 form a product term.
  Groups of 0 form a sum term
Try to form the largest possible groups.
Try to end up with as few groups as possible.
Groups may be in sizes that are powers of 2:
20 = 1, 21= 2, 22= 4, 23= 8, 24 = 16, ...
5. Groups may be square or rectangular only (including wraparound at the grid edges). No diagonals or zig-zags can be used to form a group.

## Slide 5: Number of variables minimized
The larger a group is, the more inputs are minimized:
  i. A group of 1 has no minimized inputs.
  ii. A group of 2 has 1 minimized input.
  iii. A group of 4 has 2 minimized inputs.
  iv. A group of 8 has 3 minimized inputs.
  v. A group of 16 has 4 minimized inputs.
Will be more clear with example…

## Slide 6: Rules for Grouping
A group must contain either 1,2,4,8,or 16 cells (depending on number of variables in the expression)
Each cell in a group must be adjacent to one or more cells in that same group, but all cells in the group do not have to be adjacent to each other.
Always include the largest possible number of 1’s in a group in accordance with rule 1.
Each 1 on the map must be included in at least one group.
The 1’s already in a group can be included in another group as long as the overlapping groups include at least one non-common 1’s.

## Slide 7: Constructing Karnaugh Maps
The shape and size of the map is dependent on the number of binary inputs in the circuit to be analysed.
  2 input circuits with inputs A and B require maps with 22 = 4 cells
  3 input circuits with inputs A B and C require maps with 23 = 8 cells
  4 input circuits with inputs A B C and D require maps with 24 = 16 cells.

## Slide 8
Groups may not include any cell containing a zero.
Groups may be horizontal or vertical, but not diagonal.
Each group should be as large as possible.

## Slide 9
Groups may overlap.
Groups may wrap around the table. The leftmost cell in a row may be grouped with the rightmost cell and the top cell in a column may be grouped with the bottom cell.

## Slide 10: Rules for Grouping
No zeros allowed.
No diagonals.
Only power of 2 number of cells in each group.
Groups should be as large as possible.
Every one must be in at least one group.
Overlapping allowed.
Wrap around allowed.
Fewest number of groups possible.

## Slide 11: Two Variable k-Map
The Possible MinTerms with 2 Variables (A and B) are: A.B, A.B’, A’.B And A’.B’.
The following table shows the positions of all the possible outputs of 2-variable Boolean function on a K-map.
A general representation of a 2 variable K-map plot is shown below.

## Slide 12: Example:2-variable
Simplify the given 2-variable Boolean equation by using K-map.
F = X Y’ + X’ Y + X’Y’
The reduced equation will be : X’ +Y’

## Slide 13: Three Variable k-Map
For a 3-variable Boolean function, there is a possibility of 8 output min terms.

## Slide 14: Three Variable k-Map
The general representation of all the min terms using 3-variables is shown below:
The largest group size will be 8 but we can also form the groups of size 4 and size 2, by possibility.

## Slide 15: Example:3-variable
Simplify the given 3-variable Boolean equation by using k-map.
F = X’ Y Z + X’ Y’ Z + X Y Z’ + X’ Y’ Z’ + X Y Z + X Y’ Z’
The reduced equation will be X Z’ + Y’ + X’ Z.
In this equation, no further minimization is possible.

## Slide 17: 4 variable K-maps
There are 16 possible min terms in case of a 4-variable Boolean function.

## Slide 18: 4 variable K-maps
The general representation of minterms using 4 variables is shown below:
The possible number of cells that can be grouped together are 1, 2, 4, 8 and 16.

## Slide 19: Example:4-variable
Simplify the given 4-variable Boolean equation by using k-map.
F (W, X, Y, Z) = (1, 5, 12, 13)
We can minimize the given Boolean equation using k-map as:
F = W Y’ Z + W ‘Y’ Z

## Slide 23: Determining the Minimum SOP Expression from the Map
For a 3-variable map:
  A 1-cell group yields a 3-variable product term
  A 2-cell group (pair) yields a 2-variable product term
  A 4-cell group (quad) yields a 1-variable product term
  An 8-cell group (octet) yields a value of 1 for the expression.
For a 4-variable map:
  A 1-cell group yields a 4-variable product term
  A 2-cell group yields a 3-variable product term
  A 4-cell group yields a 2-variable product term
  An 8-cell group yields a 1-variable product term
  A 16-cell group yields a value of 1 for the expression.

## Slide 24: Problems: 2-variable
F(X,Y)=∑(0,1,2)
F(X,Y)=∑(0,1)
F(X,Y)=∑(0,2)
F(X,Y)=∑(1,2)
F(X,Y)=∑(2,3)
F(X,Y)=∑(0,3)
F(X,Y)=∑(1,3)
F(X,Y)=∑(0,1,3)
F(X,Y)=∑(0,2,3)
F(X,Y)=∑(1,2,3)
F(X,Y)=∑(0,1,2,3)

## Slide 25: Problems: 3-variable
F(X,Y,Z)=∑(0,1,2,5,7)
F(X,Y,Z)=∑(2,3,4,5)
F(X,Y,Z)=∑(3,4,6,7)
F(X,Y,Z)=∑(0,2,4,6)
F(X,Y,Z)=∑(0,2,4,5,6)
F(X,Y,Z)=∑(0,2,4,5)
F(X,Y,Z)=∑(0,1,2,4,5,6)
F(X,Y,Z)=∑(0,1,2,3,5)
F(X,Y,Z)=∑(0,1,5,7)
F(X,Y,Z)=∑(1,2,3,7)
F(X,Y,Z)=∑(1,2,3,6,7)
F(X,Y,Z)=∑(1,2,3,4,5,6,7)
F(X,Y,Z)=∑(1,2,3,5,6,7)
F(X,Y,Z)=∑(2,3,6,7)
F(X,Y,Z)=∑(3,4,5,6,7)
F(A,B,C)=A’C+A’C+AB’C+BC
F(X,Y,Z)=XY+X’Y’Z’+X’YZ’
F(X,Y,Z)=X’Y’+YZ+X’YZ’
F(X,Y,Z)=X’Y+YZ’+Y’Z’
F(X,Y,Z)=X’YZ+XY’Z’+XY’Z

## Slide 26: Problems: 4-variable
F(A,B,C,D)= ∑(4,5,6,7,15)
F(W,X,Y,Z)= ∑(0,1,2,4,5,6,8,9,12,13,14)
F(A,B,C,D)=A’B’C’+B’CD’+A’BCD+AB’C’
F(A,B,C,D)= ∑(3,7,11,13,14,15)
F(A,B,C,D)= ∑(2,3,12,13,14,15)
F(A,B,C,D)= ∑(11,12,13,14,15)
F(A,B,C,D)= ∑(8,10,12,13,14)
F(A,B,C,D)= ∑(1,4,5,6,12,14,15)
F(A,B,C,D)= ∑(2,3,6,7,12,13,14)
F(A,B,C,D)= ∑(1,3,4,5,6,7,9,11,13,15)
F(A,B,C,D)= ∑(0,2,4,5,6,7,8,10,13,15)

## Slide 27
THANK YOU