## Slide 1: Outline of today’s session
Karnaugh maps
  Don’t cares
Problems

## Slide 2: What are Don’t cares?
For each combination of input variable we have specified a minterm by representing them as 1 in the K-Map. But, there may arise a case when for a given combination of input we may not have a specified output or the input combination may be invalid.
The combinations for which we don't have any output expression specified are called don't care combination.
For Example, in 8421 code, input states 1001, 1010, 1011, 1100, 1101, 1110 and 1111 are invalid and the corresponding output is the don't care. Similarly, in Excess-3 code, binary input states 0000, 0001, 0010, 1101, 1110 and 1111 are unspecified and are also represented by don't care.
These don't care combinations in the K-Map are denoted by an X (cross) symbol.
The X is called "Don't care conditions".

## Slide 3: Rules with don’t cares
General rules to be followed while minimizing the expressions using K-Map which include don't care conditions are as follows:
  After forming the K-Map, fill 1's at the specified positions corresponding to the given minterms. Fill X at the positions where don't care combinations are present.
  Now, Encircle the groups in the K-Map. One thing to be kept in mind is, now we can treat Don't Care conditions (X) as 1s if these help in forming the largest groups.
  No such group can be encircled whose all the elements are X.

## Slide 4: K-map with “Don’t care” conditions
The “Don’t care” conditions are used to replace the empty cell to form a possible grouping of variables.
They can be used as either 0 or 1, based on the adjacent variables in the group.
The cells that contain “don’t care” conditions are represented by ‘X’ symbol among the normal 0’s and 1’s.

## Slide 5: When to use “Don’t care” conditions?
When forming groups of cells, treat the don’t care cell as either a 1 or a 0, or ignore the don’t cares.
This is helpful if it allows us to form a larger group than would otherwise be possible without the don’t cares. There is no requirement to group all or any of the don’t cares.
Only use them in a group if it simplifies the logic.

## Slide 6: Example

## Slide 7: Problems
1. f(A,B,C,D) = m(1,3,5,7,9) + d(6,12,13)
f = A'D + B'C'D without don't cares
f = A1D+C1D with don't cares
2. F (A, B, C, D) = Σ m (1, 5, 6, 12, 13, 14) + d (2, 4)
3. F = m(1,5,6,12,13,14) + d(4)
4. F(A,B,C,D) = m(0,1,2,3,4,5) + d(10,11,12,13,14,15)
5. F(A, B, C, D) = m(1, 2, 6, 7, 8, 13, 14, 15) + d(3, 5, 12)
6. F(A,B,C,D)= ∑ (0,6,8,13,14) d(A,B,C,D)= ∑ (2,4,10)
7. F(A,B,C,D)= ∑ (4,5,6,7,12,13,14) d(A,B,C,D)= ∑ (1,9,11,15)

## Slide 8: Significance of Don’t cares
Simplification:
  These conditions denote the set of inputs that never occurs for given digital circuits. Therefore, to simplify the boolean output expressions, the 'don't care' are used.
Reduced Power Consumption:
  The switching of the state is reduced when we group the terms long with "don't care". This reduces the required memory space resulting in lower power consumption.
Lesser number of gates:
  For reducing the number of gates that are used to implement the given expression, simplification places an important role. So, the 'don't care' makes the logic design more economical.
Prevention of Hazards:
  In the digital system, the 'don't care' place an important role in hazards prevention.
States in Code Converters:
  These also play an important role in code conversion. For example- In the design of a 4-bit BCD-to-XS-3 code converter, the input combinations 1010, 1011, 1100, 1101, 1110, and 1111 are don't cares.

## Slide 9: Application
The electronics class of Lightning State College has been asked to build the lamp logic for a stationary bicycle exhibit at the local science museum. As a rider increases his pedaling speed, lamps will light on a bar graph display.
No lamps will light for no motion. As speed increases, the lower lamp, L1 lights, then L1 and L2, then, L1, L2, and L3, until all lamps light at the highest speed. Once all the lamps illuminate, no further increase in speed will have any effect on the display.
Let the inputs be ABC, 23 or 8-codes, but we only have five lamps. A is the most significant bit, C the least significant bit.
The lamp logic needs to respond to the six codes out of the A to D. For ABC=000, no motion, no lamps light.
We do not care about the response to input codes (110, 111) because these codes will never come out.

## Slide 10: Truth Table
A | B | C | L1 | L1 | L3 | L4 | L5
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | X | X | X | X | X
1 | 1 | 1 | X | X | X | X | X

## Slide 12
THANK YOU