## Slide 1: Topics
Decoder
Higher order decoders with lower order decoders
Encoder
Priority Encoder
Multiplexer
Higher order multiplexers with lower order multiplexers
Demultiplexers

## Slide 2: Outline of today’s session
Decoder
  Block Diagram
  Operation
  Circuit

## Slide 3: Decoder
A decoder is a logic circuit that converts an n bit binary input code into M (=2n) output lines such that each output line will be activated for only one of the possible combinations of inputs.
(OR)
A decoder is a Combinational circuit that converts binary information from ‘n’ input lines to a maximum of 2n unique output lines.

## Slide 4: Decoder
The decoder is called n-to-m-line decoder, where m≤2n.
A decoder selects one of 2n outputs by decoding the binary value on the n inputs.
The decoder generates all of the minterms of the n input variables.
Exactly one output will be active for each combination of the inputs.

## Slide 5: Decoder

## Slide 6: Decoder with ENABLE input
ENABLE input performs no logical operation, but is only responsible for making the decoder ACTIVE or INACTIVE

## Slide 7: Decoder with ENABLE input
ENABLE input=0 circuit is activated with low ENABLE input and deactivated with high ENABLE input.
ENABLE input=1 circuit is activated with high ENABLE input and deactivated with low ENABLE input.

## Slide 8: Decoder
2 inputs2*4 decoder
3 inputs3*8 decoder
4 inputs4*16 decoder
5 inputs5*32 decoder
6 inputs6*64 decoder

## Slide 9: 2 to 4 Line Decoder
A0 and A1 are the two inputs where D0 through D3 are the four outputs.
Truth table explains the operations of a decoder.
It shows that each output is 1 for only a specific combination of inputs.

## Slide 10: 2 to 4 Line Decoder

## Slide 11: 2 to 4 Line Decoder with HIGH ENABLE input

## Slide 12: 2 to 4 line Decoder with active LOW enable input

## Slide 13: 3 to 8 Line Decoder
In 3 to 8 line decoder, for each possible input combination, there are seven outputs that are equal to 0 and only one that is equal to 1.
3 to 8 line decoder is also called Binary-to-Octal decoder or converter.
It is also called 1of 8 decoder, because only one of the 8 outputs is active at a time.
Decoders are widely used in the memory system of computer, where they respond to the address code input from the CPU to activate the memory storage location specified by the address code.
Decoders are also used to convert binary data to a form suitable for displaying on decimal read outs.
Decoders can be used to implement combinational circuits, Boolean functions etc.

## Slide 14: 3 to 8 Line Decoder

## Slide 15: 3 to 8 Line Decoder with HIGH Enable

## Slide 16
THANK YOU