## Slide 1: Outline of today’s session
Higher order MUX with lower order MUX
  4*1 using 2*1
  8*1 using 4*1 & 2*1
  16*1 using 8*1, 4*1 & 2*1
  64*1 using 16*1, 8*1
Implementing Boolean function using MUX
Demultiplexer

## Slide 2: 4*1 using 2*1
4*1 MUX requires THREE 2*1 MUX
S1 | S0 | Output
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3

## Slide 3: 8*1 using 4*1 & 2*1
S2 | S1 | S0 | Output
0 | 0 | 0 | I0
0 | 0 | 1 | I1
0 | 1 | 0 | I2
0 | 1 | 1 | I3
1 | 0 | 0 | I4
1 | 0 | 1 | I5
1 | 1 | 0 | I6
1 | 1 | 1 | I7
8*1 MUX requires TWO 4*1 MUX and ONE 2*1 MUX
(OR)
8*1 MUX requires FOUR 2*1 MUX and ONE 4*1 MUX

## Slide 4: 16*1 using 4*1
S3 | S2 | S1 | S0 | Output
0 | 0 | 0 | 0 | I0
0 | 0 | 0 | 1 | I1
0 | 0 | 1 | 0 | I2
0 | 0 | 1 | 1 | I3
0 | 1 | 0 | 0 | I4
0 | 1 | 0 | 1 | I5
0 | 1 | 1 | 0 | I6
0 | 1 | 1 | 1 | I7
1 | 0 | 0 | 0 | I8
1 | 0 | 0 | 1 | I9
1 | 0 | 1 | 0 | I10
1 | 0 | 1 | 1 | I11
1 | 1 | 0 | 0 | I12
1 | 1 | 0 | 1 | I13
1 | 1 | 1 | 0 | I14
1 | 1 | 1 | 1 | I15
16*1 MUX requires FIVE 4*1 MUX

## Slide 5: Implementing Boolean Function using MUX
A Boolean function with n variables can be implemented using MUX only when the function is expressed in the form of Sum of Minterms.
Consider one variable as input and remaining (n-1) variables as select lines.

## Slide 6: Example
f(A1 , A2 , A3 ) =∑(3,5,6,7)
A1 A2

## Slide 7: Problems
Implement the following boolean function using MUX: f(A, B, C) = m(0, 1, 4, 6, 7)
Implement 64*1 MUX using 16*1 MUX.
Implement the Boolean function f (A,B,C,D) = ∑(2,4,9,10) with multiplexer having active-HIGH Enable input.
4. Implement the following Boolean function using 8:1 MUX.
F(w,x,y,z)=∑ m (0, 3, 5, 8, 9, 10, 12, 14)

## Slide 8: Demultiplexer
A demultiplexer (or demux) is a device that takes a single input line and routes it to one of several digital output lines.
A demultiplexer of 2n outputs has n select lines, which are used to select which output line to send the input.
A demultiplexer is also called a data distributor.

## Slide 9: 1*4 Demultiplexer-Block Diagram

## Slide 10: 1*4 Demultiplexer-Block Diagram

## Slide 11
THANK YOU