## Slide 1: TOPICS
Design of combinational circuit.
Design of half adder
Full adder
Half subtractor
Full subtractor
Ripple adders and subtractors
Ripple adder/subtractor using 1’s and 2’s complement method, serial adder.

## Slide 2: Outline of today’s session
Combinational circuit
Classification of combinational circuit
Steps to design a combinational circuit
Example
Problems

## Slide 3: What is a combinational circuit?
Made up from basic gates (AND, OR, NOT) or universal gates (NAND, NOR) gates that are "combined" or connected together.
In these circuits “the outputs at any instant of time depends on the inputs present at that instant only.” ·
Examples for combinational digital circuits are Half adder, Full adder, Half subtractor, Full subtractor, Code converter, Decoder, Multiplexer, Demultiplexer, Encoder, ROM, etc

## Slide 4: Classification of Combinational circuits
UNIT-3
UNIT-4

## Slide 6: Boolean Function
To obtain the output Boolean functions from a logic diagram:
  Label all gate outputs that are a function of input variables.
  Determine the Boolean functions for each gate output.
  Repeat the process until the outputs of the circuit are obtained.
  By repeated substitution, obtain the output Boolean function in terms of input variables.

## Slide 7: How to get a Boolean Function?

## Slide 8: Truth Table
To obtain the truth table from logic diagram:
  Determine the number of input variables in the circuit. For n inputs, form the 2n possible input combinations and list the binary numbers from 0 to (2n -1) in a table.
  Label the outputs of selected gates with arbitrary symbols.
  Obtain the truth table for the outputs of those gates which are a function of the input variables only.
  Proceed to obtain the truth table for the outputs of these gates which are a function of previously defined values.

## Slide 9: How to get a Truth Table?

## Slide 10: Logic Diagram
To design a logic diagram:
  Determine the required number of inputs and outputs and assign a symbol to each.
  Derive the truth table that defines the required relationship between inputs and outputs.
  Obtain the simplified Boolean function for each output.
  Draw the logic diagram, using gates.

## Slide 11: Design of a Combinational Circuit
Input : the specification of the problem.
Output: the logic circuit diagram (or Boolean functions).
Step 1: Determine the required number of inputs and outputs from the specification.
Step 2: Derive the truth table that defines the required relationship between inputs and outputs.
Step 3: Obtain the simplified Boolean function for each output as a function of the input variables.
Step 4: Draw the logic diagram and verify the correctness of the design.

## Slide 12: Example-Design of CC
Design a circuit that has a 3-bit binary input and a single output (Z) specified as follows:
  Z = 0, when the input is less than 510
  Z = 1, otherwise
Step 1: Determine the inputs and Outputs
  Label the inputs (3 bits) as A, B, C
    A is the most significant bit
    C is the least significant bit
  The output (1 bit) is Z
    Z = 1 -> 1012, 1102, 1112
    Z = 0 -> other inputs

## Slide 13: Example-Design of CC
Step 2: Derive the Truth Table
A | B | C | Z
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 14: Example-Design of CC
Step 3: Simplify the Boolean Expression
From the truth table, we use one of the following 2 methods to obtain the simplified boolean expression
  Use karnaugh map to minimise the logic:
  Z=∑(5,6,7)
  From the truth table, get the canonical sum of products boolean expression. Z = A B1C + ABC1 + ABC
  Use Boolean Algebra to simplify the boolean expression to:

## Slide 15: Example-Design of CC
Step 3: Simplify the Boolean Expression
From the truth table, we use one of the following 2 methods to obtain the simplified boolean expression
  Use karnaugh map to minimise the logic
  Z=AB+AC
  Z=A(B+C)
  From the truth table, get the canonical sum of products boolean expression. Z = A B1C + ABC1 + ABC
  Z = A B1C + AB(C1 + C)
  Z = A B1C + AB
  Z = A( B1C + B)
  Z = A(C+ B) Use Boolean Algebra to simplify the boolean expression to: Z = A *(B + C)

## Slide 16: Example-Design of CC
Step 4: Draw the logic diagram
Draw a logic diagram that represents the simplified Boolean expression. Verify the design of the circuit.

## Slide 17: Problems
Design a circuit that has a 3-bit binary input and a single output that output 1 if it is a prime number. eg 210, 310, 510, 710 otherwise output 0.
Given two input bits A and B, produce three outputs X, Y, and Z so that X is 1 only when only when A > B, Y is 1 only when A < B, and Z is 1 only when A = B.
A bank wants to install an alarm system with 3 movement sensors.
To prevent false alarms produced by a single sensor activation, the alarm will be triggered only when at least two sensors activate simultaneously.
4. Design a circuit that has a 3-bit binary input B2,B1,B0 (where B2 is MSB and B0 is LSB) and a single output (Z) specified as follows:
  Z = 0, even numbers
  Z = 1, odd numbers 1, 3, 5, 7
5. Design a circuit that compares two 2-bit numbers, A and B. The circuit should have three outputs:
  G (“Greater”) should be 1 only when A > B
  E (“Equal”) should be 1 only when A = B
  L (“Lesser”) should be 1 only when A < B

## Slide 18: Code converters
Design BCD to Excess-3 converter.
Design BCD to 7-segment display converter.

## Slide 19
THANK YOU