## Slide 1: Outline of today’s session
Half Adder
Full Adder
Full Adder using Half Adder circuit

## Slide 2: What is an Adder?
An adder is a digital circuit that performs addition of numbers.
The most common adders operate on binary numbers
Binary Adders are arithmetic circuits in the form of half-adders and full-adders used to add two or three binary digits.

## Slide 3: Binary Addition of TWO bits
When adding binary numbers, a carry out is generated when the “SUM” equals or is greater than two (1+1) and this becomes a “CARRY” bit for any subsequent addition being passed over to the next column for addition and so on.
The operation of a simple adder requires two data inputs producing two outputs, the Sum (S) of the equation and a Carry (C) bit

## Slide 4: Half Adder
The half adder is a combinational arithmetic circuit that adds two single binary digits A and B and produces two outputs, sum (S) and carry (C).
Block Diagram
Truth Table

## Slide 5: Half Adder
Sum bit (S) is the X-OR of A and B and the carry bit (C) will be the AND of A and B.
Boolean Functions:
S= ∑(1,2)
C= ∑(3)

## Slide 6: Half Adder
Circuit/Logic Diagram

## Slide 7: Half Adder using NAND and NOR

## Slide 8: Full Adder
Full Adder is the adder which adds three inputs and produces two outputs. The first two inputs are A and B and the third input is an input carry as C-IN. The output carry is designated as C-OUT and the normal output is designated as S which is SUM.
Block Diagram

## Slide 9: Full Adder
Truth Table:
Logical Expression for SUM:
= ∑(1,2,4,7) = A’ B’ C-IN + A’ B C-IN’ + A B’ C-IN’ + A B C-IN = C-IN (A’ B’ + A B) + C-IN’ (A’ B + A B’) = C-IN XOR (A XOR B)
Logical Expression for C-OUT:
= ∑(3,5,6,7) = A’ B C-IN + A B’ C-IN + A B C-IN’ + A B C-IN = A B + B C-IN + A C-IN

## Slide 10: Full Adder
S= ∑(1,2,4,7)
COUT= ∑(3,5,6,7)

## Slide 11: Full Adder
Another form in which C-OUT can be implemented: = A B + A C-IN + B C-IN (A + A’) = A B C-IN + A B + A C-IN + A’ B C-IN = A B (1 +C-IN) + A C-IN + A’ B C-IN = A B + A C-IN + A’ B C-IN = A B + A C-IN (B + B’) + A’ B C-IN = A B C-IN + A B + A B’ C-IN + A’ B C-IN = A B (C-IN + 1) + A B’ C-IN + A’ B C-IN = A B + A B’ C-IN + A’ B C-IN = AB + C-IN (A’ B + A B’) Therefore COUT = AB + C-IN (A EX – OR B)

## Slide 12: Full Adder
Circuit/Logic Diagram

## Slide 13: Full Adder using two Half adders

## Slide 14: Full Adder using NAND gates

## Slide 15: Full Adder using NOR gates

## Slide 16
THANK YOU