## Slide 1: Outline of today’s session
Binary Adder
Binary Adder/Subtractor(4-bit)
Example

## Slide 2: Binary adder
Addition of n-bit numbers requires a chain of n full adders or a chain of one-half adder and n - 1 full adders.
4-bit binary ripple carry adder: Interconnection of four full-adder (FA) circuits (or) one half adder and three full adders

## Slide 3: Binary adder
This is also called Ripple Carry Adder ,because of the construction with full adders are connected in cascade.

## Slide 4: Binary adder
The augend bits of A and the addend bits of B are designated by subscript numbers from right to left, with subscript 0 denoting the least significant bit.
The carries are connected in a chain through the full adders. The input carry to the adder is C0, and it ripples through the full adders to the output carry C4.
The S outputs generate the required sum bits. An n-bit adder requires n full adders, with each output carry connected to the input carry of the next higher order full adder.

## Slide 5: Binary adder

## Slide 6: Binary Adder/Subtractor
The subtraction A-B can be performed by taking the 2's complement of B and adding to A.
The 2's complement of B can be obtained by complementing B and adding one to the result.
A-B = A + 2C(B) = A + 1C(B) + 1 = A + B’ + 1

## Slide 7: Binary Adder/subtractor
M = 1subtractor M = 0adder

## Slide 8: 4-bit Binary Adder/Subtractor
When M=0, the circuit performs A + B. The carry in is 0, and the XOR gates simply pass B untouched.
When M=1, the carry into the least significant bit (LSB) is 1, and
B is complemented (1’s complement) prior to the addition;
hence, the circuit adds to A the 1’s complement of B plus 1 (from the carry into the LSB).

## Slide 9: 4-bit Binary Adder/Subtractor

## Slide 10: 4-bit Binary Adder/Subtractor

## Slide 11: Overflow
Overflow is a problem in digital computers because the number of bits that hold the number is finite and a result that contains n+1 bits cannot be accommodated.
When two n-bit numbers are added and the result is n+1 bits, we call it as OVERFLOW.

## Slide 12: OVERFLOW
An overflow condition can be detected by observing the carry into the sign bit position and carry out of the sign bit position.
If these two carries are not equal an overflow has occurred.
An overflow is detected from the end carry out of the most significant position, when two unsigned numbers are added.
An overflow cannot occur after an addition if one number is positive and other is negative, since adding a positive number to a negative number produces a result which is not than the larger of the two original numbers.

## Slide 13: OVERFLOW
Overflow Occurs when C-in≠ C-out.

## Slide 14: OVERFLOW
In first Figure the MSB of two numbers are 0 which means they are positive. Here if C-in is 1 we get answer’s MSB as 1 means answer is negative (Overflow) and C-out as 0. C-in≠ C-out hence overflow.
In second Figure the MSB of two numbers are 1 which means they are negative. Here if C-in is 0 we get answer MSB as 0 means answer is positive(Overflow) and C-out as 1. C-in ≠ C-out hence overflow.

## Slide 15: OVERFLOW
Carry-in and Carry-out at MSB’s are enough to detect Overflow.

## Slide 16: Example
Note that the 8-bit result that should have been positive has a negative sign bit and the 8-bit that should have been negative has a positive sign bit.
If, however, the carry out of the sign bit position is taken as the sign bit of the result, then the 9-bit answer so obtained will be correct. Since the answer cannot be accommodated within 8-bits, we say that an overflow has occurred.
An overflow condition can be detected by observing the carry into the sign bit position and the carry out of the sign bit position. If these two carries are not equal, an overflow has occurred.

## Slide 17
THANK YOU