## Slide 1: Outline of today’s session
Serial adder
Problems

## Slide 2: Serial Adder
The serial binary adder or bit-serial adder is a digital circuit that performs binary addition bit by bit.
The serial full adder has three single-bit inputs for the numbers to be added and the carry in.
There are two single-bit outputs for the sum and carry out.

## Slide 3: Serial Adder
Sequential serial adders are economically efficient and simple to build.
A serial adder consists of a 1-bit full-adder and several shift registers.
In serial adders, pairs of bits are added simultaneously during each clock cycle.
Two right-shift registers are used to hold the numbers (A and B) to be added, while one right-shift register is used to hold the sum (S).

## Slide 4: Serial Adder
Parallel adder perform the adding two bit operation very fast but the disadvantage of this adder is its require large number of gate.
One the other hand in serial adder the bit addition is bit-by-bit.
Serial adder require simple circuitry as compare to parallel adder , so causes of simple circuitry this give low speed and perform bit-by-bit operation.

## Slide 5: Serial Adder
This is the one which would accept bit by bit input of the n-bit numbers and there is a bit by bit output of the n-bit Sum. In this adder we would be required one full adder and a memory element.

## Slide 6: Serial Adder

## Slide 7: Serial Adder
During each clock cycle, two input bits ai and bi are shifted from the two input right-shift registers into the 1-bit full-adder, which adds the two bits and evaluates the sum bit si and the carryout bit ci+1.
The sum bit si, is shifted out to the right-shift register and the carryout bit ci+1 is stored in the state memory of the serial adder for the next two bits.

## Slide 8: Serial Adder

## Slide 9: Difference between Serial and parallel adder
Serial Adder:
It is basically slow
It uses shift registers
It needs one full adder circuit.
It is sequential circuit.
Time needed for addition depends on number of bits.
Parallel adder:
It is faster than serial adder
It uses registers with parallel load capacity
No. of full adder circuit is actually equal to no. of bits in binary adder.
It is considered as a combination circuit
In this case, time does not depend on the number of bits.

## Slide 10: Example: Code COnverter
  A ‘code converter’ is to be designed to convert from the BCD (5421) code to normal BCD (8421) code. The input BCD combinations for each digit are given below. A block diagram of the converter is shown in figure.

## Slide 11: BCD(5421)BCD(8421)

## Slide 12
THANK YOU