## Slide 1: UNIT-3
PROCESSOR ORGANIZATION

## Slide 3
The CPU performs a variety of functions dictated by the type of instructions that are incorporated in the computer.
Computer architecture includes the instruction formats, addressing modes, the instruction set, and the general organization of the CPU registers.

## Slide 4
One boundary where the computer designer and the computer programmer see the same machine is the part of the CPU associated with the instruction set.
From the designer's point of view, the computer instruction set provides the specifications for the design of the CPU.
The design of a CPU is a task that in large part involves choosing the hardware for implementing the machine instructions.
The user who programs the computer in machine or assembly language must be aware of the register set, the memory structure, the type of data supported by the instructions, and the function that each instruction.
We will learn the organization and architecture of the CPU with an emphasis on the user’s view of the computer.

## Slide 5
Memory locations are needed for storing pointers, counters, return addresses, temporary results, and partial products during multiplication.
Having to refer to memory locations for such applications is time consuming because memory access is the most time-consuming operation in a computer.
It is more convenient and more efficient to store these intermediate values in processor registers.
When a large number of registers are included in the CPU, it is most efficient to connect them through a common bus system.
The registers communicate with each other not only for direct data transfers, but also while performing various micro operations.
Hence it is necessary to provide a common unit that can perform all the arithmetic, logic, and shift micro operations in the processor.
A bus organization for seven CPU registers is shown in the next slide.
The output of each register is connected to two multiplexers (MUX) to form the two buses A and B.
The selection lines in each multiplexer select one register or the input data for the particular bus.

## Slide 6
The A and B buses form the inputs to a common arithmetic logic unit (ALU).
The operation selected in the ALU determines the arithmetic or logic micro operation that is to be performed.
The result of the micro operation is available for output data and also goes into the inputs of all the registers.
The register that receives the information from the output bus is selected by a decoder.
The decoder activates one of the register load inputs, thus providing a transfer path between the data in the output bus and the inputs of the selected destination register.

## Slide 8
R1
R2
R3
R4
R5
R6
R7
MUX - A
MUX - B
Arithmetic Logic Unit
(ALU)
3x8
decoder
Clock
Input
Output
SEL B
SEL A
SEL D
OPR
Load
(7 lines)
A - bus
B - bus

## Slide 10
The four control selection variables are generated in the control unit and must be available at the beginning of a clock cycle.
The data from the two source registers propagate through the gates in the multiplexers and the ALU, to the output bus, and into the inputs of the destination register, all during the clock cycle interval.
Then, when the next clock transition occurs, the binary information from the output bus is transferred into R1.
To achieve a fast response time, the ALU is constructed with high-speed circuits.

## Slide 11
OPERATION OF CONTROL UNIT
There are 14 binary selection inputs in the unit, and their combined value specifies a control word.

## Slide 12
ALU CONTROL

## Slide 13
ALU CONTROL

## Slide 14: Stack Organization
Register Stack
Memory Stack
Reverse Polish Notation
Evaluation of Arithmetic Expressions

## Slide 15: INTRODUCTION
A useful feature that is included in the CPU of most computers is a stack or last-in, first-out (LIFO) list. A stack is a storage device that stores information in such a manner that the item stored last is the first item retrieved.

## Slide 16
The stack in digital computers is essentially a memory unit with an address register that can count only (after an initial value is loaded into it).
The register that holds the address for the stack is called a stack pointer (SP) because its value always points at the top item in the stack.
The two operations of a stack are the insertion and deletion of items.
The operation of insertion is called push (or push-down) because it can be thought of as the result of pushing a new item on top.
The operation of deletion is called pop (or pop-up) because it can be thought of as the result of removing one item so that the stack pops up. However, nothing is pushed or popped in a computer stack.
These operations are simulated by incrementing or decrementing the stack pointer register.

## Slide 17
Register Stack
A stack can be placed in a portion of a large memory or it can be organized as a collection of a finite number of memory words or registers.
The stack pointer register SP contains a binary number whose value is equal to the address of the word that is currently on top of the stack.
Three items are placed in the stack: A, B, and C, in that order.
Item C is on top of the stack so that the content of SP is now 3. To remove the top item, the stack is popped by reading the memory word at address 3 and decrementing the content of SP.

## Slide 18
Item B is now on top of the stack since SP holds address 2. To insert a new item, the stack is pushed by incrementing SP and writing a word in the next-higher location in the stack.
Note that item C has been read out but not physically removed. This does not matter because when the stack is pushed, a new item is written in its place.
In a 64-word stack, the stack pointer contains 6 bits because 2^6 = 64. Since SP has only six bits, it cannot exceed a number greater than 63 (111111 in binary).
When 63 is incremented by 1, the result is 0 since 111111 + 1 = 1000000 in binary, but SP can accommodate only the six least significant bits.
Similarly, when 000000 is decremented by 1, the result is 111111.

## Slide 19
The one-bit register FULL is set to 1 when the stack is full, and the one-bit register EMTY is set to 1 when the stack is empty of items.
DR is the data register that holds the binary data to be written into or read out of the stack.
Initially, SP is cleared to 0, EMTY is set to 1, and FULL is cleared to 0, so that SP points to the word at address 0 and the stack is marked empty and not full.
If the stack is not full (if FULL = 0), a new item is inserted with a push operation.

## Slide 20: The organization of a 64-word register stack

## Slide 21
The stack pointer is incremented so that it points to the address of the next-higher word.
A memory write operation inserts the word from DR into the top of the stack.
Note that SP holds the address of the top of the stack and that M[SP] denotes the memory word specified by the address presently available in SP.
The first item stored in the stack is at address 1.
The last item is stored at address 0.
If SP reaches 0, the stack is full of items, so FULL is set to 1.

## Slide 22
This condition is reached if the top item prior to the last push was in location 63 and, after incrementing SP, the last item is stored in location 0.
Once an item is stored in location 0, there are no more empty registers in the stack.
If an item is written in the stack, obviously the stack cannot be empty, so EMTY is cleared to 0.
A new item is deleted from the stack if the stack is not empty (if EMTY = 0).

## Slide 23
The top item is read from the stack into DR.
The stack pointer is then decremented. If its value reaches zero, the stack is empty, so EMTY is set to 1.
This condition is reached if the item read was in location 1.
Once this item is read out, SP is decremented and reaches the value 0, which is the initial value of SP.
Note that if a pop operation reads the item from location 0 and then SP is decremented, SP changes to 111111, which is equivalent to decimal 63.
In this configuration, the word in address 0 receives the last item in the stack. Note also that an erroneous operation will result if the stack is pushed when FULL = 1 or popped when EMTY = 1.

## Slide 25
A stack can exist as a stand-alone unit or can be implemented in a random-access memory attached to a CPU.
The implementation of a stack in the CPU is done by assigning a portion of memory to a stack operation and using a processor register as a stack pointer.
A portion of computer memory partitioned into three segments: program, data, and stack.
The program counter PC points at the address of the next instruction in the program which is used during the fetch phase to read an instruction.
The address registers AR points at an array of data which is used during the execute phase to read an operand.
The stack pointer SP points at the top of the stack which is used to push or pop items into or from the stack.
We assume that the items in the stack communicate with a data register DR.

## Slide 26
The three registers are connected to a common address bus, and either one can provide an address for memory.
The advantage of a memory stack is that the CPU can refer to it without having to specify an address, since the address is always available and automatically updated in the stack pointer.

## Slide 27
Most computers do not provide hardware to check for stack overflow (full stack) or underflow (empty stack).
The stack limits can be checked by using two processor registers:
  one to hold the upper limit (3000 in this case),
  and the other to hold the lower limit (4001 in this case).
  After a push operation, SP is compared with the upper-limit register and after a pop operation, SP is compared with the lower-limit register.

## Slide 28: A stack organization is very effective for evaluating arithmetic expressions.

## Slide 29: Evaluation of arithmetic expressions
Reverse Polish notation, combined with a stack arrangement of registers, is the most efficient way known for evaluating arithmetic expressions.
This procedure is employed in some electronic calculators and also in some computers.
The stack is particularly useful for handling long, complex problems involving chain calculations.
It is based on the fact that any arithmetic expression can be expressed in parentheses-free Polish notation.

## Slide 31: Instruction Format

## Slide 32: Instruction Format
The bits of the instruction are divided into groups called fields.
The most common fields found in instruction formats are:
1. An operation code field that specifies the operation to be performed.
2. An address field that designates a memory address or a processor register.
3. A mode field that specifies the way the operand or the effective address is determined.

## Slide 36: The three most common CPU organizations
  Single accumulator organization: (One Address)
  ADD X /* AC  AC + M[X] */
  General register organization: (Two & Three Address)
  ADD R1, R2, R3 /* R1  R2 + R3 */
  ADD R1, R2 /* R1  R1 + R2 */
  MOV R1, R2 /* R1  R2 */
  ADD R1, X /* R1  R1 + M[X] */
  Stack organization: (Zero Address)
  PUSH X /* TOS  M[X] */
  ADD

## Slide 42: Addressing Modes
Microprocessor executes the instructions stored in memory (RAM).
It executes one instruction at a time.
Each of the instruction contains operations and operands.
Operation specifies the type of action to be performed.
For example: ADD, SUB, MOV, INC, LOAD, STORE
Operands are the data on which the operation is to be performed.
MOV B, A Here MOV is operation and (B & A) are operands.
ADD B Here ADD is operation and (B) is operand.

## Slide 43
Operand can be place either in one of the processor register or in memory.
There are different ways to get the operands.
The way in which the operand is taken from register or memory is named as addressing mode.

## Slide 44: ADDRESSING MODES
Specifies a rule for interpreting or modifying the address field of the instruction (before the operand is actually referenced)
The different ways of specifying the location of an operand in an instruction are called as addressing modes
Variety of addressing modes
- to give programming flexibility to the user
- to use the bits in the address field of the instruction efficiently
Types of addressing Modes:
  Implied Mode
  Immediate Mode
  Register Mode
  Register Indirect Mode
  Auto-increment or Auto-decrement
  Direct Address Mode
  Indirect Addressing Mode
  Relative Addressing Modes
  Indexed Addressing Mode
  Base Register Addressing Mode
  Stack addressing

## Slide 51: 1. Implied Mode
Address of the operands are specified implicitly in the definition of the instruction
  No need to specify address in the instruction
  Opcode specifies the address of the operands
  EA = AC, or EA = Stack[SP], EA: Effective Address.
  Examples :
  CMA ( A A’ )
  RAL
Notes: 3

## Slide 52: 2. Immediate Addressing
Operand is part of instruction
Operand = address field, No need to specify address in the instruction
e.g. ADD 5
  Add 5 to contents of accumulator
  5 is operand
No memory reference to fetch data
Fast to acquire an operand
Limited range
The instruction having ‘I’ (Immediate) letter fall under this category
Examples :
MVI C,25H
MVI M,7CH
LXI D,245EH
ADI 87H
Notes: 3

## Slide 53: 3. Register Addressing
Data transfer between Registers
Operand is held in register named in address filed
EA = R
Limited number of registers
Very small address field needed
  Shorter instructions
  Faster instruction fetch
No memory access
Very fast execution
Very limited address space
Multiple registers helps performance
  Requires good assembly programming or compiler writing
  N.B. C programming
    register int a;
  Examples :
  MOV A, R1
  ADD A
Address specified in the instruction is the register address
-Designated operand need to be in a register
- Shorter address than the memory address
- Saving address field in the instruction
- Faster to acquire an operand than the memory addressing
- EA = IR(R) (IR(R): Register field of IR)
Notes: 10

## Slide 54: 4.Register Indirect Addressing
Instruction specifies a register which contains the memory address of the operand
  Saving instruction bits since register address is shorter than the memory address
  Slower to acquire an operand than both the register addressing or memory addressing
  EA = [IR(R)] ([x]: Content of x)
EA = (R)
Operand is in memory cell pointed to by contents of register R
Large address space (2n)
One fewer memory access than indirect addressing
Notes: 13

## Slide 55
A special case of indirect register mode
The register whose number is included in the instruction code, contains the address of the operand.
When the address in the register is used to access memory, the value in the register is incremented or decremented by 1 (after or before the execution of the instruction), PC
Autoincrement Mode = after operand addressing , the contents of the register is incremented.
  Example : The register R4, the autoincrement mode is written as (R4)+.
Decrement Mode = before operand addressing, the contents of the register is decrement.
  Example : The register R4, the autodecrement mode is written as -(R4).
The autoincrement and autodecrement modes helps us in implementing the structure of the stack.
5. Auto-increment or Auto-decrement

## Slide 56: 6. Direct Address Mode
Instruction specifies the memory address which can be used directly to the physical memory
Faster than the other memory addressing modes
Too many bits are needed to specify the address for a large physical memory space
EA = IR(address), (IR(address): address field of IR), Effective address (EA) = address field (A)
Single memory reference to access data
No additional calculations to work out effective address
Limited address space

## Slide 57: 7. Indirect Addressing Mode
Memory cell pointed to by address field contains the address of (pointer to) the operand
The address field of an instruction specifies the address of a memory location that contains the address of the operand
When the abbreviated address is used, large physical memory can be addressed with a relatively small number of bits
Slow to acquire an operand because of an additional memory access
EA = M[IR(address)]
Large address space
2n where n = word length
May be nested, multilevel, cascaded
  e.g. EA = (((A)))
    Draw the diagram yourself
Multiple memory accesses to find operand
Hence slower

## Slide 58
EA = Displacement + CPU Register
EA = A + (R), In this the address field holds two values, A (which is the base value) and R (that holds the displacement), or vice versa.

## Slide 59: 8. Relative Addressing Modes
A version of displacement addressing
  EA = A + (R), R = Program counter, PC, A = base value
EA = A + (PC), i.e. get operand from A cells from current location pointed to by PC c.f locality of reference & cache usage
The Address fields of an instruction specifies the part of the address PC Relative Addressing Mode (R = PC)
- EA = PC + IR (address)
Address field of the instruction is short.
Large physical memory can be accessed with a small number of address bits.
Advantage
  The relative addressing mode doesn’t require memory references.
Disadvantage
  The relative addressing mode doesn’t have any disadvantages as such.

## Slide 60: 9. Indexed Addressing Mode
The index addressing mode is pretty helpful whenever the instructions in a program access an array or large ranges of memory addresses.
The effective address, in such a mode, is generated when we add a constant to the content of the register. The register content does not ever change.
Example:
XR: Index Register:
EA = XR + IR(address)
Advantage
  Using the index addressing mode, we get flexibility for specifying several locations of the memory.
Disadvantage
  It is very complex to implement the index addressing mode.

## Slide 61: 10. Base Register Addressing Mode
A holds displacement
R holds pointer to base address
R may be explicit or implicit
e.g. segment registers in 80x86
BAR: Base Address Register:
- EA = BAR + IR(address)

## Slide 62: 11. Stack Addressing
Operand is (implicitly) on top of stack
e.g.
  ADD Pop top two items from stack and add

## Slide 63: Computer Arithmetic
Addition and Subtraction
  Addition and Subtraction with signed magnitude data
  Addition and Subtraction with 2’s complement data
Multiplication Algorithms
  Booth Multiplication Algorithm
Decimal Arithmetic Unit
  BCD Adder
  BCD Subtraction
Decimal Arithmetic Operations
  Addition
  Subtraction

## Slide 64: Introduction
Arithmetic instructions in digital computer manipulate data to produce re­sults necessary for the solution of computational problems.
The four basic arithmetic operations are addition, subtraction, multiplication and division.
An arithmetic processor is the part of a processor unit that executes arithmetic operations.
The data type assumed to reside in processor registers during the execution of an arithmetic instruction is specified in the definition of the instruction.
An arithmetic instruction may specify binary or decimal data, and in each case the data may be in fixed point or floating-point form.
Fixed-point numbers may represent integers or fractions.
Negative numbers may be in signed-magnitude or signed complement representation.
We consider addition, subtraction, multiplication, and division for the following types of data:
  1. Fixed-point binary data in signed-magnitude representation
  2. Fixed-point binary data in signed-2's complement representation
  3. Floating-point binary data
  4. Binary-coded decimal (BCD) data
Complements are used in digital computers for simplifying the subtraction operation and for logical manipulation

## Slide 65: Complements
  Subtraction of Unsigned Numbers
    1) M + (rn-N)
    2) M  N : Discard end carry, Result = M-N
    3) M  N : No end carry, Result = - r’s complement of (N-M)
      Decimal Example)
      72532(M) - 13250(N) = 59282
      72532
      + 86750 (10’s complement of 13250)
      1 59282
      Result = 59282
      Binary Example)
      1010100(X) - 1000011(Y) = 0010001
      1010100
      + 0111101 (2’s complement of 1000011)
      1 0010001
      Result = 0010001
(M-N), N0
      13250(M) - 72532(N) = -59282
      13250
      + 27468 (10’s complement of 72532)
      0 40718
      Result = -(10’s complement of 40718)
      = -(59281+1) = -59282
M  N
M  N
Discard End Carry
No End Carry
      1000011(X) - 1010100(Y) = -0010001
      1000011
      + 0101100 (2’s complement of 1010100)
      0 1101111
      Result = -(2’s complement of 1101111)
      = -(0010000+1) = -0010001
X  Y
X  Y

## Slide 66: Addition and Subtraction
Addition and Subtraction with Signed-Magnitude Data

## Slide 68
Hardware Algorithm

## Slide 69
Addition and Subtraction with Signed-2's
+ 33 is represented as 00100001 and - 33 as 1101 1 1 1 1 .
Note that 11011111 is the 2's complement of 00100001, and vice versa.
The addition of two numbers in signed-2's complement form consists of adding the numbers with the sign bits treated the same as the other bits of the number.
A carry-out of the sign-bit position is discarded.
The subtraction consists of first taking the 2' s complement of the subtrahend and then adding it to the minuend.

## Slide 71
Multiplication Algorithms
Multiplication of two fixed-point binary numbers in signed-magnitude representation
The process consists of looking at successive bits of the multiplier, least significant bit first.
If the multiplier bit is a 1, the multiplicand is copied down; otherwise, zeros are copied down.
The numbers copied down in successive lines are shifted one position to the left from the previous number.
Finally, the numbers are added and their sum forms the product.

## Slide 72: Hardware Implementation for Signed-Magnitude Data
Number of bits in the multiplier
partial product
multiplier
Multiplicand
Initially, the multiplicand is in register B and the multiplier in Q.
The sum of A and B forms a partial product which is transferred to the EA register.
Both partial product and multiplier are shifted to the right.
This shift will be denoted by the statement shr EAQ to designate the right shift depicted in Fig. 10-5.
The least significant bit of A is shifted into the most significant position of Q, the bit from E is shifted into the most significant position of A, and 0 is shifted into E.
After the shift, one bit of the partial product is shifted into Q, pushing the multiplier bits one position to the right.
In this manner, the rightmost flip-flop in register Q, designated by Qn, will hold the bit of the multiplier, which must be inspected next.

## Slide 73
Hardware Algorithm
Initially, the multiplicand is in B and the multiplier in Q.
Their corresponding signs are in Bs, and Qs., respectively.
The signs are compared, and both A and Q are set to correspond to the sign of the product since a double-length product will be stored in registers A and Q.
Registers A and E are cleared and the sequence counter SC is set to a number equal to the number of bits of the multiplier.
We are assuming here that operands are transferred to registers from a memory unit that has words of n bits.
Since an operand must be stored with its sign, one bit of the word will be occupied by the sign and the magnitude will consist of n - 1 bits.
After the initialization, the low-order bit of the multiplier in Q, is tested.
If it is a 1, the multiplicand in B is added to the present partial product in A .
If it is a 0 , nothing is done. Register EAQ i s then shifted once to the right to form the new partial product.
The sequence counter is decremented by 1 and its new value checked.
If it is not equal to zero, the process is repeated and a new partial product is formed.
The process stops when SC = 0.
Note that the partial product formed in A is shifted into Q one bit at a time and eventually replaces the multiplier.
The final product is available in both A and Q, with A holding the most significant bits and Q holding the least significant bits.

## Slide 76
Booth Multiplication Algorithm
Booth algorithm gives a procedure for multiplying binary integers in signed-2's complement representation.
It operates on the fact that strings of 0's in the multiplier require no addition but just shifting, and a string of 1's in the multiplier from bit weight 2k to weight 2m can be treated as 2K+1 - 2m.
For example, the binary number 001 110 ( + 14) has a string of 1's from 23 to 21. (k = 3, m = 1).
The number can be represented as 2k+ l - 2m = 24 - 21 = 16 - 2 = 14.
Therefore, the multiplication M x 14, where M is the multiplicand and 14 the multiplier, can be done as M x 24 - M X 21
Thus the product can be obtained by shifting the binary multiplicand M four times to the left and subtracting M shifted left once.
Booth algorithm requires examination of the multiplier bits and shifting of the partial product. Prior to the shifting, the multiplicand may be added to the partial product, subtracted from the partial product, or left unchanged according to the following rules:
  The multiplicand is subtracted from the partial product upon encountering the first least significant 1 in a string of 1's in the multiplier.
  The multiplicand is added to the partial product upon encountering the first 0 (provided that there was a previous 1) in a string of 0's in the multiplier.
  The partial product does not change when the multiplier bit is identical to the previous multiplier bit.

## Slide 77
Hardware for Booth algorithm.

## Slide 78
Flowchart for Booth algorithm

## Slide 79
(-9)*(-13)=+117

## Slide 80
    BR = -5 = 1011, BR'+1 = 0101
    QR = -7 = 1001
OPERATION | AC | QR | Qn+1 | SC
 | 0000 | 1001 | 0 | 4
AC + BR’ + 1 | 0101 | 1001 | 0 | 
ASHR | 0010 | 1100 | 1 | 3
AC + QR | 1101 | 1100 | 1 | 
ASHR | 1110 | 1110 | 0 | 2
ASHR | 1111 | 0111 | 0 | 1
AC + BR’ + 1 | 0010 | 0011 | 1 | 0
Product is calculated as follows:
Product = AC QR Product = 0010 0011 = 35
Example : (-5)*(-7)=+35

## Slide 85: BCD SUBTRACTION