## Slide 1: UNIT-4
The Memory Organization

## Slide 2: Contents
Memory Hierarchy
Main Memory
  RAM and ROM Chips
  ROM, PROM, EEPROM, Flash Memory
Auxiliary Memory
  Magnetic Disks
  Magnetic Tape
Associative Memory
  Block Diagram
  Read Operation
  Write Operation
Cache Memory
Virtual Memory
  Address Space and Memory Space
  Page replacement

## Slide 3: Memory Hierarchy

## Slide 4
The memory unit is an essential component in any digital computer since it is needed for storing programs and data.
Most general-purpose computers would run more efficiently if they were equipped with additional storage beyond the capacity of the main memory.
Not all accumulated information is needed by the processor at the same time.
Therefore, it is more economical to use low-cost storage devices to serve as a backup for storing the information that is not currently used by the CPU.
The memory unit that communicates directly with the' CPU is called the main memory.
Devices that provide backup storage are called auxiliary memory.
The most common auxiliary memory devices used in computer systems are magnetic disks and tapes.
They are used for storing system programs, large data files, and other backup information.
Only programs and data currently needed by the processor reside in main memory.

## Slide 5
All other information is stored in auxiliary memory and transferred to main memory when needed.
The total memory capacity of a computer can be visualized as being a hierarchy of components.
The memory hierarchy system consists of all storage devices employed in a computer system from the slow but high-capacity auxiliary memory to a relatively faster main memory, to an even smaller and faster cache memory accessible to the high-speed processing logic.
At the bottom of the hierarchy are the relatively slow magnetic tapes used to store removable files.
Next are the magnetic disks used as backup storage.
The main memory occupies a central position by being able to communicate directly with the CPU and with auxiliary memory devices through an I/O processor.
When programs not residing in main memory are needed by the CPU, they are brought in from auxiliary memory.
Programs not currently needed in main memory are transferred into auxiliary memory to provide space for currently used programs and data.

## Slide 6
Cache memory:
  special very-high-speed memory called a cache is sometimes used to increase the speed of processing by making current programs and data available to the CPU at a rapid rate.
  The cache memory is employed in computer systems to compensate for the speed differential between main memory access time and processor logic.
  CPU logic is usually faster than main memory access time, with the result that processing speed is limited primarily by the speed of main memory.
  A technique used to compensate for the mismatch in operating speeds is to employ an extremely fast, small cache between the CPU and main memory whose access time is close to processor logic clock cycle time.
  The cache is used for storing segments of programs currently being executed in the CPU and temporary data frequently needed in the present calculations.

## Slide 7
While the VO processor manages data transfers between auxiliary memory and main memory,
the cache organization is concerned with the transfer of information between main memory and CPU.
As the storage capacity of the memory increases, the cost per bit for storing binary information decreases and the access time of the memory becomes longer.
The auxiliary memory has a large storage capacity, is relatively inexpensive, but has low access speed compared to main memory.
The cache memory is very small, relatively expensive, and has very high access speed.
Thus as the memory access speed increases, so does its relative cost.
The overall goal of using a memory hierarchy is to obtain the highest-possible average access speed while minimizing the total cost of the entire memory system.

## Slide 8
Auxiliary and cache memories are used for different purposes.
The cache holds those parts of the program and data that are most heavily used.
The auxiliary memory holds those parts that are not presently used by the CPU.
the CPU has direct access to both cache and main memory but not to auxiliary memory.
The transfer from auxiliary to main memory is usually done by means of direct memory access of large blocks of data

## Slide 9
Multiprogramming:
  Many operating systems are designed to enable the CPU to process a number of independent programs concurrently.
  This concept, called multiprogramming, refers to the existence of two or more programs in different parts of the memory hierarchy at the same time.
  In this way it is possible to keep all parts of the computer busy by working with several programs in sequence.
  For example, suppose that a program is being executed in the CPU and an I/O transfer is required.
  The CPU initiates the VO processor to start executing the transfer.
  This leaves the CPU free to execute another program.
  In a multiprogramming system, when one program is waiting for input or output transfer, there is another program ready to utilize the CPU.
  The part of the computer system that supervises the flow of information between auxiliary memory and main memory is called the memory management system.

## Slide 10: Main Memory

## Slide 20: Memory Address Map

## Slide 21: Memory Connection to CPU

## Slide 22: Auxiliary Memory

## Slide 25: Magnetic Disks

## Slide 29: Magnetic Tape

## Slide 32: Associative memory
Need for Data Search in Applications:
  Many data-processing applications require searching for items in a memory-stored table.
  Examples include:
    An assembler program searching a symbol address table for a symbol's binary equivalent.
    Searching an account number in a file to find the holder's name and account status.
Conventional Search Methods:
  Traditionally, tables are stored in memory where items are addressed sequentially.
  The search strategy involves choosing a sequence of addresses, reading memory content at each address, and comparing it with the search item until a match is found.
  The efficiency of this search process depends on:
    The item's location in memory.
    The effectiveness of the search algorithm.
  Various search algorithms are designed to minimize memory accesses.

## Slide 33
Content Addressable Memory (CAM):
  CAM allows faster search by identifying data based on its content rather than its address.
  Known as Associative Memory or Content Addressable Memory (CAM).
  Unlike traditional memory, CAM accesses data in parallel based on content, without needing specific addresses.
Advantages of Associative Memory:
  When writing data, CAM finds an empty location automatically without requiring an address.
  When reading data, CAM locates all words that match specified content and marks them for reading.
Parallel Search Capability:
  CAM is well-suited for parallel searches using data association.
  Searches can be performed on entire words or specific fields within a word.
Cost and Use Cases:
  Associative memory is more expensive than Random Access Memory (RAM).
  It includes storage and logic circuits for content matching.
  Due to high costs, CAM is used in applications where search time is critical and needs to be very short.

## Slide 34: Block diagram of Associative memory

## Slide 40: Match Logic

## Slide 44: Read and write operations