## Slide 1
Computer Organization and Architecture
UNIT-1
Register Transfer and Micro-Operations: Register Transfer Language, Register Transfer, memory Transfers, Bus construction with Multiplexers, Arithmetic Micro-operations, Logic Micro-operations, Shift Micro-operations, Arithmetic Logic Shift Unit.
UNIT-2
Basic Computer Organization: Instruction codes, Computer Registers, Computer Instructions, Timing and Control, Instruction Cycle, Memory-Reference Instructions, Input- Output and Interrupt.
UNIT-3
Central Processing Unit: General registers Organization, Stack Organization, Instruction Formats, Addressing Modes, Data Transfer and Manipulation, Program Control.
UNIT-4
Computer Arithmetic: Introduction, Addition and Subtraction, Booth Multiplication Algorithm.
Memory Organization: Memory Hierarchy, Main Memory, Auxiliary memory, Associative Memory, Cache Memory, Virtual Memory.
UNIT-5
Input-Output Organization: Peripheral Devices, Input-output Interface, Asynchronous Data Transfer, Priority Interrupt, Direct Memory Access (DMA), Input-Output Processor.
Pipeline and Parallel Processing: Parallel processing, Pipelining, Arithmetic pipeline,
Instruction pipeline.

## Slide 2: UNIT-2: BASIC COMPUTER ORGANIZATION AND DESIGN
BASIC COMPUTER ORGANIZATION AND DESIGN:
  Instruction Codes,
  Computer Registers,
  Computer Instructions,
  Timing and Control,
  Instruction Cycle,
  Memory-Reference Instructions,
  Input-Output and Interrupt,
  Complete Computer Description,
  Design of Basic Computer,
  Design of Accumulator Logic.

## Slide 3: Instruction Codes
Program:
  The set of instructions that specify the operations, operands, and the sequence by which processing has to occur.
Instruction:
  A binary code that specifies a sequence of micro-operations for the computer.
Instruction Cycle:
  The computer reads each instruction from memory and places it in a control register.
  The control then interprets the binary code of the instruction and proceeds to execute it by issuing a sequence of micro-operations.
Instruction Code:

## Slide 4: Stored Program Organization

## Slide 5: Addressing of Operand

## Slide 6: Worksheet-1
A computer uses a memory unit with 256k words of 32 bits each. A binary instruction code is stored in one word of memory. The instruction has four parts: an indirect bit. an operation code, a register code part to specify one of 64 registers, and an address part.
  a. How many bits are there in the operation code, the register code part, and the address part?
  b. Draw the instruction word format and indicate the number of bits in each part.
  c. How many bits are there in the data and address inputs of the memory?

## Slide 7: Sol.

## Slide 8: Worksheet-2
What is the difference between a direct and an indirect address instruction? How many references to memory are needed for such type of instruction to bring an operand into a processor registet?

## Slide 9: Sol.
A direct address instruction needs two references to memory:
  (1) Read instruction;
  (2) Read operand.
An indirect address instruction needs three references to memory:
  (1) Read instruction;
  (2) Read effective address;
  (3) Read operand.

## Slide 10: 2. Computer Registers
It is necessary to provide a register in the control unit for storing the instruction code after it is read from memory.
The computer needs processor registers for manipulating data and a register for holding a memory address.
Figure 2.4: Basic Computer Register and Memory

## Slide 11: Computer Registers

## Slide 12: Computer Registers
The data register (DR) holds the operand read from memory.
The accumulator (AC) register is a general purpose processing register.
The instruction read from memory is placed in the instruction register (IR).
The temporary register (TR) is used for holding temporary data during the processing.
The memory address register (AR) has 12 bits since this is the width of a memory address.
The program counter (PC) also has 12 bits and it holds the address of the next instruction to be read from memory after the current instruction is executed.
Two registers are used for input and output.
  The input register (INPR) receives an 8-bit character from an input device.
  The output register (OUTR) holds an 8-bit character for an output device.

## Slide 13: Common Bus System
The basic computer has eight registers, a memory unit, and a control unit
Paths must be provided to transfer information from one register to another and between memory and registers.
A more efficient scheme for transferring information in a system with many registers is to use a common bus.
The connection of the registers and memory of the basic computer to a common bus system is shown in Fig.
The outputs of seven registers and memory are connected to the common bus.
The specific output that is selected for the bus lines at any given time is determined from the binary value of the selection variables S2, S1, and S0.
The number along each output shows the decimal equivalent of the required binary selection.
For example, the number along the output of DR is 3. The 16-bit outputs of DR are placed on the bus lines when S2S1S0 = 011.

## Slide 14
Common Bus
System

## Slide 15
The lines from the common bus are connected to the inputs of each register and the data inputs of the memory.
The particular register whose LD (load) input is enabled receives the data from the bus during the next clock pulse transition.
The memory receives the contents of the bus when its write input is activated.
The memory places its 16-bit output onto the bus when the read input is activated and S2S1S0 = 111.
Two registers, AR and PC, have 12 bits each since they hold a memory address.
When the contents of AR or PC are applied to the 16-bit common bus, the four most significant bits are set to 0's.
When AR or PC receives information from the bus, only the 12 least significant bits are transferred into the register.
The input register INPR and the output register OUTR have 8 bits each.
They communicate with the eight least significant bits in the bus.
INPR is connected to provide information to the bus but OUTR can only receive information from the bus.

## Slide 16
This is because INPR receives a character from an input device which is then transferred to AC.
OUTR receives a character from AC and delivers it to an output device.
Five registers have three control inputs: LD (load), INR (increment), and CLR (clear).
This type of register is equivalent to a binary counter with parallel load and synchronous clear.
Two registers have only a LD input.
The input data and output data of the memory are connected to the common bus, but the memory address is connected to AR.
Therefore, AR must always be used to specify a memory address.
The 16 inputs of AC come from an adder and logic circuit. This circuit has three sets of inputs.
  One set of 16-bit inputs come from the outputs of AC.
  Another set of 16-bit inputs come from the data register DR.
  The result of an addition is transferred to AC and the end carry-out of the addition is transferred to flip-flop E (extended AC bit).
  A third set of 8-bit inputs come from the input register INPR.

## Slide 17
The content of any register can be applied onto the bus and an operation can be performed in the adder and logic circuit during the same clock cycle.
For example, the two microoperations DR AC and AC DR can be executed at the same time.
This can be done by placing the content of AC on the bus (with S2S1S0 = 100), enabling the LD (load) input of DR, transferring the content of DR through the adder and logic circuit into AC, and enabling the LD (load) input of AC, all during the same clock cycle.

## Slide 18: Workseet-3
The following control inputs are active in the bus system shown in Fig. 5-4.For each case, specify the register transfer that-will be executed during the next clock transition.

## Slide 19: Computer Instructions
The basic computer has three instruction code formats

## Slide 20
Memory-reference instruction:
  A memory-reference instruction uses 12 bits to specify an address and one bit to specify the addressing mode I.
  I is equal to 0 for direct address and to 1 for indirect address.
Register reference instructions
  The register reference instructions are recognized by the operation code 111 with a 0 in the leftmost bit (bit 15) of the instruction.
  A register-reference instruction specifies an operation on or a test of the AC register.
  An operand from memory is not needed; therefore, the other 12 bits are used to specify the operation or test to be executed.
Input-output instruction:
  An input-output instruction does not need a reference to memory and is recognized by the operation code 111 with a 1 in the leftmost bit of the instruction.
  The remaining 12 bits are used to specify the type of input-output operation or test performed.

## Slide 22: Instruction Set Completeness
A computer should have a set of instructions so that the user can construct machine language programs to evaluate any function.
The set of instructions are said to be complete if the computer includes a sufficient number of instructions in each of the following categories:
  Arithmetic, logical, and shift instructions
  Instructions for moving information to and from memory and processor registers
  Program control instructions together with instructions that check status conditions
  Input and output instructions

## Slide 23: Class Test-1
1. Consider the following register transfer statements
xT: R1  R1 + R1 (if x = 1); xT: R1 R2 (if x = 0)
where T represents clock. Draw a diagram showing the hardware implementation of the above statements.
2. Logic microoperations can be used to manipulate individual bits or a portions of a word in a register. Explain the applications of logic microoperations.
3. What do you mean by arithmetic logic shift unit? With a neat diagram, explain the design process of arithmetic logic shift unit.
4. A digital computer has a common bus system for 8 registers of 32bits each. The bus is controlled with multiplexers
How many selection inputs are there in each multiplexer?
What sizes of multiplexers are needed?
How many multiplexers are there in the bus?

## Slide 24: 4. Timing and Control
The timing for all registers in the basic computer is controlled by a master clock generator.
The clock pulses are applied to all flip-flops and registers in the system, including the flip-flops and registers in the control unit.
The clock pulses do not change the state of a register unless the register is enabled by a control signal.
The control signals are generated in the control unit and provide control inputs for the multiplexers in the common bus, control inputs in processor registers, and microoperations for the accumulator.
Functions of the Control Unit –
  It coordinates the sequence of data movements into, out of, and between a processor’s many sub-units.
  It interprets instructions.
  It controls data flow inside the processor.
  It receives external instructions or commands to which it converts to sequence of control signals.
  It controls many execution units(i.e. ALU, data buffers and registers) contained within a CPU.
  It also handles multiple tasks, such as fetching, decoding, execution handling and storing results.
There are two major types of control Units:
  Hardwired control
  Microprogrammed control
Clock Time
Clock time (CT) is the period of the clock that synchronizes the circuits in a processor. It is the reciprocal of the clock frequency.
For example, a 1 GHz processor has a cycle time of 1.0 ns and a 4 GHz processor has a cycle time of 0.25 ns.

## Slide 25: Hardwired control Vs Microprogrammed control

## Slide 26: Hardwired control unit
Components of Control unit are
  1. Two decoders
  2. A sequence counter
  3. Control logic gates
An instruction read from memory is placed in the instruction register (IR). It is divided into three parts: The I bit, the operation code, and bits 0 through 11.
The operation code in bits 12 through 14 are decoded with a 3 x 8 decoder. The eight outputs of the decoder are designated by the symbols D0 through D7.
Bit 15 of the instruction is transferred to a flip-flop designated by the symbol I.
Bits 0 through 11 are applied to the control logic gates.
The 4-bit sequence counter can count in binary from 0 through 15.

## Slide 27
D3T4: SC ← 0

## Slide 28
The outputs of counter are decoded into 16 timing signals T0 through T15.
The sequence counter SC can be incremented or cleared synchronously.
Most of the time, the counter is incremented to provide the sequence of timing signals out of 4 X 16 decoder.
Once in awhile, the counter is cleared to 0, causing the next timing signal to be T0.
As an example, consider the case where SC is incremented to provide timing signals T0, T1, T2, T3 and T4 in sequence.
At time T4, SC is cleared to 0 if decoder output D3 is active.
This is expressed symbolically by the statement
D3T4: SC ← 0

## Slide 29: Timing Diagram
shows the time relationship of the control signals

## Slide 30
The timing diagram shows the time relationship of the control signals.
The sequence counter SC responds to the positive transition of the clock.
Initially, the CLR input of SC is active
The first positive transition of the clock clears SC to 0, which in turn activates the timing T0 out of the decoder.
T0 is active during one clock cycle.
The positive clock transition labeled T0 in the diagram will trigger only those registers whose control inputs are connected to timing signal T0.
SC is incremented with every positive clock transition, unless its CLR input is active.
This procedures the sequence of timing signals T0, T1, T2, T3 and T4, and so on.
If SC is not cleared, the timing signals will continue with T5, T6, up to T15 and back to T0.
The last three waveforms shows how SC is cleared when D3T4 = 1.
Output D3 from the operation decoder becomes active at the end of timing signal T2. When timing signal T4 becomes active, the output of the AND gate that implements the control function D3T4 becomes active.
This signal is applied to the CLR input of SC. On the next positive clock transition the counter is cleared to 0. This causes the timing signal T0 to become active instead of T5 that would have been active if SC were incremented instead of cleared.

## Slide 31
Block diagram of 8086 Micro computer

## Slide 33: Instruction Cycle
A program residing in the memory unit of the computer consists of a sequence of instructions.
The program is executed in the computer by going through a cycle for each instruction.
Each instruction cycle in turn is subdivided into a sequence of sub cycles or phases.
In the basic computer each instruction cycle consists of the following phases:
  Fetch an instruction from memory.
  Decode the instruction.
  Read the effective address from memory if the instruction has an indirect address.
  Execute the instruction.
Upon the completion of step 4, the control goes back to step 1 to fetch, decode, and execute the next instruction.

## Slide 34
Fetch and Decode:
  Initially, the program counter PC is loaded with the address of the first instruction in the program.
  The sequence counter SC is cleared to 0, providing a decoded timing signal T0.
  The microoperations for the fetch and decode phases can be specified by the following register transfer statements.

## Slide 36
Determine the Type of Instruction
  The timing signal that is active after the decoding is T3.
  During time T3, the control unit determine the type of instruction that was read from the memory.
  The flowchart of fig.5-9 shows the initial configurations for the instruction cycle and also how the control determines the instruction cycle type after the decoding.
  Decoder output D7 is equal to 1 if the operation code is equal to binary 111.
  If D7=1, the instruction must be a register-reference or input-output type.
  If D7 = 0, the operation code must be one of the other seven values 000 through 110, specifying a memory-reference instruction.
  Control then inspects the value of the first bit of the instruction, which is now available in flip-flop I.
  If D7 = 0 and I = 1, indicates a memory-reference instruction with an indirect address. So it is then necessary to read the effective address from memory.
  If D7 = 0 and I = 0, indicates a memory-reference instruction with a direct address.
  If D7 = 1 and I = 0, indicates a register-reference instruction.
  If D7 = 01and I = 1, indicates an input-output instruction.
  The three instruction types are subdivided into four separate paths.
  The selected operation is activated with the clock transition associated with timing signal T3.
  This can be symbolized as follows:

## Slide 38: Register-Reference Instructions
Register-reference instructions are recognized by the control when D7 = 1 and I=0.
These instructions use bits 0 through 11 of the instruction code to specify one of 12 instructions.
These 12 bits are available in IR (0-11).
The control functions and microoperations for the register-reference instructions are listed in Table.
These instructions are executed with the clock transition associated with timing variable T3.
Control function needs the Boolean relation D7I’T3, which we designate for convenience by the symbol r.
By assigning the symbol Bi to bit i of IR, all control functions can be simply denoted by rBi.

## Slide 39
These 12 bits are available in IR (0-11).

## Slide 40
For example, the instruction CLA has the hexadecimal code 7800, which gives the binary equivalent 0111 1000 0000 0000. The first bit is a zero and is equivalent to I’.
The next three bits constitute the operation code and are recognized from decoder output D7.
Bit 11 in IR is 1 and is recognized from B11. The control function that initiates the microoperation for this instruction is D7I’T3 B11 = rB11.
The execution of a register-reference instruction is completed at time T3.
The sequence counter SC is cleared to 0 and the control goes back to fetch the next instruction with timing signal T0.
The first seven register-reference instructions perform clear, complement, circular shift, and increment microoperations on the AC or E registers.
The next four instructions cause a skip of the next instruction in sequence when a stated condition is satisfied. The skipping of the instruction is achieved by incrementing PC once again.
The condition control statements must be recognized as part of the control conditions.
The AC is positive when the sign bit in AC(15) = 0; it is negative when AC(15) = 1. The content of AC is zero (AC = 0) if all the flip-flops of the register are zero.
The HLT instruction clears a start-stop flip-flop S and stops the sequence counter from counting.

## Slide 41: Memory-Reference Instructions
Table 5-4 lists the seven memory-reference instructions.
The decoded output Di for i = 0, 1, 2, 3, 4, 5, and 6 from the operation decoder that belongs to each instruction is included in the table.
The effective address of the instruction is in the address register AR and was placed there during timing signal T2 when I= 0, or during timing signal T3 when I = 1.
The execution of the memory-reference instructions starts with timing signal T4.
The symbolic description of each instruction is specified in the table in terms of register transfer notation.

## Slide 43
AND to AC:
  This is an instruction that performs the AND logic operation on pairs of bits in AC and the memory word specified by the effective address.
  The result of the operation is transferred to AC.
  The microoperations that execute this instruction are:
ADD to AC:
  This instruction adds the content of the memory word specified by the effective address to the value of AC.
  The sum is transferred into AC and the output carry Cout is transferred to the E (extended accumulator) flip-flop.
  The microoperations needed to execute this instruction are

## Slide 44
LDA: Load to AC
  This instruction transfers the memory word specified by the effective address to AC.
  The microoperations needed to execute this instruction are
STA: Store AC
  This instruction stores the content of AC into the memory word specified by the effective address.
  Since the output of AC is applied to the bus and the data input of memory is connected to the bus, we can execute this instruction with one microoperation.

## Slide 45
BUN: Branch Unconditionally
  This instruction transfers the program to the instruction specified by the effective address.
  The BUN instruction allows the programmer to specify an instruction out of sequence and we say that the program branches (or jumps) unconditionally.
  The instruction is executed with one microoperation:

## Slide 46
BSA: Branch and Save Return Address
  This instruction is useful for branching to a portion of the program called a subroutine or procedure.
  When executed, the BSA instruction stores the address of the next instruction in sequence (which is available in PC) into a memory location specified by the effective address.
  The effective address plus one is then transferred to PC to serve as the address of the first instruction in the subroutine.
  This operation was specified with the following register transfer:

## Slide 47
A numerical example that demonstrates how this instruction is used with a subroutine is shown in Fig.

## Slide 48
The BSA instruction is assumed to be in memory at address 20.
The I bit is 0 and the address part of the instruction has the binary equivalent of 135.
After the fetch and decode phases, PC contains 21, which is the address of the next instruction in the program (referred to as the return address). AR holds the effective address 135.
This is shown in part (a) of the figure.
The BSA instruction performs the following numerical operation:
When this instruction is executed, control goes to the indirect phase to read the effective address at location 135, where it finds the previously saved address 21.
When the BUN instruction is executed, the effective address 21 is transferred to PC.
The next instruction cycle finds PC with the value 21, so control continues to execute the instruction at the return address.
The BSA instruction must be executed with a sequence of two microoperations:

## Slide 49
ISZ: Increment and Skip if Zero
  This instruction increment the word specified by the effective address, and if the incremented value is equal to 0, PC is incremented by 1 to skip the next instruction in the program.
  Since it is not possible to increment a word inside the memory, it is necessary to read the word into DR, increment DR, and store the word back into memory.
  This is done with the following sequence of microoperations:

## Slide 50
Control Flowchart:
  A flowchart showing all microoperations for the execution of the seven memory-reference instructions is shown in Fig. 5.11.

## Slide 51
Input-Output and Interrupt
Input-Output
  Input-Output Configuration
  Input-Output Instructions
Interrupt
  Program Interrupt
  Interrupt cycle
  A

## Slide 52
A computer can serve no useful purpose unless it communicates with the external environment.
Instructions and data stored in memory must come from some input device.
Computational results must be transmitted to the user through some output device.
To demonstrate the most basic requirements for input and output communication, we will use as an illustration a terminal unit with a keyboard and printer.
Input-Output

## Slide 53: Input-Output Configuration
The terminal sends and receives serial information.
Each quantity of information has eight bits of an alphanumeric code.
The serial information from the keyboard is shifted into the input register INPR.
The serial information for the printer is stored in the output register OUTR.
These two registers communicate with a communication interface serially and with the AC in parallel.
The input—output configuration is shown in Fig.

## Slide 54
The serial information from the keyboard is shifted into the input register INPR.
The serial information for the printer is stored in the output register OUTR.
The input flag FGI is cleared to 0
When a key is struck in the keyboard, an 8-bit alphanumeric code is shifted into INPR and the input flag FGI is set to 1.
The computer checks the flag bit; if it is 1, the information from INPR is transferred in parallel into AC and FGI is cleared to 0.
The output flag FGO is set to 1, the information from AC is transferred in parallel to OUTR and FGO is cleared to 0.
The output device accepts the coded information, prints the corresponding character, and when the operation is completed, it sets FGO to 1.

## Slide 55: The process of input information transfer
Initially, the input flag FGI is cleared to 0.
When a key is struck in the keyboard, an 8-bit alphanumeric code is shifted into INPR and the input flag FGI is set to 1.
As long as the flag is set, the information in INPR cannot be changed by striking another key.
The computer checks the flag bit; if it is 1, the information from INPR is transferred in parallel into AC and FGI is cleared to 0.
Once the flag is cleared, new information can be shifted into INPR by striking another key.

## Slide 56: The process of outputting information
The output register OUTR works similarly but the direction of information flow is reversed.
Initially, the output flag FGO is set to 1. The computer checks the flag bit; if it is 1, the information from AC is transferred in parallel to OUTR and FGO is cleared to 0.
The output device accepts the coded information, prints the corresponding character, and when the operation is completed, it sets FGO to 1.
The computer does not load a new character into OUTR when FGO is 0 because this condition indicates that the output device is in the process of printing the character.

## Slide 57: Input-Output Instructions
Input and output instructions are needed for transferring information to and from AC register, for checking the flag bits, and for controlling the interrupt facility.
Input-output instructions have an operation code 1111 and are recognized by the control when D7 = 1 and I = 1.
The remaining bits of the instruction specify the particular operation.
The control functions and microoperations for the input-output instructions are listed in Table.
These instructions are executed with the clock transition associated with timing signal T3.
Each control function needs a Boolean relation D7IT3, which we designate for convenience by the symbol p.
The control function is distinguished by one of the bits in IR (6-11).
By assigning the symbol Bi to bit i of IR, all control functions can be denoted by pBi for i = 6 though 11.
The sequence counter SC is cleared to 0 when p = D7IT3 = 1.
The last two instructions set and clear an interrupt enable flip-flop IEN.

## Slide 59: Program Interrupt:
The computer keeps checking the flag bit, and when it finds it set, it initiates an information transfer.
The difference of information flow rate between the computer and that of the input—output device makes this type of transfer inefficient.
Example: To see why this is inefficient, consider a computer that can go through an instruction cycle in 1µs.
Assume that the input-output device can transfer information at a maximum rate of 10 characters per second.
This is equivalent to one character every 100,000 µs.
Two instructions are executed when the computer checks the flag bit and decides not to transfer the information.
This means that at the maximum rate, the computer will check the flag 50,000 times between each transfer.
The computer is wasting time while checking the flag instead of doing some other useful processing task.

## Slide 60
An alternative to the programmed controlled procedure is to let the external device inform the computer when it is ready for the transfer.
In the meantime the computer can be busy with other tasks. This type of transfer uses the interrupt facility.
While the computer is running a program, it does not check the flags.
When a flag is set, the computer is momentarily interrupted from the current program.
The computer deviates momentarily from what it is doing to perform of the input or output transfer.
It then returns to the current program to continue what it was doing before the interrupt.
The interrupt enable flip-flop IEN can be set and cleared with two instructions.
  When IEN is cleared to 0 (with the IOF instruction), the flags cannot interrupt the computer.
  When IEN is set to (with the ION instruction), the computer can be interrupted.

## Slide 61
The way that the interrupt is handled by the computer can be explained by means of the flowchart of Fig.
An interrupt flip-flop R is included in the computer. When R = 0, the computer goes through an instruction cycle.
During the execute phase of the instruction cycle IEN is checked by the control.
If it is 0, it indicates that the programmer does not want to use the interrupt, so control continues with the next instruction cycle.
If IEN is 1, control checks the flag bits.
If both flags are 0, it indicates that neither the input nor the output registers are ready for transfer of information.
In this case, control continues with the next instruction cycle.
If either flag is set to 1 while IEN = 1, flip-flop R is set to 1.
At the end of the execute phase, control checks the value of R, and if it is equal to 1, it goes to an interrupt cycle instead of an instruction cycle.

## Slide 63: Interrupt cycle:
The interrupt cycle is a hardware implementation of a branch and save return address operation.
The return address available in PC is stored in a specific location.
This location may be a processor register, a memory stack, or a specific memory location.
An example that shows what happens during the interrupt cycle is shown in Fig.
When an interrupt occurs and R is set to 1 while the control is executing the instruction at address 255.
At this time, the returns address 256 is in PC.
The programmer has previously placed an input—output service program in memory starting from address 1120 and a BUN 1120 instruction at address 1. This is shown in Fig (a).

## Slide 64
When control reaches timing signal T0 and finds that R = 1, it proceeds with the interrupt cycle.
The content of PC (256) is stored in memory location 0, PC is set to 1, and R is cleared to 0.
The branch instruction at address 1 causes the program to transfer to the input—output service program at address 1120.
This program checks the flags, determines which flag is set, and then transfers the required input or output information.
Once this is done, the instruction ION is executed to set IEN to 1 (to enable further interrupts), and the program returns to the location where it was interrupted. This is shown in Fig. (b).

## Slide 66
The interrupt cycle is a hardware implementation of a branch and save return address operation.
The return address available in PC is stored in a specific location where it can be found later when the program returns to the instruction at which it was interrupted. This location may be a processor register, a memory stack, or a specific memory location.
Here we choose the memory location at address 0 as the place for storing the return address.
Control then inserts address 1 into PC and clears IEN and R so that no more interruptions can occur until the interrupt request from the flag has been serviced.
An example that shows what happens during the interrupt cycle is shown in Figure.
Suppose that an interrupt occurs and R = 1, while the control is executing the instruction at address 255. At this time, the return address 256 is in PC
The programmer has previously placed an input-output service program in memory starting from address 1120 and a BUN 1120 instruction at address 1
The content of PC (256) is stored in memory location 0, PC is set to 1, and R is cleared to 0.

## Slide 67
At the beginning of the next instruction cycle, the instruction that is read from memory is in address 1 since this is the content of PC.
The branch instruction at address 1 causes the program to transfer to the input-output service program at address 1120.
This program checks the flags, determines which flag is set, and then transfers the required input or output information.
Once this is done, the instruction ION is executed to set IEN to 1 (to enable further interrupts), and the program returns to the location where it was interrupted.
The instruction that returns the computer to the original place in the main program is a branch indirect instruction with an address part of 0.
This instruction is placed at the end of the I/O service program.
The execution of the indirect BUN instruction results in placing into PC the return address from location 0.

## Slide 68: Register transfer statements for the interrupt cycle

## Slide 69: Complete Computer Description
Flowchart for computer operation.

## Slide 70
Control Functions and Microoperations for the Basic Computer

## Slide 72: Design of Basic Computer
The basic computer consists of the following hardware components:
  A memory unit with 4096 words of 16 bits each
  Nine registers: AR, PC, DR, AC, IR, TR, OUTR, INPR, and SC
  Seven flip-flops: I, S , E, R, IEN, FGI, and FGO
  Two decoders: a 3 x 8 operation decoder and a 4 x 16 timing decoder
  A 16-bit common bus
  Control logic gates
  Adder and logic circuit connected to the input of AC

## Slide 73: Control Logic Gates
The outputs of the control logic circuit are:
  1. Signals to control the inputs of the nine registers
  2. Signals to control the read and write inputs of memory
  3, Signals to set, clear, or complement the flip-flops
  4. Signals for S2, S1, and S0 to select a register for the bus
  5. Signals to control the AC adder and logic circuit

## Slide 74: Control of Registers and Memory
The control inputs of the registers are LD (load), INR (increment), and CLR (clear).
The control functions can be combined into three Boolean expressions as follows:
The read operation is recognized from the symbol  M [AR]
The output of the logic gates that implement the Boolean expression above must be connected to the read input of memory.

## Slide 75
The control gate logic associated with AR
In a similar fashion we can derive the control gates for the other registers as well as the logic needed to control the read and write inputs of memory.

## Slide 76: Control of Single Flip-flops
The control gates for the seven flip-flops can be determined in a similar manner.
IEN may change as a result of the two instructions ION and IOF.
where p = D71T3, and B7, B6 are bits 7 and 6 o f IR, respectively. Moreover, at the end of the interrupt cycle IEN is cleared to 0.
I f we use a JK flip-flip for IEN, the control gate logic will b e a s shown in Fig.

## Slide 77
Control inputs for IEN.

## Slide 78: Control of Common Bus
Encoder for Bus Selection Circuit
Encoder for bus selection inputs.

## Slide 79
For example, to find the logic that makes x1 = I, we scan all register transfer statements in Table 5-6 and extract those statements that have AR as a source.
Therefore, the Boolean function for x1 is
The data output from memory are selected for the bus when x7 = 1 and S2S1S0 = 111. The gate logic that generates x7 must also be applied to the read input of memory. Therefore, the Boolean function for x7 is the same as the one derived previously for the read operation.
In a similar manner we can determine the gate logic for the other registers.

## Slide 80: Open Test-1
Q1.
The content of AC in the basic computer is hexadecimal A937 and the initial value of E is 1. Determine the contents of AC, E, PC, AR, and IR in hexadecimal after the execution of the CLA instruction. Repeat 11 more times, starting from each one of the register-reference instructions. The initial value of PC is hexadecimal 021 .

## Slide 81: Q2. Describe the Design of Accumulator Logic
Circuits associated with AC

## Slide 83
Gate structure for controlling the LD, INR, and CLR of AC.

## Slide 84: Adder and Logic Circuit
One stage of adder and logic circuit