## Slide 1
Computer Organization and Architecture
UNIT-1
Register Transfer and Micro-Operations: Register Transfer Language, Register Transfer, memory Transfers, Bus construction with Multiplexers, Arithmetic Micro-operations, Logic Micro-operations, Shift Micro-operations, Arithmetic Logic Shift Unit.
UNIT-2
Basic Computer Organization: Instruction codes, Computer Registers, Computer Instructions, Timing and Control, Instruction Cycle, Memory-Reference Instructions, Input- Output and Interrupt.
UNIT-5
Input-Output Organization: Peripheral Devices, Input-output Interface, Asynchronous Data Transfer, Priority Interrupt, Direct Memory Access (DMA), Input-Output Processor.
Pipeline and Parallel Processing: Parallel processing, Pipelining, Arithmetic pipeline,
Instruction pipeline.
UNIT-3
Central Processing Unit: General registers Organization, Stack Organization, Instruction Formats, Addressing Modes, Data Transfer and Manipulation, Program Control
UNIT-4
Computer Arithmetic: Introduction, Addition and Subtraction, Booth Multiplication Algorithm.
Memory Organization: Memory Hierarchy, Main Memory, Auxiliary memory, Associative Memory, Cache Memory, Virtual Memory.

## Slide 2: Course Outcomes
CO1: Understand the basic functional units of a computer system and its organization (L2)
CO2: Apply appropriate instructions for processing various types of computer operations (L3).
CO3: Apply various types of organizations on registers (L3).
CO4: Analyze memory hierarchy, I/O communication and pipelining (L4).
L1-remembering, L2-understanding, L3-applying, L4-analyzing, L5-evaluating, and L6-creating.

## Slide 3: UNIT-4 Computer Arithmetic: Introduction, Addition and Subtraction, Booth Multiplication Algorithm. Memory Organization: Memory Hierarchy, Main Memory, Auxiliary memory, Associative Memory, Cache Memory, Virtual Memory.

## Slide 4: Unit-4-Part-1
Computer Arithmetic
  Addition and Subtraction
  Multiplication Algorithms

## Slide 5: Introduction
Arithmetic instructions in digital computer manipulate data to produce re­sults necessary for the solution of computational problems.
The four basic arithmetic operations are addition, subtraction, multiplication and division.
An arithmetic processor is the part of a processor unit that executes arithmetic operations.
The data type assumed to reside in processor registers during the execution of an arithmetic instruction is specified in the definition of the instruction.
An arithmetic instruction may specify binary or decimal data, and in each case the data may be in fixed point or floating-point form.
Fixed-point numbers may represent integers or fractions.
Negative numbers may be in signed-magnitude or signed complement representation.
We consider addition, subtraction, multiplication, and division for the following types of data:
  1. Fixed-point binary data in signed-magnitude representation
  2. Fixed-point binary data in signed-2's complement representation
  3. Floating-point binary data
  4. Binary-coded decimal (BCD) data
Complements are used in digital computers for simplifying the subtraction operation and for logical manipulation

## Slide 6: Complements
  Subtraction of Unsigned Numbers
    1) M + (rn-N)
    2) M  N : Discard end carry, Result = M-N
    3) M  N : No end carry, Result = - r’s complement of (N-M)
      Decimal Example)
      72532(M) - 13250(N) = 59282
      72532
      + 86750 (10’s complement of 13250)
      1 59282
      Result = 59282
      Binary Example)
      1010100(X) - 1000011(Y) = 0010001
      1010100
      + 0111101 (2’s complement of 1000011)
      1 0010001
      Result = 0010001
(M-N), N0
      13250(M) - 72532(N) = -59282
      13250
      + 27468 (10’s complement of 72532)
      0 40718
      Result = -(10’s complement of 40718)
      = -(59281+1) = -59282
M  N
M  N
Discard End Carry
No End Carry
      1000011(X) - 1010100(Y) = -0010001
      1000011
      + 0101100 (2’s complement of 1010100)
      0 1101111
      Result = -(2’s complement of 1101111)
      = -(0010000+1) = -0010001
X  Y
X  Y

## Slide 7: 3. Fixed-Point Representation
Fixed-Point Representation
  Computers must represent everything with 1’s and 0’s, including the sign of a number and fixed/floating point number
  Binary/Decimal Point
    The position of the binary/decimal point is needed to represent fractions, integers, or mixed integer-fraction number
  Two ways of specifying the position of the binary point in a register
    1) Fixed Point : the binary point is always fixed in one position
      A binary point in the extreme left of the register(Fraction : 0.xxxxx)
      A binary point in the extreme right of the register(Integer : xxxxx.0)
        The binary point is not actually present, but the number stored in the register is treated as a fraction or as an integer
    2) Floating Point : the second register is used to designate the position of the
    binary point in the first register
  Integer Representation
    Signed-magnitude representation
    Signed-1’s complement representation
    Signed-2’s complement representation
*Numeric Data
1) Fixed Point
2) Floating Point
* 32.25
1) 0.25, 2) 32.0, 3) 32.25
+14 -14
0 0001110 1 0001110
0 0001110 1 1110001
0 0001110 1 1110010
* MSB for Sign
“0” is plus +
“1” is minus -
Most Common

## Slide 8: 3. Fixed-Point Representation
  Arithmetic Addition
    Addition Rules of Ordinary Arithmetic
      The signs are same : sign= common sign, result= add
      The signs are different : sign= larger sign, result= larger-smaller
    Addition Rules of the signed 2’s complement
      Add the two numbers including their sign bits
      Discard any carry out of the sign bit position
  Arithmetic Subtraction
    Subtraction is changed to an Addition
      (± A) - (+ B) = (± A) + (- B)
      (± A) - ( - B) = (± A) + (+ B)
  Overflow
    Two numbers of n digits each are added and the sum occupies n+1 digits
    n + 1 bit cannot be accommodated in a register with a standard length of n bits(many computer detect the occurrence of an overflow, and a corresponding F/F is set)
(-12) + (-13) = -25
(+12) + (+13) = +25
(+25) + (-37)
= 37 - 25 = -12
*Addition Exam)
+ 6 00000110 - 6 11111010
+ 13 00001101 + 13 00001101
+ 19 00010011 + 7 00000111
+ 6 00000110 - 6 11111010
- 13 11110011 - 13 11110011
- 7 11111001 - 19 11101101
* Subtraction Exam) (- 6) - ( - 13) = +7
11111010 - 11110011 = 11111010 + 2’s comp of 11110011
= 11111010 + 00001101
= 1 00000111 = +7
Discard End Carry

## Slide 9: Addition and Subtraction
Addition and Subtraction with Signed-Magnitude Data

## Slide 11
Hardware Algorithm

## Slide 12
Addition and Subtraction with Signed-2's
+ 33 is represented as 00100001 and - 33 as 1101 1 1 1 1 .
Note that 11011111 is the 2's complement of 00100001, and vice versa.
The addition of two numbers in signed-2's complement form consists of adding the numbers with the sign bits treated the same as the other bits of the number.
A carry-out of the sign-bit position is discarded.
The subtraction consists of first taking the 2' s complement of the subtrahend and then adding it to the minuend.

## Slide 14
Multiplication Algorithms
Multiplication of two fixed-point binary numbers in signed-magnitude representation
The process consists of looking at successive bits of the multiplier, least significant bit first.
If the multiplier bit is a 1, the multiplicand is copied down; otherwise, zeros are copied down.
The numbers copied down in successive lines are shifted one position to the left from the previous number.
Finally, the numbers are added and their sum forms the product.

## Slide 15: Hardware Implementation for Signed-Magnitude Data
When multiplication is implemented in a digital computer, it is convenient to change the process slightly.
First, instead of providing registers to store and add simultaneously as many binary numbers as there are bits in the multiplier, it is convenient to provide an adder for the summation of only two binary numbers and successively accumulate the partial products in a register.
Second, instead of shifting the multiplicand to the left, the partial product is shifted to the right, which results in leaving the partial product and the multiplicand in the required relative positions.
Third, when the corresponding bit of the multiplier is 0, there is no need to add all zeros to the partial product since it will not alter its value.

## Slide 16: Hardware Implementation for Signed-Magnitude Data
Number of bits in the multiplier
partial product
multiplier
Multiplicand
Initially, the multiplicand is in register B and the multiplier in Q.
The sum of A and B forms a partial product which is transferred to the EA register.
Both partial product and multiplier are shifted to the right.
This shift will be denoted by the statement shr EAQ to designate the right shift depicted in Fig. 10-5.
The least significant bit of A is shifted into the most significant position of Q, the bit from E is shifted into the most significant position of A, and 0 is shifted into E.
After the shift, one bit of the partial product is shifted into Q, pushing the multiplier bits one position to the right.
In this manner, the rightmost flip-flop in register Q, designated by Qn, will hold the bit of the multiplier, which must be inspected next.

## Slide 17
Hardware Algorithm
Initially, the multiplicand is in B and the multiplier in Q.
Their corresponding signs are in Bs, and Qs., respectively.
The signs are compared, and both A and Q are set to correspond to the sign of the product since a double-length product will be stored in registers A and Q.
Registers A and E are cleared and the sequence counter SC is set to a number equal to the number of bits of the multiplier.
We are assuming here that operands are transferred to registers from a memory unit that has words of n bits.
Since an operand must be stored with its sign, one bit of the word will be occupied by the sign and the magnitude will consist of n - 1 bits.
After the initialization, the low-order bit of the multiplier in Q, is tested.
If it is a 1, the multiplicand in B is added to the present partial product in A .
If it is a 0 , nothing is done. Register EAQ i s then shifted once to the right to form the new partial product.
The sequence counter is decremented by 1 and its new value checked.
If it is not equal to zero, the process is repeated and a new partial product is formed.
The process stops when SC = 0.
Note that the partial product formed in A is shifted into Q one bit at a time and eventually replaces the multiplier.
The final product is available in both A and Q, with A holding the most significant bits and Q holding the least significant bits.

## Slide 20
Booth Multiplication Algorithm
Booth algorithm gives a procedure for multiplying binary integers in signed-2's complement representation.
It operates on the fact that strings of 0's in the multiplier require no addition but just shifting, and a string of 1's in the multiplier from bit weight 2k to weight 2m can be treated as 2K+1 - 2m.
For example, the binary number 001 110 ( + 14) has a string of 1's from 23 to 21. (k = 3, m = 1).
The number can be represented as 2k+ l - 2m = 24 - 21 = 16 - 2 = 14.
Therefore, the multiplication M x 14, where M is the multiplicand and 14 the multiplier, can be done as M x 24 - M X 21
Thus the product can be obtained by shifting the binary multiplicand M four times to the left and subtracting M shifted left once.
Booth algorithm requires examination of the multiplier bits and shifting of the partial product. Prior to the shifting, the multiplicand may be added to the partial product, subtracted from the partial product, or left unchanged according to the following rules:
  The multiplicand is subtracted from the partial product upon encountering the first least significant 1 in a string of 1's in the multiplier.
  The multiplicand is added to the partial product upon encountering the first 0 (provided that there was a previous 1) in a string of 0's in the multiplier.
  The partial product does not change when the multiplier bit is identical to the previous multiplier bit.

## Slide 21
Hardware for Booth algorithm.

## Slide 22
Flowchart for Booth algorithm

## Slide 23
(-9)*(-13)=+117

## Slide 24
    BR = -5 = 1011, BR'+1 = 0101
    QR = -7 = 1001
OPERATION | AC | QR | Qn+1 | SC
 | 0000 | 1001 | 0 | 4
AC + BR’ + 1 | 0101 | 1001 | 0 | 
ASHR | 0010 | 1100 | 1 | 3
AC + QR | 1101 | 1100 | 1 | 
ASHR | 1110 | 1110 | 0 | 2
ASHR | 1111 | 0111 | 0 | 1
AC + BR’ + 1 | 0010 | 0011 | 1 | 0
Product is calculated as follows:
Product = AC QR Product = 0010 0011 = 35
Example : (-5)*(-7)=+35

## Slide 25
Checking the bits of the multiplier one at a time and forming partial products is a sequential operation that requires a sequence of add and shift microoperations.
The multiplication of two binary numbers can be done with one microoperation by means of a combinational circuit that forms the product bits all at once.
This is a fast way of multiplying two numbers since all it takes is the time for the signals to propagate through the gates that form the multiplication array.
However, an array multiplier requires a large number of gates, and for this reason it was not economical until the development of integrated circuits.
Array Multiplier; Fast approach

## Slide 26
Array Multiplier; Fast approach

## Slide 27
4 bit by 3 bit array muhiplier.