## Slide 1: Computer Networks

## Slide 2
Computer Network
A network is simply a collection of computers or other hardware devices that are connected, either physically or logically, using special hardware and software, to allow them to exchange information and cooperate.

## Slide 3
Networking
Networking is the term that describes the processes involved in designing, implementing, upgrading, managing and otherwise working with networks and network technologies.

## Slide 4
Advantages of Networking
Connectivity and Communication
Data/Resource Sharing
Reliability
Scalability
Entertainment
Data Security and Management
Performance Enhancement and Balancing
Backup

## Slide 5
Protocol
A protocol is a synonym for the rule.
In Computer Networks, communication occurs between entities in different systems.
Any two entities cannot simply send bitstreams to each other and expect to be understood.
The entities must need to agree on a protocol in order of occurrence of the communication.
A Protocol is a set of rules that mainly govern data communications. The protocol mainly defines what is communicated, how it is communicated, and when it is communicated.

## Slide 6
Standards
Standards provide guidelines to manufacturers, vendors, government agencies, and to other service providers in order to ensure the kind of interconnectivity that is necessary for today's marketplace and in international communications.
Some Standard Creation committees are :
  International Organization of Standardization(ISO)
  American National Standards Institute(ANSI)
  Electronic Industries Association(EIA)
  Institute of Electrical and Electronics Engineers(IEEE)

## Slide 7
Transmission Medium
Transmission medium is the means through which we send our data from one place to another.
Transmission Rate
Cost and Ease of Installation
Resistance to Environmental Conditions
Distances

## Slide 8
Line Configuration
A Network is a connection made through connection links between two or more devices.
There are two ways to connect the devices :
Point-to-Point connection
We can connect the two devices by means of a pair of wires or using a microwave or satellite link.
2. Multipoint connection
It is also called Multidrop configuration. In this connection two or more devices share a single link.

## Slide 9
Transmission Modes
Transmission mode refers to the mechanism of transferring of data between two devices connected over a network. It is also called Communication Mode.
These modes direct the direction of flow of information.
Three modes are:
Simplex Mode
Half duplex Mode
Full duplex Mode
Simplex Mode
Half duplex Mode
Full duplex Mode

## Slide 10
Computer Role in Networking
Client Server: Client computers normally request and receive information over the network from server
A peer-to-peer network is a network where the computers act as both workstations and servers.

## Slide 11
Network Classification
Local Area Networks
Metropolitan Area Networks
Wide Area Networks
Internet
Intranet
Wireless Networks

## Slide 12
Local Area Networks
A local area network (LAN) is a computer network covering a small geographic area, like a home, office, or group of buildings
Client
Client
Client
Client
Client
Client

## Slide 13
Metropolitan Area Networks
The communication infrastructures that have been developed in and around large cities

## Slide 14
Wide Area Networks
Wide Area Network (WAN) is a computer network that covers a broad area (i.e., any network whose communications links cross metropolitan, regional, or national boundaries).
Or, less formally,
a network that uses routers and public communications links

## Slide 15
Internet
The Internet is the global system of interconnected computer networks that use the Internet protocol suite (TCP/IP) to link devices worldwide.
It is a network of networks that consists of private, public, academic, business, and government networks of local to global scope, linked by a broad array of electronic, wireless, and optical networking technologies.

## Slide 16
Intranet
An intranet is a private network that is contained within an enterprise.
It may consist of many interlinked local area networks and use leased lines in the wide area network
An intranet uses TCP/IP, HTTP, and other Internet protocols and in general looks like a private version of the Internet.
With tunneling, companies can send private messages through the public network, using the public network with special encryption/decryption and other security safeguards to connect one part of their intranet to another.

## Slide 17
Wireless Networks
System Interconnection
Piconet
Wireless LAN
Wireless MAN
Wireless WAN
Mobile Networks

## Slide 18
Network Topology
A topology is a way of “laying out” the network. Topologies can be either physical or logical.
Physical topologies describe how the cables are run.
Logical topologies describe how the network messages travel
  Bus (can be both logical and physical)
  Ring (can be both logical and physical)
  Star (physical only)
  Mesh (can be both logical and physical)
  Hybrid

## Slide 19
Bus Topology
A bus is the simplest physical topology
It consists of a single cable that runs to every workstation
This topology uses the least amount of cabling, but also covers the shortest distance.
Each computer shares the same data and address path.
it is difficult to add a workstation
if any one of the cables breaks, the entire network is disrupted.

## Slide 20
Ring Topology
Each computer connects to two other computers, joining them in a circle creating a unidirectional path where messages move workstation to workstation.
The ring makes it difficult to add new computers

## Slide 21
Star Topology
A physical star topology branches each network device off a central device called a hub, making it very easy to add a new workstation.
Star topologies are easy to install. A cable is run from each workstation to the hub. The hub is placed in a central location in the office.

## Slide 22
Mesh Topology
In this physical topology, each device is connected to every other device.
If there are x computers, there will be
(x × (x–1)) ÷ 2 cables in the network.
The advantage you gain from it is its high fault tolerance.
With a logical mesh topology, however, there will always be a way of getting the data from source to destination

## Slide 23
Topologies
Topology | Advantages | Disadvantages
Bus | Cheap. Easy to install. | Difficult to reconfigure. Break in bus disables entire network.
Star | Cheap. Easy to install. Easy to reconfigure. Fault tolerant. | More expensive than bus.
Ring | Efficient. Easy to install. | Reconfiguration difficult. Very expensive.
Mesh | Simplest. Most fault tolerant. | Reconfiguration extremely difficult. Extremely expensive. Very complex.

## Slide 24
Hardware and Networks Peripherals (devices)
Network Interface Card (NIC)
Repeater
Bridge
Hub
Switch
Routers

## Slide 25
Network Interface Card (NIC)
NIC provides the physical interface between computer and cabling.
It prepares data, sends data, and controls the flow of data. It can also receive and translate data into bytes for the CPU to understand.
It is the NIC job to translate the data from the computer into signals that can flow easily along the cable
Each card will have a unique hardware address (EUI – Extended Unique Identifier).

## Slide 26
Repeaters
They allow a cabling system to extend beyond its maximum allowed length by amplifying the network voltages, so they travel farther.
The main disadvantage to repeaters is that they just amplify signals. These signals not only include the network signals, but any noise on the wire as well.
Analog Repeaters
Digital Repeaters
Wired Repeaters
Wireless Repeaters

## Slide 27
Bridges
They join similar topologies and are used to divide network segments.
Unlike repeaters, bridges can filter out noise
The main disadvantage to bridges is that they can't connect dissimilar network types or perform intelligent path selection.

## Slide 28
Hubs
They repeat any signal that comes in on one port and copy it to the other ports (a process that is also called broadcasting)
Passive hubs simply connect all ports together electrically and are usually not powered.
Active hubs use electronics to amplify and clean up the signal before it is broadcast to the other ports.

## Slide 29
Switch
Network switches are capable of inspecting data packets as they are received, determining the source and destination device of that packet, and forwarding it appropriately.
A device connected to a switch port has the full bandwidth all to itself.

## Slide 30
Routers
Routers are highly intelligent devices that connect multiple network types and determine the best path for sending data.
They are slower than bridges because they are more intelligent devices; as such, they analyze every packet, causing packet-forwarding delays. Because of this intelligence, they are also more expensive.