## Slide 1
Computer Networks

## Slide 2
Data Link Layer

## Slide 3
FRAMING
The data link layer needs to pack bits into frames, so that each frame is distinguishable from another.
Our postal system practices a type of framing. The simple act of inserting a letter into an envelope separates one piece of information from another; the envelope serves as the delimiter.
The data-link layer encapsulates packets from the network layer into frames. Then, on the hardware, it delivers each frame bit by bit.

## Slide 4
FRAMING
Frames separate a message from one source to a destination, by adding a sender address and a destination address.
A good design must make it easy for a receiver to find the start of new frames:
  Character/Byte count
  Flag bytes with byte stuffing
  Flag bits with bit stuffing
HEAD | PAYLOAD/DATA | TRAILER

## Slide 5
Character Count
This method is rarely used and is generally required to count total number of characters that are present in frame.
This is be done by using field in header.
Character count method ensures data link layer at the receiver or destination about total number of characters that follow, and about where the frame ends.
If character count is disturbed or distorted by an error occurring during transmission, then destination or receiver might lose synchronization. The destination or receiver might also be not able to locate or identify beginning of next frame.

## Slide 6
Character Count

## Slide 7
Character Count
6 | 1 | 2 | 3 | 4 | 5 | 4 | 5 | 6 | 1 | 3 | 5 | 2 | 6 | 3 | 7 | 3 | 5 | 7 | 8 | 9 | 4 | 6 | 8 | 9 | 0 | 2

## Slide 8
Character/Byte Stuffing
Character stuffing is also known as byte stuffing or character-oriented framing.
Byte stuffing is the process of adding 1 extra byte whenever there is a flag or escape character in the text.
Special byte that is basically known as ESC (Escape Character).

## Slide 9
Character/Byte Stuffing

## Slide 10
Character/Byte Stuffing
A | Flag | D | Flag | Esc | Flag | Esc | C | Flag | Flag

## Slide 11
Bit Stuffing
Bit stuffing is also known as bit-oriented framing or bit-oriented approach.
Flag in Bit Stuffing is 0111110
Bit stuffing is the process of adding one extra 0 whenever five consecutive 1s follow a 0 in the data, so that the receiver does not mistake the pattern 0111110 for a flag.

## Slide 12
Bit Stuffing

## Slide 13
Bit Stuffing
1101111101111111111011
1111111111111111111111
1101111100111110111110011
11111011111011111011111011

## Slide 14
Error Detection and
Correction

## Slide 15
Errors During Transmission
Data can be corrupted during transmission.
Some applications require that errors be detected and corrected.
Error Detections is a mechanism to find out if there is any error in the data or not.
  It does not necessary to mean that the exact location can be identified.
  It may or may not find the exact location of the error depending on the mechanism used.

## Slide 16
Types of Errors
In a single-bit error, only 1 bit in the data unit has changed.

## Slide 17
Types of Errors
A burst error means that 2 or more bits in the data unit have changed.

## Slide 18
Error Detection
To detect or correct errors, we need to send extra (redundant) bits with data.

## Slide 19
Error Control

## Slide 20
Parity Bit - Detection
ASCII – 7 bit code (hex 00 to 7F)
Could use “8th” bit for parity bit:
1011010X
Even parity: make total number of “1” bits is even
  10110100
Odd parity: make total number of “1” bits odd
  10110101
If a parity bit is added to a bit stream, then there is a basis to check for bit(s) being corrupted.

## Slide 21
Parity Bit – Single bit error Detection

## Slide 22
A cyclic redundancy check (CRC) is an error-detecting code commonly used in digital networks and storage devices to detect accidental changes to raw data.
Blocks of data entering these systems get a short check value attached, based on the remainder of a polynomial division of their contents.
Advantage
Very good performance in detecting single-bit errors, double errors, an odd number of errors and burst errors.
Easy to implement.
Cyclic Redundancy Check (CRC)

## Slide 23
Cyclic Redundancy Check (CRC)

## Slide 24
Cyclic Redundancy Check (CRC)
n : Number of bits in data to be sent from sender side.
k : Number of bits in the key obtained from generator polynomial.
Sender Side
The binary data is first augmented by adding k-1 zeros in the end of the data
Use modulo-2 binary division to divide binary data by the key and store remainder of division.
Append the remainder at the end of the data to form the encoded data and send the same

## Slide 25
Cyclic Redundancy Check (CRC)
n : Number of bits in data to be sent from sender side.
k : Number of bits in the key obtained from generator polynomial.
Receiver Side (Check if there are errors introduced in transmission) Perform modulo-2 division again and if the remainder is 0, then there are no errors.

## Slide 26
CRS- Sender Side
The division is done to have the most left bit 0, and is done from left to right like a regular division. The division is done until the quotient has as many bits as the dividend. The new codeword is the dataword extended by the remainder.
The divisor (generator) is agreed upon.

## Slide 27
CRS- Receiver Side

## Slide 28
Cyclic Redundancy Check (CRC)
The divisor in a cyclic code is normally called the generator polynomial
or simply the generator.
X4 + X2 +X
X3+1
10110
1001
X15+X12+X11+X8+X6+X4+X3+X
X4 + X2 +X

## Slide 29
Error Correction
Error Correction can be handled in two ways:
Backward error correction: Once the error is discovered, the receiver requests the sender to retransmit the entire data unit.
Forward error correction: In this case, the receiver uses the error-correcting code which automatically corrects the errors.
A single additional bit can detect the error, but cannot correct it.
For correcting the errors, one has to know the exact position of the error.

## Slide 30
Two-Dimensional Parity Bit
Parity check bits are calculated for each row, which is equivalent to a simple parity check bit.
Parity check bits are also calculated for all columns, then both are sent along with the data.
At the receiving end these are compared with the parity bits calculated on the received data.

## Slide 31
Hamming Code
Hamming code is a block code that is capable of correcting single-bit errors.
It was developed by R.W. Hamming for error correction.
In this coding method, the source encodes the message by inserting redundant bits within the message.
These redundant bits are extra bits that are generated and inserted at specific positions in the message itself to enable error detection and correction.
When the destination receives this message, it performs recalculations to detect errors and find the bit position that has error.

## Slide 32
Hamming Code - Sender
Step 1: Calculation of the number of redundant bits. (Find the K)
Select the Value of K such that
2K - 1 >= M + K
Where M is the number of Data Bits and K is the proposed number of Redundant Bits.
Example: For M = 8:
and K = 3: 23 – 1 = 7 < 8 + 3 (doesn’t work)
and K = 4: 24 – 1 = 15 > 8 + 4 (works!)
Therefore, we must choose K =4,
i.e., the minimum size of the syndrome is 4

## Slide 33
Hamming Code - Sender
Step 2 − Positioning the redundant bits.
The K redundant bits placed at bit positions of powers of 2, i.e. 1, 2, 4, 8, 16 etc.
They are referred in the rest of this text as K1 (at position 1), K2 (at position 2), K3 (at position 4), K4 (at position 8) and so on.
Write the bit positions starting from 1 in binary form (1, 10, 11, 100, etc).
All the bit positions that are a power of 2 are marked as parity bits (1, 2, 4, 8, etc).
All the other bit positions are marked as data bits.

## Slide 34
Hamming Code - Sender
Step 3 − Calculating the values of each redundant bit.
The redundant bits are parity bits either Even Parity or Odd Parity.
Each redundant bit, ki, is calculated as the parity, generally even parity, based upon its bit position. It covers all bit positions whose binary representation includes a 1 in the ith position except the position of ki. Thus −
k1 is the parity bit for all data bits in positions whose binary representation includes a 1 in the least significant position excluding 1 (3, 5, 7, 9, 11 and so on)
k2 is the parity bit for all data bits in positions whose binary representation includes a 1 in the position 2 from right except 2 (3, 6, 7, 10, 11 and so on)
k3 is the parity bit for all data bits in positions whose binary representation includes a 1 in the position 3 from right except 4 (5-7, 12-15, 20-23 and so on)

## Slide 35
Hamming Code - Sender
Step 3 − Calculating the values of each redundant bit. – Alternate Method
The redundant bits are parity bits either Even Parity or Odd Parity.
Each redundant bit, ki, is calculated as the parity, generally even parity, based upon its bit position.
For k1 (parity bit position 1) use check one and skip one method starting with 1st position (1,3, 5, 7, 9, 11 and so on)
For k2 (parity Bit position 2) use check two and skip two method starting with 2nd position (2,3, 6, 7, 10, 11 and so on)
For k3 (parity bit position 4) use check four and skip four (4-7, 12-15, 20-23 and so on)

## Slide 36
Hamming Code - Receiver
Once the receiver gets an incoming message, it performs recalculations to detect errors and correct them.
The steps for recalculation are −
Step 1 − Calculation of the number of redundant bits.
Step 2 − Positioning the redundant bits.
Step 3 − Parity checking.
Step 4 − Error detection and correction

## Slide 37
Hamming Code - Receiver
Step 4 − Error detection and correction
The decimal equivalent of the parity bits binary values is calculated.
If it is 0, there is no error.
Otherwise, the decimal value gives the bit position which has error.
For example, if c1c2c3c4 = 1001, it implies that the data bit at position 9, decimal equivalent of 1001, has error.
The bit is flipped to get the correct message.