## Slide 1: Medium Access Control (MAC)

## Slide 2
Broadcast Channels
Broad cast channels are also called as Multiple channels or Random- access channels
In any broadcast network, the key issue is how to determine who gets to use the channel when there is competition for it
The task is done with the help of sub layer of data link layer called MAC (Medium Access Layer)
Static Channel Allocation in LANs and MANs
Dynamic Channel Allocation in LANs and MANs

## Slide 3
Static Allocation Channel
Disadvantages:
  Not efficient for large or more users
  Random division of the channel into N-regions, but if the users (n) are less than the regions (N), then the spectrum will be wasted and vice-versa
  If a user is not using a channel allocated, then it becomes unused, even for those who require
Traditionally Frequency Division Multiplexing (FDM) was used
A frequency band is given to the user all the time

## Slide 4: MAC Protocols
single shared broadcast channel
two or more simultaneous transmissions by nodes: interference
  collision if node receives two or more signals at the same time
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit
communication about channel sharing must use channel itself!
  no out-of-band channel for coordination
Multiple Access Protocol

## Slide 5
PURE ALOHA
The original ALOHA protocol is called pure ALOHA.
This is a simple, but elegant protocol
Each station sends a frame whenever it has a frame to send.
Since there is only one channel to share, there is the possibility of collision between frames from different stations
The ALOHA protocol relies on acknowledgments from the receiver.
When a station sends a frame, it expects the receiver to send an acknowledgment.
If the acknowledgment does not arrive after a time-out period, the station assumes that the frame (or the acknowledgment) has been destroyed and resends the frame.

## Slide 6
PURE ALOHA

## Slide 7
Procedure pure ALOHA

## Slide 8: Performance Pure Aloha
vulnerable time = 2 x Tfr
The throughput for pure ALOHA is
S =G x e-2G
where, G is the average no of frames generated by system during one frame transmission time and S is the average no of successful transmissions
G=1/2
Maximum Efficiency of Pure Aloha
(η) = 18.4%

## Slide 9: SLOTTED ALOHA
To improve the efficiency of pure ALOHA
Divide time into slots of Tfr’s and force the station to send the frame only at the beginning of the time slot

## Slide 10: SLOTTED ALOHA
vulnerable time = Tfr
The throughput for slotted ALOHA is S =: G x e-G.
Collision occurs if two stations try to send at the beginning of the same slot
Substituting G = 1
Maximum Efficiency of Slotted Aloha (η) = 36.8%

## Slide 11: Differences Between Pure ALOHA and Slotted ALOHA
Transmission
  Immediately, Starting of Time Slot
Timing
  Random Time, Beginning of Time Slot
Synchronization
Mode of Transfer
  Continues, Discrete
Collision
Efficiency

## Slide 12: Carrier Sense Multiple Access
The chance of collision can be reduced if a station senses the medium before trying to use it.
Carrier sense multiple access (CSMA) requires that each station first listen to the medium before sending.
In other words, CSMA is based on the principle "sense before transmit" or "listen before talk.”
CSMA can reduce the possibility of collision, but it cannot eliminate it.
The possibility of collision still exists because of propagation delay; when a station sends a frame, it still takes time (although very short) for the first bit to reach every station and for every station to sense it.

## Slide 13: Carrier Sense Multiple Access
At time t1 station B senses the medium and finds it idle, so it sends a frame. At time t2
(t2> t1) station C senses the medium and finds it idle because, at this time, the first bits from station B have not reached station C. Station C also sends a frame. The two signals collide and both frames are destroyed.
CSMA vulnerable time = Tp
This is the time needed for a signal to propagate from one end of the medium to the other. When a station sends a frame, and any other station tries to send a frame during this time, a collision will result.

## Slide 14: Carrier Sense Multiple Access
What should a station do if the channel is busy?
What should a station do if the channel is idle?
1-Persistent
Non persistent
P-persistent
3-Options
1 - Persistent
The 1-persistent method is simple and straightforward. In this method, after the station finds the line idle, it sends its frame immediately (with probability 1).
This method has the highest chance of collision because two or more stations may find the line idle and send their frames immediately.

## Slide 15: Carrier Sense Multiple Access
non - Persistent
A station that has a frame to send senses the line. If the line is idle, it sends immediately.
If the line is Busy, it waits a random amount of time and then senses the line again.
P-persistent
With probability p, the station sends its frame.
With probability q = 1 - p, the station waits for the beginning of the next time slot and checks the line again.
    a. If the line is idle, it goes to step 1.
    b. If the line is busy, it acts as though a collision has occurred and uses the
    backoff procedure.

## Slide 16: Comparison

## Slide 17: Carrier Sense Multiple Access/Collision Detection
Collision Detection
Collision can be detected based on the level of energy in a channel.
When there is no collision, the station receives one signal: its own signal.
When there is a collision, the station receives two signals: its own signal and the signal transmitted by a second station.
A station that has a frame to send or is sending a frame needs to monitor the energy level to determine if the channel is idle, busy, or in collision mode
Zero Level  At the zero level, the channel is idle.
Normal Level At the normal level, a station has successfully captured the channel and is sending its frame.
Abnormal Level At the abnormal level, there is a collision and the level of the energy is twice the normal level

## Slide 18: Carrier Sense Multiple Access/Collision Detection
In this method, a station monitors the medium after it sends a frame to see if the transmission was successful.
If so, the station is finished. If, however, there is a collision, the station stops sending the remaining bits and the frame is sent again.

## Slide 19: Carrier Sense Multiple Access/Collision Detection
Minimum Frame Size
For CSMA/CD to work, we need a restriction on the frame size.
Before sending the last bit of the frame, the sending station must detect a collision, if any, and abort the transmission.
This is so because the station, once the entire frame is sent, does not keep a copy of the frame and does not monitor the line for collision detection.
If the two stations involved in a collision are the maximum distance apart, the signal from the first takes time Tp to reach the second and the effect of the collision takes another time Tp to reach the first. So the requirement is that the first station must still be transmitting after 2Tp .

## Slide 20
CSMA/CD

## Slide 21: Collision Free Protocols/Controlled Access
Almost collisions can be avoided in CSMA/CD.
They can still occur during the contention period.
The collision during the contention period adversely affects the system performance, this happens when the cable is long and length of packet are short.
This problem becomes serious as fiber optics network come into use.
some protocols that resolve the collision during the contention period.
1. Bit-map Protocol/Reservation Protocol.
2. Binary Countdown

## Slide 22: Bit Map Protocol
In bitmap protocol method, each contention period consists of exactly N slots.
if any station has to send frame, then it transmits a 1 bit in the respective slot.
For example if station 2 has a frame to send, it transmits a 1 bit during the second slot.
In general, station j may announce that it has a frame to send by inserting a 1 bit into slot j.
After all N slots have passed by, each station has complete knowledge of which stations wish to transmit.

## Slide 23: Bit Map Protocol
When station 1 has a slot in the window and after its chance, if it requires to transmit once again in the same slot, then station 1 has to wait for the next contention period.
Protocols like this in which the desire to transmit is broadcast before the actual transmission are called reservation protocols because they reserve channel ownership in advance and prevent collisions.
PERFORMANCE:
  Works fine for high-numbered stations
  At low load, the bit map will be simply repeated.

## Slide 24: Binary Count Down
The disadvantage of Bit Map protocol is that a station can send only one bit hence it suffers from scalability issue.
In binary countdown, binary station addresses are used.
A station wanting to use the channel broadcast its address as binary bit string starting with the high order bit.
All addresses are assumed of the same length.
In this method, different station addresses are ORed together who decide the priority of transmitting.

## Slide 25: Binary Count Down Example
Consider stations 1,9,11,12 wants to transmits
first consider binary address of those stations 0001, 1001, 1100, 1011
consider MSB bits of all stations are 0,1,1,1 if ORed then get 1
So 0001 has no chance to transmit
Again next bit after MSB of remaining three stations as 1,1,0 if Ored then 1
So 1100 that is station 12 got chance to transmit

## Slide 26: Carrier Sense Multiple Access/Collision Avoidance
Why CSMA/CD Fails
Collision detection: CSMA/CD relies on detecting collisions while transmitting. However, in wireless networks, it's difficult to detect collisions due to signal attenuation and interference.
Half-duplex transmission: Wireless devices often operate in half-duplex mode, making it challenging to detect collisions while transmitting.
Limitations in Wireless Mediums
Hidden Node Problem
Exposed Node Problem
Signal Attenuation
Interference

## Slide 27: Carrier Sense Multiple Access/Collision Avoidance
Hidden Node Problem
For A and C, The medium appears to be free, the carrier sense fails.
Thus, C also starts sending causing a collision at B.
But now A cannot detect this collision and continues with its transmission. A is hidden for C and vice versa
A
B
C

## Slide 28: Carrier Sense Multiple Access/Collision Avoidance
Exposed Terminal Problem
A is outside the interference range of B waiting is not necessary Causing a ‘collision’ at B does not matter because the collision is too weak to propagate to A.
In this situation, C is exposed to B
A
B
C

## Slide 29: Carrier Sense Multiple Access/Collision Avoidance
Carrier Sense
Collision Avoidance
Request to Send
  Sender Node, Receiver Node, Time to Send
Clear to Send
  Sender Node, Receiver Node, Time to Send
A Node receiving RTS and CTS packet will restrain from transmission until the Time is elapsed

## Slide 30: Carrier Sense Multiple Access/Collision Avoidance
Solving Hidden Terminal Problem
After receiving a CTS, C is not allowed to send anything for the duration indicated in the CTS toward B.
Thus, a collision cannot occur at B during data transmission, and the hidden terminal problem is solved.
A
B
C
RTS
CTS
CTS

## Slide 31: Carrier Sense Multiple Access/Collision Avoidance
Solving Exposed Terminal Problem
C does not receive CTS and concludes that A is outside the detection range. Thus, C can start its transmission, assuming not to cause a collision at A.
The problem with exposed terminals is solved without fixed access patterns or a base station.
RTS
CTS
RTS

## Slide 32: Polling
A polling MAC protocol is a Media Access Control (MAC) protocol where a centralized node (or coordinator) polls other nodes to permit them to transmit data.
Polling: The central node sends a poll request to one or more designated nodes.
Data Transmission: The polled nodes, once they receive permission, transmit their data packets.
Scheduling: The central node manages the polling sequence, determining which node gets to transmit next, often through a pre-defined schedule or a dynamic process.

## Slide 33: Polling
Key Features and Benefits
Collision Avoidance
Guaranteed Access
Efficiency and Throughput
Predictable Performance

## Slide 34: Wireless/Mobile Technologies
Technology | Frequency Range | Max Data Rate | Typical Coverage Range
GSM (2G) | 850 / 900 / 1800 / 1900 MHz | ~14.4 kbps (GSM) Up to 384 kbps (EDGE) | 2 – 35 km (up to 70 km rural)
LTE (4G) | 700 MHz – 2600 MHz | 100 Mbps – 1 Gbps (LTE-Advanced) | 2 – 15 km
5G (Low Band) | <1 GHz | 100 Mbps – 1 Gbps | 10 – 20 km
5G (Mid Band) | 2 – 6 GHz | 1 – 3 Gbps | 1 – 5 km
5G (High Band) | 24 – 52 GHz | 10 Gbps+ | 100 – 500 meters
Wi-Fi (802.11n/ac/ax) | 2.4 GHz & 5 GHz (Wi-Fi 6 also uses 6 GHz) | Up to 600 Mbps (Wi-Fi 4) Up to 9.6 Gbps (Wi-Fi 6) | 10 – 30 meters
Bluetooth (5.0) | 2.4 GHz (ISM band) | Up to 2 Mbps (Bluetooth 5 LE) | 10 – 100 meters

## Slide 35: Space Division Multiple Access
Assigning an optimal base station to a mobile phone user.
SDMA is never used in isolation
SDMA is always in combination with one or more other schemes.
The basis for the SDMA algorithm is formed by cells and sectorized antennas which constitute the infrastructure implementing space division multiplexing (SDM)

## Slide 36: Frequency Division Multiple Access
The total available bandwidth is divided into several smaller, dedicated frequency bands.
Small, unused gaps called "guard bands" are placed between adjacent frequency channels to prevent interference between them.
Each user or communication link is assigned one of these dedicated frequency bands.
Each user can transmit and receive independently on their assigned frequency band without waiting for others.
Fixed Allocation or Dynamic Allocation

## Slide 37: Frequency Division Duplex

## Slide 38: Frequency Division Multiple Access
Dynamic FDMA
A dynamic FDMA system divides the total available bandwidth into smaller frequency sub-channels.
Instead of a fixed assignment, these sub-channels are dynamically allocated to different users based on their current data demands and the quality of the frequency channels.
Frequency Hopping
Change frequencies according to a certain pattern
Sender and receiver have to agree on a hopping pattern
  Slow and Fast Frequency Hopping

## Slide 39: Frequency Division Multiple Access
  Slow Frequency Hopping

## Slide 40: Frequency Division Multiple Access
Fast Frequency Hopping
Rapid Frequency Switching
Pseudorandom Sequence
Bluetooth devices use FHSS at 1600 hops per second.

## Slide 41: Time Division Multiple Access
Allocate certain time slots for communication
Fixed TDMA
Dynamic TDMA

## Slide 42: Time Division Multiple Access
Dynamic TDMA

## Slide 43: Time Division Multiple Access
Dynamic TDMA

## Slide 44: Code Division Multiple Access
Shared medium without interference
Properties of Good Code
Orthogonal
  Two vectors are called orthogonal if their inner product is 0
  The case for the two vectors (2, 5, 0)*(0, 0, 17) = 0 + 0 + 0 = 0.
  But also vectors like (3, —2, 4) and (—2, 3,3) are orthogonal: (3, —2, 4)*(_2, 3, 3) = —6 — 6 + 12 = 0.
Autocorrelation
  The inner product with itself is large
  The Barker code (+1, —1, +1, +1, —1, +1, +1, +1, —1, —1,—1), for example, has a good autocorrelation, i.e., the inner product with itself is large, the result is 11.

## Slide 45: Code Division Multiple Access - Example
Step 1
Two senders, A and B, want to send data. CDMA assigns the following key sequences: key Ak = 010011, key Bk = 110101.
Sender wants to send the bit Ad = 1, sender B sends Bd = 0.
To illustrate this example, let us assume that we code a, binary 0 as —1, a binary 1 as +1.
We can then apply the standard addition and multiplication rules.

## Slide 46: Code Division Multiple Access - Example
Step 2
Both senders spread their signal using their key as chipping sequence.
In reality, parts of- a much longer chipping sequence are applied to single bits for spreading.
Sender A then sends the signal
A = Ad*Ak = +1*( -1, +1, —1, —1, +1, +1) = (—1, +1, —1, —1, +1, +1).
Sender B does the same with its data to spread the signal with the code
B = Bd*Bk = -1*(+1, +1, —1, +1, —1, +1) = (—1, —1, +1, —1, +1, —1).

## Slide 47: Code Division Multiple Access - Example
Step 3
Both signals are then transmitted at the same time using the same frequency, thus, the sign in space.
Neglecting interference from senders and environmental noise for this simple example, and assuming that the signals have the same strength at the receiver, the following signal C is received at a receiver:
C = As + Bs = (—2, 0, 0, —2, +2, 0).

## Slide 48: Code Division Multiple Access - Example
Step 4: Receiver
The receiver now wants to receive data from
Sender A and, therefore, tunes in to the code of A, i.e., applies A’s code for despreading:
C*Ak = (—2, 0, 0, —2, + 2, 0)*(-1, +1, —1, —1, +1, +1)
= 2 +.0 + 0 + 2 + 2 + 0 = 6.
As the result is much larger than 0, the receiver detects a binary 1.
Tuning in to sender B, i.e. applying B’s code gives
C*Bk = (—2, 0, 0, —2, ÷2,0)*(+1, +1, —1, +1, —1, +1)
= —2 +0+0—2—2+0=—6
The result is negative thus the values is Binary 0

## Slide 49: Code Division Multiple Access - Example
Sender A System

## Slide 50: Code Division Multiple Access - Example
Sender B System

## Slide 51: Code Division Multiple Access - Example
Reconstruction of A’s Data

## Slide 52: Code Division Multiple Access - Example
Reconstruction of B’s Data

## Slide 53: Code Division Multiple Access - Example
Using Wrong Key