## Slide 1: IP Addressing

## Slide 2: IPv4 ADDRESSES
An IPv4 address is a 32-bit address that uniquely and universally defines the connection of a device (for example, a computer or a router) to the Internet.

## Slide 3: IPv4 Address
The IPv4 addresses are unique and universal.
An IPv4 address is 32 bits long.
  The address space of IPv4 is 232 (4,294,967,296)
  Notation.
    Binary notation
    Dotted-decimal notation

## Slide 4
Change the following IPv4 addresses from binary notation to dotted-decimal notation.
Example
Solution
We replace each group of 8 bits with its equivalent decimal number and add dots for separation.

## Slide 5
Change the following IPv4 addresses from dotted-decimal notation to binary notation.
Example
Solution
We replace each decimal number with its binary equivalent (see Appendix B).

## Slide 6: IPv4 Address
RULES:
1. There must be no leading zero
2. There can be no more than four bytes in IPV4 address
3. Each number must be less than or equal to 255
4. A mixture of binary and decimal notation is not allowed.

## Slide 7
Find the error, if any, in the following IPv4 addresses.
Example 19.3
Solution
a. There must be no leading zero (045).
b. There can be no more than four numbers.
c. Each number needs to be less than or equal to 255.
d. A mixture of binary notation and dotted-decimal notation is not allowed.

## Slide 8: Classful Addressing
In classful addressing, the address space is divided into five classes: A, B, C, D, and E.

## Slide 9: Classful Addressing
Special IP addresses.

## Slide 10
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Example 19.4
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 11: Classes and Blocks
The classful addressing wastes a large part of the address space.
  Class A:
  Class B:
  Class C:
  Class D:

## Slide 12: Find NetID and Host ID
Consists of Net ID and Host ID.
Mask
  32-bit number of contiguous 1’s followed by contiguous 0’s.
  To help to find the net ID and the host ID.

## Slide 13: Subnet and SuperNet
Subnetting
  Divide a large address block into smaller sub-groups.
  Use of flexible net mask.
Supernetting
  Exhausted class A and B address space
  Huge demand for class B address space
  To combine several contiguous address spaces into a larger single address space

## Slide 14: Subnetting
Subnetting
  Divide a large address block into smaller sub-groups.
  Use of flexible net mask.
A class B network subnetted into 64 subnets.

## Slide 15: Comparison of a default mask and a subnet mask
#of Subnetworks = 23 (always a power of 2)
#of Addresses/subnet(Hosts) = 213 (always a power of 2)
Special Addresses:
  Hostid 0 : Subnetwork Address
  HostId all 1’s: Limited Broadcast inside subnetwork

## Slide 16: A network with two levels of hierarchy (not subnetted)
All hosts in such a large network must be laid out as ONE physical network
May not always be feasible (due to geographic constraints)

## Slide 17: A network with three levels of hierarchy (subnetted)
3-step delivery: site, subnet, host.

## Slide 18: Finding the Subnet Address
Given an IP address, we can find the subnet address the same way we found the network address in the previous chapter.
We apply the mask to the address. We can do this in two ways: straight or short-cut.

## Slide 19: Default mask and subnet mask
Subnetwork

## Slide 20
Straight Method
In the straight method, we use binary notation for both the address and the mask and then apply the AND operation to find the subnet address.
Example 1
What is the subnetwork address of the destination address is 200.45.34.56 and the subnet mask is 255.255.240.0?
11001000 | 00101101 | 00100010 | 00111000
11111111 | 11111111 | 11110000 | 00000000
11001000 | 00101101 | 00100000 | 00000000
The subnetwork address is 200.45.32.0.

## Slide 21
Short-Cut Method
** If the byte in the mask is 255, copy the byte in the address.
** If the byte in the mask is 0, replace the byte in the address with 0.
** If the byte in the mask is neither 255 nor 0, we write the mask and the address in binary and apply the AND operation.

## Slide 22
Designing Subnets
The number of subnets N must be a power of 2.
1. Find the Subnet Mask
  1-Bits: 1’s from default mask + Log2 N
  0-Bits: The remaining bits (of the 32-bit IP address)
2. Number of Addresses in Each Subnet = 2 #of 0-Bits.
3. Range of Addresses in each Subnet.

## Slide 23: Example 3
A company is granted the site address 201.70.64.0 (class C). The company needs six subnets. Design the subnets.
The number of 1s in the default mask is 24 (class C).
The company needs six subnets. This number 6 is not a power of 2. The next number that is a power of 2 is 8 (23). We need 3 more 1s in the subnet mask. The total number of 1s in the subnet mask is 27 (24 + 3).
The total number of 0s is 5 (32 - 27). The mask is
11111111 11111111 11111111 11100000 or 255.255.255.224
The number of subnets is 8.
The number of addresses in each subnet is 25 (5 is the number of 0s) or 32.

## Slide 24: Example 4
The company needs 1000 subnets. This number is not a power of 2. The next number that is a power of 2 is 1024 (210). We need 10 more 1s in the subnet mask.
The total number of 1s in the subnet mask is 26 (16 + 10).
The total number of 0s is 6 (32 - 26). The mask is
11111111 11111111 11111111 11000000 or 255.255.255.192
The number of subnets is 1024.
The number of addresses in each subnet is 26 (6 is the number of 0s) or 64.
A company is granted the site address 181.56.0.0 (class B). The company needs 1000 subnets. Design the subnets.

## Slide 25: Variable-length subnetting
Granted a Class C address
Needs 5 subnets of 60, 60, 60, 30, 30 hosts, respectively
2-bit Subnet mask is too small
3-bit Subnet mask → #hosts too small

## Slide 26: A supernetwork
Combine several Class C blocks to create a larger superblock
#of blocks N is a power of 2
Blocks are contiguous
Byte 3 of starting address is divisible by N.

## Slide 27
Comparison of subnet, default, and supernet masks
In supernetting, we need the first address of the supernet and the supernet mask to define the range of addresses.

## Slide 28: Example 5
A company needs 600 addresses. Which of the following set of class C blocks can be used to form a supernet for this company?
198.47.32.0 198.47.33.0 198.47.34.0
198.47.32.0 198.47.42.0 198.47.52.0 198.47.62.0
198.47.31.0 198.47.32.0 198.47.33.0 198.47.52.0
198.47.32.0 198.47.33.0 198.47.34.0 198.47.35.0

## Slide 29: We need to make a supernetwork out of 16 class C blocks. What is the supernet mask?
Example 6
Solution
We need 16 blocks. For 16 blocks we need to change four 1s to 0s in the default mask. So the mask is
11111111
11111111 11110000 00000000
or
255.255.240.0

## Slide 30: Example
A supernet has a first address of 205.16.32.0 and a supernet mask of 255.255.248.0. A router receives three packets with the following destination addresses:
205.16.37.44
205.16.42.56
205.17.33.76
Which packet belongs to the supernet?
We apply the supernet mask to see if we can find the beginning address.
205.16.37.44 | AND | 255.255.248.0 |  | 205.16.32.0
205.16.42.56 | AND | 255.255.248.0 |  | 205.16.40.0
205.17.33.76 | AND | 255.255.248.0 |  | 205.17.32.0
Only the first address belongs to this supernet.

## Slide 31: Example 8
A supernet has a first address of 205.16.32.0 and a supernet mask of 255.255.248.0. How many blocks are in this supernet and what is the range of addresses?
Solution
The supernet has 21 1s. The default mask has 24 1s.
Since the difference is 3, there are 23 or 8 blocks in this supernet.
The blocks are 205.16.32.0 to 205.16.39.0.
The first address is 205.16.32.0. The last address is 205.16.39.255.

## Slide 32: Classless Addressing
  The addresses in a block must be contiguous.
  The number of addresses in a block must be a power of 2.
  The first address must be evenly divisible by the number of address.
Mask
  Consists of n consecutive 1’s followed by zeros.
  n can be any number b/w 0 and 32.
Tips:
  In IPv4 addressing, a block of addresses can be defined as x.y.z.t /n, in which x.y.z.t defines one of the addresses and the /n defines the mask.
  The first address in the block can be found by setting the rightmost 32 − n bits to 0s.
  The last address in the block can be found by setting the rightmost 32 − n bits to 1s.
  The number of addresses in the block can be found by using the formula 232−n.

## Slide 33
Figure 19.3 shows a block of addresses, in both binary and dotted-decimal notation, granted to a small business that needs 16 addresses.
Example

## Slide 34
A block of addresses is granted to a small organization. We know that one of the addresses is 205.16.37.39/28. What is the first address in the block?
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32−28 rightmost bits to 0, we get
11001101 00010000 00100101 0010000
or 205.16.37.32.
This is actually the block shown in Figure 19.3.
Example 19.6

## Slide 35
Find the last address for the block in Example 19.6.
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32 − 28 rightmost bits to 1, we get
11001101 00010000 00100101 00101111
or
205.16.37.47
This is actually the block shown in Figure 19.3.
Example 19.7

## Slide 36
Find the number of addresses in Example 19.6.
Example 19.8
Solution
The value of n is 28, which means that number of addresses is 2 32−28 or 16.

## Slide 37
Another way to find the first address, the last address, and the number of addresses is to represent the mask as a 32-bit binary (or 8-digit hexadecimal) number. This is particularly useful when we are writing a program to find these pieces of information. In 205.16.37.39/28 the /28 can be represented as
11111111 11111111 11111111 11110000
(twenty-eight 1s and four 0s).
Find
a. The first address
b. The last address
c. The number of addresses.
Example 19.9

## Slide 38
Solution
a. The first address can be found by ANDing the given addresses with the mask. ANDing here is done bit by bit. The result of ANDing 2 bits is 1 if both bits are 1s; the result is 0 otherwise.
Example 19.9 (continued)

## Slide 39
b. The last address can be found by ORing the given addresses with the complement of the mask. Oring here is done bit by bit. The result of ORing 2 bits is 0 if both bits are 0s; the result is 1 otherwise. The complement of a number is found by changing each 1 to 0 and each 0 to 1.
Example 19.9 (continued)

## Slide 40
c. The number of addresses can be found by complementing the mask, interpreting it as a decimal number, and adding 1 to it.
Example 19.9 (continued)

## Slide 41
An ISP is granted a block of addresses starting with 190.100.0.0/16 (65,536 addresses). The ISP needs to distribute these addresses to three groups of customers as follows:
a. The first group has 64 customers; each needs 256 addresses.
b. The second group has 128 customers; each needs 128 addresses.
c. The third group has 128 customers; each needs 64 addresses.
Design the subblocks and find out how many addresses are still available after these allocations.
Example 19.10

## Slide 42: Special Addresses
Network address
  The first address in a block is normally not assigned to any device; it is used as the network address that represents the organization to the rest of the world.
Broadcast address
  The last address in a block is used for broadcasting to all devices under the network.

## Slide 43: Network Address Translation (NAT)
To access the Internet, one public IP address is needed, but we can use a private IP address in our private network.
The idea of NAT is to allow multiple devices to access the Internet through a single public address.
To achieve this, the translation of a private IP address to a public IP address is required.
Network Address Translation (NAT) is a process in which one or more local IP address is translated into one or more Global IP address and vice versa in order to provide Internet access to the local hosts.

## Slide 44: Network Address Translation (NAT)
Benefits
  Use of a single IP address among many devices in a network
  Use of a dynamic IP address for home user for sharing
Private Addresses

## Slide 45
Figure 19.10 A NAT implementation

## Slide 46
Figure 19.11 Addresses in a NAT

## Slide 47
Figure 19.12 NAT address translation

## Slide 48
Table 19.4 Five-column translation table

## Slide 49
Figure 19.13 An ISP and NAT

## Slide 50: IPv6 ADDRESSES
Despite all short-term solutions, address depletion is still a long-term problem for the Internet. This and other problems in the IP protocol itself have been the motivation for IPv6.

## Slide 51: IPv6 Address
An IPv6 address is 128 bits long (16-byte).
Hexadecimal Colon Notation

## Slide 52
Figure 19.15 Abbreviated IPv6 addresses

## Slide 53
Expand the address 0:15::1:12:1213 to its original.
Example 19.11
Solution
We first need to align the left side of the double colon to the left of the original pattern and the right side of the double colon to the right of the original pattern to find how many 0s we need to replace the double colon.
This means that the original address is.

## Slide 54: IPV6

## Slide 55: Global Unicast IPV6

## Slide 56: IPv6 link-local
IPv6 link-local is a special type of unicast address that is auto-configured on any interface using a combination of the link-local prefix FE80::/10 (first 10 bits equal to 1111 1110 10) and the MAC address of the interface.

## Slide 57: Multicast address in IPv6
For a group of hosts
To deliver packets to each member

## Slide 58
Figure 19.18 Reserved addresses in IPv6

## Slide 59: Local addresses in IPv6
to use IPv6 without connecting to the global Internet.