## Slide 1: Network Layer

## Slide 2: Introduction
Routers forward IP datagrams from one router to another on the path from source towards destination
Routing protocols
  To decide on routes to be taken
Routers must have idea of topology of internet in order to pick best route to take
  Decisions are based on some least cost criteria
  May depend on the current conditions

## Slide 3: A Sample Configuration of Routers and Networks
Link costs are at the output of the links
There is cost of putting data to the network
There is no cost of getting data from the network
  For example, the cost of the path X-A-F-Y is 1+1+4=6

## Slide 4: Routing Table
One routing table is needed for each router
One entry for each destination network
  Not for each destination host
  Once datagram reaches router attached to destination network, that router can deliver to host
Each entry shows next node on the route to destination
  Not whole route
Routing tables may also exist in hosts
  If multiple routers attached to network, host needs table saying which to use
  If the attached network has single router, then routing table is not needed.

## Slide 5: Fixed Routing
Single permanent route configured for each source-destination pair
  Routes are fixed
  May change when topology changes (not so often)
    No dynamic updates

## Slide 6: Adaptive Routing
As conditions on internetwork change, routes may change
  Failure
    of routers or networks
  Congestion
    If a particular section of the network is heavily congested, it is better not to use that part and change the route

## Slide 7: Adaptive Routing - Challenges
Complex routing decisions
  Router processing increases
Depends on information collected in one place but used in another
  More information exchange improves routing decisions, but increases overhead
May react too fast
  causing congestion through oscillation (fluttering)
May react too slow
  By the time routing decision changes, the network conditions may be much more different
Looping
  Packet forwarded by a router eventually returns to the same router

## Slide 8: Flooding
No network info required
Packet sent by node to every neighbour
Incoming packets retransmitted on every link except incoming link
Eventually a number of copies will arrive at destination
Each packet is uniquely numbered so duplicates can be discarded at destination

## Slide 9: Flooding Example

## Slide 10: Flooding- Improvements
Precautions against unlimited grow in circulation
  Nodes can remember packets already forwarded to keep network load within allowed limits
    called "Restricted Flooding"
  Include a hop count in packets.
    Set to a maximum value
    Decrease one at each hop
    Discard when 0

## Slide 11: Properties of Flooding
All possible routes are tried
  very robust
  can be used for emergency messaging
At least one packet will use minimum hop count route
  Can be used once to set up a route
All nodes are visited
  Useful to distribute information (e.g. routing info)

## Slide 12: Random Routing
Node selects one outgoing path for retransmission of incoming packet
Selection is at random
  equally likely
    all outgoing links are utilized equally in the long-run
  can select outgoing path based on a probability
    e.g. probability based on data rate
      good traffic distribution
No network info needed
Route is typically neither least cost nor minimum hop

## Slide 13: Optimality principle
If router j is on the optimal path from i to k, then the optimal path from j to k also falls along the same route.
i
k
(j)
(j)
(j)

## Slide 14: Sink Trees
The set of optimal routes to a particular node forms a sink tree.
Sink trees are not necessarily unique
Goal of all routing algorithms
  Discover sink trees for all destinations

## Slide 15
Given a network topology and a set of weights describing the cost to send data across each link in the network
Find the shortest path from a specified source to all other destinations in the network.
Shortest path algorithm first developed by E. W. Dijkstra
Shortest Path Routing (a nonadaptive routing algorithm)

## Slide 16
Let the node at which we are starting be called the initial node. Let the distance of node Y be the distance from the initial node to Y. Dijkstra's algorithm will assign some initial distance values and will try to improve them step by step.
Assign to every node a tentative distance value:
  set it to zero for our initial node and to infinity for all other nodes.
Set the initial node as current. Mark all other nodes unvisited. Create a set of all the unvisited nodes called the unvisited set.
For the current node, consider all of its unvisited neighbors and calculate their tentative distances. Compare the newly calculated tentative distance to the current assigned value and assign the smaller one.
Steps in Dijkstra’s Algorithm

## Slide 17
When we are done considering all of the neighbors of the current node, mark the current node as visited and remove it from the unvisited set. A visited node will never be checked again.
If the destination node has been marked visited (when planning a route between two specific nodes), then stop. The algorithm has finished.
Otherwise, select the unvisited node that is marked with the smallest tentative distance, set it as the new "current node", and go back to step 3.
Steps in Dijkstra’s Algorithm

## Slide 18: Example of Shortest Path Routing

## Slide 19: Example of Shortest Path Routing

## Slide 20: Example of Shortest Path Routing

## Slide 21: Example of Shortest Path Routing

## Slide 22: Example of Shortest Path Routing

## Slide 23: Example of Shortest Path Routing

## Slide 24: Distance Vector Routing (an adaptive routing algorithm)
Bellman-Ford Routing
Neighboring routers periodically exchange information from their routing tables.
Routers replace routes in their own routing tables anytime that neighbors have found better routes.
Information provided from neighbors
  Outgoing line used for destination
  Estimate of time or distance
    can be number of hops, time delay, packet queue length, etc.

## Slide 25: Distance Vector Routing (an adaptive routing algorithm)

## Slide 26: Characteristics of Distance Vector Routing
Periodic Updates: Updates to the routing tables are sent at the end of a certain time period. A typical value is 90 seconds.
Triggered Updates: If a metric changes on a link, a router immediately sends out an update without waiting for the end of the update period.
Full Routing Table Update: Most distance vector routing protocol send their neighbors the entire routing table (not only entries which change).
Route invalidation timers: Routing table entries are invalid if they are not refreshed. A typical value is to invalidate an entry if no update is received after 3-6 update periods.

## Slide 27: The Count to Infinity Problem

## Slide 28: The Split Horizon Hack
Actual distance to a destination is not reported on the line on which packets to that destination are sent.
Instead these distances are reported as “infinity.”
B
D
A
C
C tells D the truth
about its distance to
A, but lies to B and
says the distance is
infinity.

## Slide 29: A topology where split horizon fails
Suppose that D becomes
unreachable from C.
A and B are reporting
infinite distances to C, but
they are reporting distances
of length 2 to each other.
A and B will count to infinity.

## Slide 30: Link State Routing (an adaptive routing algorithm)
Five Steps
1.) Discover your neighbors and learn their addresses.
2.) Measure the cost (delay) to each neighbor.
3.) Construct a packet containing all this information
4.) Send this packet to all other routers.
5.) Compute the shortest path to every other router.

## Slide 31: 1.) Discovering Your Neighbors
Send “Hello” packet on each point-to-point line. Destination node replies with its address.
2.) Measuring Line Cost
Send an “ECHO” packet over the line.
Destination is required to respond to “ECHO” packet immediately.
Measure the time required for this operation.

## Slide 32: 3. Build Link State Packets

## Slide 33: 4. Distributing the Link State Packets
Use selective flooding
Sequence numbers prevent duplicate packets from being propagated
Lower sequence numbers are rejected as obsolete

## Slide 34: 5. Computing the New Routes
Dijkstra’s Shortest Path algorithm is used to determine the shortest path to each destination.

## Slide 35: Multicast Routing
A method to broadcast packets to well-defined groups
Hosts can join multicast groups.
  They inform their routers
  Routers send group information throughout the subnet
Each router computes a spanning tree for each group. The spanning tree includes all the routers needed to broadcast data to the group

## Slide 36: Spanning Trees for Multicast Routing

## Slide 37
Routing in the Internet

## Slide 38: Routing in the Internet
The Global Internet consists of Autonomous Systems (AS) interconnected with each other:
  Stub AS: small corporation: one connection to other AS’s
  Multihomed AS: large corporation (no transit): multiple connections to other AS’s
  Transit AS: provider, hooking many AS’s together
Two-level routing:
  Intra-AS: administrator responsible for choice of routing algorithm within network
  Inter-AS: unique standard for inter-AS routing: BGP

## Slide 39: Internet AS Hierarchy
Intra-AS border (exterior gateway) routers
Inter-AS interior (gateway) routers

## Slide 40: Intra-AS Routing
Also known as Interior Gateway Protocols (IGP)
Most common Intra-AS routing protocols:
  RIP: Routing Information Protocol
  OSPF: Open Shortest Path First
  IGRP: Interior Gateway Routing Protocol (Cisco proprietary)

## Slide 41: OSPF (Open Shortest Path First)
“open”: publicly available
Uses Link State algorithm
  LS packet dissemination
  Topology map at each node
  Route computation using Dijkstra’s algorithm
OSPF advertisement carries one entry per neighbor router
Advertisements disseminated to entire AS (via flooding)
  Carried in OSPF messages directly over IP (rather than TCP or UDP

## Slide 42: OSPF “advanced” features (not in RIP)
Security: all OSPF messages authenticated (to prevent malicious intrusion)
Multiple same-cost paths allowed (only one path in RIP)
For each link, multiple cost metrics for different TOS (e.g., satellite link cost set “low” for best effort; high for real time)
Integrated uni- and multicast support:
  Multicast OSPF (MOSPF) uses same topology data base as OSPF
Hierarchical OSPF in large domains.

## Slide 43: Hierarchical OSPF

## Slide 44: Hierarchical OSPF
Two-level hierarchy: local area, backbone.
  Link-state advertisements only in area
  each nodes has detailed area topology; only know direction (shortest path) to nets in other areas.
Area border routers: “summarize” distances to nets in own area, advertise to other Area Border routers.
Backbone routers: run OSPF routing limited to backbone.
Boundary routers: connect to other AS’s.

## Slide 45: Hierarchical Routing

## Slide 46: Inter-AS routing in the Internet: BGP

## Slide 47: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto standard
Path Vector protocol:
  similar to Distance Vector protocol
  each Border Gateway broadcast to neighbors (peers) entire path (i.e., sequence of AS’s) to destination
  BGP routes to networks (ASs), not individual hosts
  E.g., Gateway X may send its path to dest. Z:
Path (X,Z) = X,Y1,Y2,Y3,…,Z

## Slide 48: Why different Intra- and Inter-AS routing ?
Policy:
Inter-AS: admin wants control over how its traffic routed, who routes through its net.
Intra-AS: single admin, so no policy decisions needed
Scale:
hierarchical routing saves table size, reduced update traffic
Performance:
Intra-AS: can focus on performance
Inter-AS: policy may dominate over performance

## Slide 49
Congestion Control

## Slide 50: Congestion
When one part of the subnet (e.g. one or more routers in an area) becomes overloaded, congestion results.
Because routers are receiving packets faster than they can forward them, one of two things must happen:
  The subnet must prevent additional packets from entering the congested region until those already present can be processed.
  The congested routers can discard queued packets to make room for those that are arriving.

## Slide 51: Congestion

## Slide 52: Congestion control
Congestion control refers to techniques and mechanisms that can either prevent congestion, before it happens, or remove congestion, after it has happened. In general, we can divide congestion control mechanisms into two broad categories:
open-loop congestion control (prevention)
closed-loop congestion control (removal).

## Slide 53: Congestion Control
Congestion Control is concerned with efficiently using a network at high load.
Several techniques can be employed. These include:
  Warning bit
  Choke packets
  Load shedding
  Random early discard
  Traffic shaping

## Slide 54: Warning Bit
The router sets a special bit in the packet header to warn the source when congestion is detected.
The bit is copied and piggybacked on the ACK and sent to the sender.
The sender monitors the number of ACK packets it receives with the warning bit set and adjusts its transmission rate accordingly.

## Slide 55: Choke Packets
A more direct way of telling the source to slow down.
A choke packet is a control packet generated at a congested node and transmitted to restrict traffic flow.
The source, on receiving the choke packet must reduce its transmission rate by a certain percentage.
An example of a choke packet is the ICMP Source Quench Packet.

## Slide 56: Hop-by-Hop Choke Packets
Over long distances or at high speeds choke packets are not very effective.
A more efficient method is to send to choke packets hop-by-hop.
This requires each hop to reduce its transmission even before the choke packet arrive at the source.

## Slide 57: Load Shedding
When buffers become full, routers simply discard packets.
Which packet is chosen to be the victim depends on the application and on the error strategy used in the data link layer.
For a file transfer, for, e.g. cannot discard older packets since this will cause a gap in the received data.
For real-time voice or video it is probably better to throw away old data and keep new packets.
Get the application to mark packets with discard priority.

## Slide 58: Random Early Discard (RED)
This is a proactive approach in which the router discards one or more packets before the buffer becomes full.
Each time a packet arrives, the RED algorithm computes the average queue length, avg.
If avg is lower than some lower threshold, congestion is assumed to be minimal or non-existent and the packet is queued.
If avg is greater than some upper threshold, congestion is assumed to be serious and the packet is discarded.
If avg is between the two thresholds, this might indicate the onset of congestion. The probability of congestion is then calculated.

## Slide 59
Another method of congestion control is to “shape” the traffic before it enters the network.
Traffic shaping controls the rate at which packets are sent (not just how many). Used in ATM and Integrated Services networks.
At connection set-up time, the sender and carrier negotiate a traffic pattern (shape).
Two traffic shaping algorithms are:
  Leaky Bucket
  Token Bucket
Traffic Shaping

## Slide 60: The Leaky Bucket Algorithm
A leaky bucket algorithm shapes bursty traffic into fixed-rate traffic by averaging the data rate. It may drop the packets if the bucket is full.

## Slide 61: The Leaky Bucket Algorithm
(a) A leaky bucket with water. (b) a leaky bucket with packets.
3 – 5 packets
5 – 6 packets
1 packet / sec

## Slide 62
Leaky Bucket Algorithm, cont.
The leaky bucket enforces a constant output rate (average rate) regardless of the burstiness of the input. Does nothing when input is idle.
The host injects one packet per clock tick onto the network. This results in a uniform flow of packets, smoothing out bursts and reducing congestion.
When packets are the same size (as in ATM cells), the one packet per tick is okay.
For variable length packets though, it is better to allow a fixed number of bytes per tick. E.g. 1024 bytes per tick will allow one 1024-byte packet or two 512-byte packets or four 256-byte packets on 1 tick.

## Slide 63: Token Bucket Algorithm
In contrast to the LB, the Token Bucket Algorithm, allows the output rate to vary, depending on the size of the burst.
In the TB algorithm, the bucket holds tokens. To transmit a packet, the host must capture and destroy one token.
Tokens are generated by a clock at the rate of one token every t sec.
Idle hosts can capture and save up tokens (up to the max. size of the bucket) in order to send larger bursts later.

## Slide 64: Token Bucket Algorithm

## Slide 65: Quality of Service
Reliability is the ability of a system to perform and maintain its functions in routine circumstances, as well as hostile or unexpected circumstances.
Delay
Jitter is the variation in the time between packets arriving, caused by network congestion, timing drift, or route changes.
Bandwidth

## Slide 66
Requirements
How stringent the quality-of-service requirements are.
5-30

## Slide 67: Buffering
Smoothing the output stream by buffering packets.