## Slide 1: Transport Layer

## Slide 2
Transport Layer
  Communication between processes (e.g., socket)
  Provide logical communication between application processes running on different hosts
  Relies on network layer and serves the application layer
  E.g., TCP and UDP

## Slide 3
Addressing
The transport layer provides the user address which is specified as a station or port.
The port variable represents a particular TS user of a specified station known as a Transport Service access point (TSAP).
Each station has only one transport entity.

## Slide 4
Multiplexing and Demultiplexing
Host receives IP datagrams
  Each datagram has source and destination IP address,
  Each datagram carries one transport-layer segment
  Each segment has source and destination port number
Host uses IP addresses and port numbers to direct the segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 5
Upward Multiplexing
Upward multiplexing means multiple transport layer connections use the same network connection.
To make more cost-effective, the transport layer sends several transmissions bound for the same destination along the same path;
this is achieved through upward multiplexing.

## Slide 6
Downward Multiplexing
Downward multiplexing means one transport layer connection uses the multiple network connections.
Downward multiplexing allows the transport layer to split a connection among several paths to improve the throughput.
This type of multiplexing is used when networks have a low or slow capacity.

## Slide 7
Internet Transport Protocols
Datagram messaging service (UDP)
  No-frills extension of “best-effort” IP
Reliable, in-order delivery (TCP)
  Connection set-up
  Discarding of corrupted packets
  Retransmission of lost packets
  Flow control
  Congestion control
Other services not available
  Delay guarantees
  Bandwidth guarantees

## Slide 8
Unreliable Message Delivery Service
Lightweight communication between processes
  Avoid overhead and delays of ordered, reliable delivery
  Send messages to and receive them from a socket
User Datagram Protocol (UDP)
  IP plus port numbers to support (de)multiplexing
  Optional error checking on the packet contents
SRC port
DST port
checksum
length
DATA

## Slide 9
Why Would Anyone Use UDP?
Finer control over what data is sent and when
  As soon as an application process writes into the socket
  … UDP will package the data and send the packet
No delay for connection establishment
  UDP just blasts away without any formal preliminaries
  … which avoids introducing any unnecessary delays
No connection state
  No allocation of buffers, parameters, sequence #s, etc.
  … making it easier to handle many active clients at once
Small packet header overhead
  UDP header is only eight-bytes long

## Slide 10
Popular Applications That Use UDP
Multimedia streaming
  Retransmitting lost/corrupted packets is not worthwhile
  By the time the packet is retransmitted, it’s too late
  E.g., telephone calls, video conferencing, gaming
Simple query protocols like Domain Name System
  Overhead of connection establishment is overkill
  Easier to have application retransmit if needed

## Slide 11
Transmission Control Protocol (TCP)
Connection oriented
  Explicit set-up and tear-down of TCP session
Stream-of-bytes service
  Sends and receives a stream of bytes, not messages
Reliable, in-order delivery
  Checksums to detect corrupted data
  Acknowledgments & retransmissions for reliable delivery
  Sequence numbers to detect losses and reorder data
Flow control
  Prevent overflow of the receiver’s buffer space
Congestion control
  Adapt to network congestion for the greater good

## Slide 12
Challenges of Reliable Data Transfer
Over a perfectly reliable channel
  All of the data arrives in order, just as it was sent
  Simple: sender sends data, and receiver receives data
Over a channel with bit errors
  All of the data arrives in order, but some bits corrupted
  Receiver detects errors and says “please repeat that”
  Sender retransmits the data that were corrupted
Over a lossy channel with bit errors
  Some data are missing, and some bits are corrupted
  Receiver detects errors but cannot always detect loss
  Sender must wait for acknowledgment (“ACK” or “OK”)
  … and retransmit data after some time if no ACK arrives

## Slide 13
TCP Support for Reliable Delivery
Checksum
  Used to detect corrupted data at the receiver
  …leading the receiver to drop the packet
Sequence numbers
  Used to detect missing data
  ... and for putting the data back in order
Retransmission
  Sender retransmits lost or corrupted data
  Timeout based on estimates of round-trip time
  Fast retransmit algorithm for rapid retransmission

## Slide 14
TCP “Stream of Bytes” Service
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out, or
“Pushed” by application.

## Slide 15
TCP Segment
Source port address and Destination port address: It is used to define the address of the application program in a source/destination computer. It is a 16-bit field.
Sequence number: A stream of data is divided into two or more TCP segments. The 32-bit sequence number field represents the position of the data in an original data stream.
Acknowledgement number: A 32-field acknowledgement number acknowledge the data from other communicating devices. If ACK field is set to 1, then it specifies the sequence number that the receiver is expecting to receive.

## Slide 16
TCP Segment
Header Length (HLEN): It specifies the size of the TCP header in 32-bit words. The minimum size of the header is 5 words, and the maximum size of the header is 15 words. Therefore, the maximum size of the TCP header is 60 bytes, and the minimum size of the TCP header is 20 bytes.
Reserved: It is a six-bit field which is reserved for future use.
Control bits: Each bit of a control field functions individually and independently. A control bit defines the use of a segment or serves as a validity check for other fields.

## Slide 17
TCP Segment
URG: The URG field indicates that the data in a segment is urgent.
ACK: When ACK field is set, then it validates the acknowledgement number.
PSH: The PSH field is used to inform the sender that higher throughput is needed so if possible, data must be pushed with higher throughput.
RST: The reset bit is used to reset the TCP connection when there is any confusion occurs in the sequence numbers.
SYN: The SYN field is used to synchronize the sequence numbers in three types of segments: connection request, connection confirmation ( with the ACK bit set ), and confirmation acknowledgement.
FIN: The FIN field is used to inform the receiving TCP module that the sender has finished sending data.

## Slide 18
TCP Segment
Window Size: The window is a 16-bit field that defines the size of the window.
Checksum: The checksum is a 16-bit field used in error detection.
Urgent pointer: If URG flag is set to 1, then this 16-bit field is an offset from the sequence number indicating that it is a last urgent data byte.
Options and padding: It defines the optional fields that convey the additional information to the receiver.

## Slide 19
TCP vs UDP
Basis for Comparison | TCP | UDP
Definition | TCP establishes a virtual circuit before transmitting the data. | UDP transmits the data directly to the destination computer without verifying whether the receiver is ready to receive or not.
Connection Type | It is a Connection-Oriented protocol | It is a Connectionless protocol
Speed | slow | high
Reliability | It is a reliable protocol. | It is an unreliable protocol.
Header size | 20 bytes | 8 bytes
acknowledgement | It waits for the acknowledgement of data and has the ability to resend the lost packets. | It neither takes the acknowledgement, nor it retransmits the damaged frame.

## Slide 20
TCP Connection Establishment
SYN
SYN ACK
ACK
Data
A
B
Data
Three-way handshake to establish connection
  Host A sends a SYN (open) to the host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK

## Slide 21
A’s port
B’s port
A’s Initial Sequence Number
Acknowledgment
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
A tells B it wants to open a connection…
TCP Connection Establishment

## Slide 22
TCP Connection Establishment
B’s port
A’s port
B’s Initial Sequence Number
A’s ISN plus 1
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
B tells A it accepts, and is ready to hear the next byte…

## Slide 23
TCP Connection Establishment
A’s port
B’s port
B’s ISN plus 1
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
A tells B it wants is okay to start sending
Sequence number

## Slide 24
What if the SYN Packet Gets Lost?
Suppose the SYN packet gets lost
  Packet is lost inside the network, or
  Server rejects the packet (e.g., listen queue is full)
Eventually, no SYN-ACK arrives
  Sender sets a timer and wait for the SYN-ACK
  … and retransmits the SYN-ACK if needed
How should the TCP sender set the timer?
  Sender has no idea how far away the receiver is
  Hard to guess a reasonable length of time to wait
  Some TCPs use a default of 3 or 6 seconds

## Slide 25
SYN Loss and Web Downloads
User clicks on a hypertext link
  Browser creates a socket and does a “connect”
  The “connect” triggers the OS to transmit a SYN
If the SYN is lost…
  The 3-6 seconds of delay may be very long
  The user may get impatient
  … and click the hyperlink again, or click “reload”
User triggers an “abort” of the “connect”
  Browser creates a new socket and does a “connect”
  Essentially, forces a faster send of a new SYN packet!
  Sometimes very effective, and the page comes fast

## Slide 26
Closing a Connection
FIN
FIN ACK
time
A
B
FIN
ACK
Closing the connection
  Finish (FIN) to close and receive remaining bytes
  And other host sends a FIN ACK to acknowledge
  Reset (RST) to close and not receive remaining bytes