## Slide 1: FLOW CONTROL and ERROR CONTROL

## Slide 2
The design of the simplest protocol with no flow or error control
Simplest Protocol
The sender sends a sequence of frames without even thinking about the receiver.
To send three frames, three events occur at the sender site and three events at the receiver site.

## Slide 3
Simplest Protocol

## Slide 4
Flow Control
Flow control is a design issue that generally observes proper flow of data from sender to receiver.
Flow control is a set of procedures that tells the sender how much data it can transmit before it must wait for an acknowledgement from the receiver.
Receiver has a limited speed at which it can process incoming data and a limited amount of memory in which to store incoming data.
Receiver must inform the sender before the limits are reached and request that the transmitter to send fewer frames or stop temporarily
  Stop and Wait protocol
  Sliding Window Protocol

## Slide 5
Stop and Wait
Data is broken down into multiple frames, and then receiver indicates its readiness to receive frame of data.
When acknowledgment is received, then only sender will send or transfer the next frame.

## Slide 6
Stop and Wait

## Slide 7
Stop and Wait - Piggybacking
A method to combine a data frame with ACK.
Station A and B both have data to send.
Instead of sending separately, station A sends a data frame that includes an ACK.
Station B does the same thing.
Piggybacking saves bandwidth.

## Slide 8
Sliding Window Protocol
Frame Sequence Numbers
Frames from a sender are numbered sequentially.
We need to set a limit since we need to include the sequence number of each frame in the header.
If the header of the frame allows m bits for sequence number, the sequence numbers range from 0 to 2 m – 1. for m = 3, sequence numbers are: 0, 1, 2, 3, 4, 5, 6, 7.
We can repeat the sequence number.
Sequence numbers are:
0, 1, 2, 3, 4, 5, 6, 7, 0, 1, 2, 3, 4, 5, 6, 7, 0, 1, …

## Slide 9
Sliding Window Protocol
Acknowledgements There are 2 kinds of acknowledgements namely:
Cumulative Ack: One acknowledgement is used for many packets. The main advantage is traffic is less. A disadvantage is less reliability as if one ack is the loss that would mean that all the packets sent are lost.
Independent Ack: If every packet is going to get acknowledgement independently. Reliability is high here but a disadvantage is that traffic is also high since for every packet we are receiving independent ack.

## Slide 10
Sliding Window Protocol
In this protocol both the sender and receiver agree upon total number of data frames after which acknowledgment is needed to be transmitted.
Data Link Layer requires and uses this method that simply allows sender to have more than one unacknowledged packet “in-flight” at a time.
At the sending site, to hold the outstanding frames until they are acknowledged, we use the concept of a window.
The size of the window is at most 2m -1 where m is the number of bits for the sequence number.
The window slides to include new unsent frames when the correct ACKs are received

## Slide 11
Sliding Window Protocol
Sender has 3 variables: S, SF, and SL
S holds the sequence number of recently sent frame
SF holds the sequence number of the first frame yet to receive acknowledgement
SL holds the sequence number of the last frame that can be sent before receiving any acknowledgement
If S reaches SL then sender will stop sending frames until it receive an acknowledgement.

## Slide 12
Sliding Window Protocol
Receiver has 3 variables: R, RF, and RL
R holds the sequence number of recently received frame
RF holds the sequence number of the first frame yet to send acknowledgement
RL holds the sequence number of the last frame that can be received before sending any acknowledgement
If receiver want to stop sender from sending anymore frame, it will stop sending acknowledgement for some time.
RF R RL

## Slide 13
Sliding Window Protocol
SF
S SL
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1
RF
R RL
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1
Frame 0
Frame 1
Frame 2
Frame 3
SF S SL
SF S SL
SF S SL
Frame 6
RF R
RL
RF R RL
RF R RL
ACK 0
SF S SL
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 0 | 1
RF R RL

## Slide 14
Error Control
Error control includes both error detection and error correction.
It allows the receiver to inform the sender if a frame is lost or damaged during transmission and coordinates the retransmission of those frames by the sender.
Error control in the data link layer is based on automatic repeat request (ARQ).
Whenever an error is detected, specified frames are retransmitted.
  Stop and Wait ARQ
  Go Back N ARQ
  Selective Repeat ARQ

## Slide 15
Stop & Wait ARQ
Sender keeps a copy of the last frame until it receives an acknowledgement.
For identification, both data frames and acknowledgements (ACK) frames are numbered alternatively 0 and 1.
Sender starts a timer when it sends a frame. If an ACK is not received within a allocated time period, the sender assumes that the frame was lost or damaged and resends it
Receiver send only positive ACK if the frame is intact.
ACK number always defines the number of the next expected frame

## Slide 16
Stop & Wait ARQ
Sender has a control variable (S) that holds the number of the recently sent frame. (0 or 1)
Receiver has a control variable R that holds the number of the next frame expected (0 or 1).

## Slide 17
Stop & Wait ARQ – Lost Frame
When a receiver receives a damaged frame, it discards it and keeps its value of R.
After the timer at the sender expires, another copy of frame 1 is sent.

## Slide 18
Stop & Wait ARQ – Lost Ack
If the sender receives a damaged ACK, it discards it.
When the timer of the sender expires, the sender retransmits frame 1.
Receiver has already received frame 1 and expecting to receive frame 0 (R=0). Therefore it discards the second copy of frame 1.

## Slide 19
Stop & Wait ARQ – Delayed Ack
The ACK can be delayed at the receiver or due to some problem
It is received after the timer for frame 0 has expired.
Sender retransmitted a copy of frame 0. However, R =1 means receiver expects to see frame 1. Receiver discards the duplicate frame 0.
Sender receives 2 ACKs, it discards the second ACK.

## Slide 20
Go Back N ARQ
We can send up to W frames before worrying about ACKs.
We keep a copy of these frames until the ACKs arrive.
This procedure requires additional features to be added to Stop-and-Wait ARQ.
Sender has 3 variables: S, SF, and SL
Receiver only has the one variable, R, that holds the sequence number of the frame it expects to receive. If the seq. no. is the same as the value of R, the frame is accepted, otherwise rejected.

## Slide 21
Go Back N ARQ
Receiver sends positive ACK if a frame arrived safe and in order.
If the frames are damaged/out of order, receiver is silent and discard all subsequent frames until it receives the one it is expecting.
The silence of the receiver causes the timer of the unacknowledged frame to expire.
Then the sender resends all frames, beginning with the one with the expired timer.
For example, suppose the sender has sent frame 6, but the timer for frame 3 expires (i.e. frame 3 has not been acknowledged), then the sender goes back and sends frames 3, 4, 5, 6 again. Thus it is called Go-Back-N-ARQ
The receiver does not have to acknowledge each frame received, it can send one cumulative ACK for several frames.

## Slide 22
Go Back N ARQ
The sender keeps track of the outstanding frames and updates the variables and windows as the ACKs arrive.

## Slide 23
Go Back N ARQ – Lost Frame
Frame 2 is lost
When the receiver receives frame 3, it discards frame 3 as it is expecting frame 2 (according to window).
After the timer for frame 2 expires at the sender site, the sender sends frame 2 and 3. (go back to 2)

## Slide 24
Go Back N ARQ
Size of the sender window must be less than 2 m. Size of the receiver is always 1. If m = 2, window size = 2 m – 1 = 3.
Fig compares a window size of 3 and 4.
Accepts as the 1st frame in the next cycle-an error

## Slide 25
Selective Repeat ARQ
Go-Back-N ARQ simplifies the process at the receiver site. Receiver only keeps track of only one variable, and there is no need to buffer out-of-order frames, they are simply discarded.
However, Go-Back-N ARQ protocol is inefficient for noisy link. It bandwidth inefficient and slows down the transmission.
In Selective Repeat ARQ, only the damaged frame is resent. More bandwidth efficient but more complex processing at receiver.
It defines a negative ACK (NAK) to report the sequence number of a damaged frame before the timer expires.

## Slide 26
Selective Repeat ARQ

## Slide 27
Frames 0 and 1 are accepted when received because they are in the range specified by the receiver window. Same for frame 3.
Receiver sends a NAK2 to show that frame 2 has not been received and then sender resends only frame 2 and it is accepted as it is in the range of the window.
Selective Repeat ARQ

## Slide 28
Size of the sender and receiver windows must be at most one-half of 2 m. If m = 2, window size should be 2 m /2 = 2. Fig compares a window size of 2 with a window size of 3. Window size is 3 and all ACKs are lost, sender sends duplicate of frame 0, window of the receiver expect to receive frame 0 (part of the window), so accepts frame 0, as the 1st frame of the next cycle – an error.
Selective Repeat ARQ