## Slide 1: ACTUATORS
Actuators are the devices which provide the actual motive force for the robot joints.
Actuators are the muscles of robots. If you imagine that the links and the joints are the skeleton of the robot, the actuators act as muscles, which moves or rotate the links to change the configuration of robots. The actuators must have enough power to accelerate and decelerate the links and to carry the loads, yet be light, economical, accurate, responsive, reliable and easy to maintain.
Actuators in robotic system basically consists of :
  A power supply.
  A power amplifier.
  A servomotor.
  A transmission system.

## Slide 2: Actuator system
POWER
SUPPLIES
POWER
AMPLIFIER
TRANSMISSION
MOTOR
OR
SERVO MOTOR
PP
Pu
Pa
Pm
Pc
Pda
Pds
Pdt
Pp : Primary source of power (Electric, Press.fluid, compress. Air)
Pc : Input control power usually electric .
Pa : Input power to motor Electric, Hydraulic, or Pneumatic.
Pm: Power output from motor.
Pu : mechanical power required
Pds, Pdt , Pda : Powers lost in dissipation for the conversion performed by the Amplifier, Motor, Transmission

## Slide 3: ISSUES/CHARACTERISTICS OF AN ACTUATOR
Load (e.g. torque to overcome own inertia)
Speed (fast enough but not too fast)
Accuracy (will it move to where you want?)
Resolution (can you specify exactly where?)
Repeatability (will it do this every time?)
Reliability (mean time between failures)
Power consumption (how to feed it)
Energy supply & its weight.

## Slide 4: TYPES OF ACTUATORS
Based on the source of Input Power actuators are classified in to three groups :
  Pneumatic Actuators.
    These utilize pneumatic energy provided by the compressor and transforms it into mechanical energy by means of pistons or turbines.
  Hydraulic Actuators.
    These Transform the energy stored in reservoir into mechanical energy by means of suitable pumps.
  Electric Actuators.
    Electric actuators are simply electro-mechanical devices which allow movement through the use of an electrically controlled systems of gears

## Slide 5: Pneumatic and Hydraulic Actuators
Both these actuators are powered by moving fluids.
In the first case, the fluid is compressed air and
In the second case, the fluid is pressurized oil.
Pneumatic systems typically operate at about 100lb/in2
Hydraulic systems at 1000 to 3000 lb/in2.
Both Hydraulic and Pneumatic actuators are classified as
    linear Actuators (Cylinders).
    Rotary Actuators (Motors).

## Slide 6: Pneumatic and Hydraulic Actuators
linear Actuators

## Slide 7: Pneumatic and Hydraulic Actuators
The simplest power device could be used to actuate a linear joint by means of a moving piston.
There are two relationships of particular interest when discussing actuators:
  The velocity of the actuator with respect to input power and
  Force of the actuator with respect to the input power.
linear Actuators
UNIT VII Robot Actuators & Feed Back Components

## Slide 8: Pneumatic and Hydraulic Actuators
linear Actuators
UNIT VII Robot Actuators & Feed Back Components

## Slide 9: Pneumatic and Hydraulic Actuators
Rotary Actuators

## Slide 10: Pneumatic and Hydraulic Actuators
There is a relationship of particular interest when discussing Rotary actuator:
The angular velocity, ω, and Torque, T.
R, outer radius of the vane., r, inner radius., h, thickness of the vane., ω, angular velocity., T, torque.
Rotary Actuators

## Slide 11: Advantages and limitations of Pneumatic actuators
ADVANTAGES
It is cheapest form of all actuators. Components are readily available and compressed air normally is an readily available facility in factories.
Compressed air can be stored and conveyed easily over long distances.
They have few moving parts making them inherently reliable and reducing maintenance costs.
They have quick action and response time thus allowing for fast work cycles.
No mechanical transmission is usually required.
These systems are usually compact thus the control is simple e.g: mechanical stops are often used.
LIMITATIONS
Since air is compressible, precise control of speed and position is not easily obtainable unless much more complex electro mechanical devices are incorporated in to system.
If mechanical stops are used resetting the system can be slow.
If moisture penetrates the units and ferrous metals have been used then damage to individual components may happen.

## Slide 12: Advantages and limitations of Hydraulic actuators
ADVANTAGES
High efficiency and high power to size ratio.
Complete and accurate control over speed position and direction of actuators are possible.
No mechanical linkage is required i.e., a direct drive is obtained with mechanical simplicity.
They generally have a greater load carrying capacity than electric and pneumatic actuators.
Self lubricating and non corrosive.
Hydraulic robots are more capable of with standing shock loads than electric robots.
LIMITATIONS
Leakages can occur causing a loss in performance and general contamination of the work area. There is also a higher fire risk.
The power pack can be noisy typically about 70 decibel or louder if not protected by an acoustic muffler.
Changes in temp alter the viscosity of hydraulic fluid. Thus at low temperatures fluid viscosity will increase possibly causing sluggish movement of the robot.

## Slide 13: Electric and Stepper Motors
There are a variety of types of motors used in robots. The most common types are Servomotors and Stepper motors.
      Electric actuators are simply electro-mechanical devices which allow movement through the use of an electrically controlled systems of gear.

## Slide 14: ELECTRIC MOTORS
Electric motors usually have a small rating, ranging up to a few horsepower.
They are used in small appliances, battery operated vehicles, for medical purposes and in other medical equipment like x-ray machines.
Electric motors are also used in toys, and in automobiles as auxiliary motors for the purposes of seat adjustment, power windows, sunroof, mirror adjustment, blower motors, engine cooling fans.

## Slide 15
ROTATING
(COMMUTATOR)
Brushes
ARMATURE
STATOR

## Slide 16: COMPONENTS OF DC ELECTRIC MOTOR
The principle components of an electric motor are: North and south magnetic poles to provide a strong magnetic field. Being made of bulky ferrous material they traditionally form the outer casing of the motor and collectively form the stator.
An armature, which is a cylindrical ferrous core rotating within the stator and carries a large number of windings made from one or more conductors.
A commutator, which rotates with the armature and consists of copper contacts attached to the end of the windings.
Brushes in fixed positions and in contact with the rotating commutator contacts. They carry direct current to the coils, resulting in the required motion.

## Slide 17: ELECTRIC MOTORS
DC motors :In DC motors, the stator is a set of fixed permanent magnets, creating a fixed magnetic field, while the rotor carries a current. Through brushes and commutators, the direction of current is changed continuously, causing the rotor to rotate continuously.
AC motors : These are similar to DC motors except that the rotor is permanent magnet, the stator houses the windings, and all commutators and brushes are eliminated.
A Servomotor is a DC,AC, brushless, or even stepper motor with feedback that can be controlled to move at a desired speed (and consequently, torque), for a desired angle of rotation. To do this, a feedback device sends signals to the controller circuit of the servomotor reporting its angular position and velocity.

## Slide 18: COMPONENTS OF DC ELECTRIC MOTOR
A simple DC electric motor: when the coil is powered, a magnetic field is generated around the armature. The left side of the armature is pushed away from the left magnet and drawn toward the right, causing rotation. The armature continues to rotate, When the armature becomes horizontally aligned, the commutator reverses the direction of current through the coil, reversing the magnetic field. The process then repeats.

## Slide 20: STEPPER MOTOR
When incremental rotary motion is required in a robot, it is possible to use stepper motors.
A stepper motor possesses the ability to move a specified number of revolutions or fraction of a revolution in order to achieve a fixed and consistent angular movement.
This is achieved by increasing the numbers of poles on both rotor and stator
Additionally, soft magnetic material with many teeth on the rotor and stator cheaply multiplies the number of poles(reluctance motor)

## Slide 21: Construction of Stepper Motor
A stepper motor is a special type of electric motor that converts electrical pulses into precise mechanical angular movements (steps). It is mainly made of the following parts:
Stator
  The stationary part of the motor.
  Made of laminated steel and has several salient poles.
  Each pole is wound with a coil (stator winding) that produces a magnetic field when energized.
Rotor
  The rotating part, placed inside the stator.
  It can be of three types:
    Permanent Magnet Rotor – uses a permanent magnet, simple construction.
    Variable Reluctance Rotor – made of soft iron with teeth to provide a low reluctance path for magnetic flux.
    Hybrid Rotor – combines both permanent magnet and reluctance features for high precision.

## Slide 22: Construction of Stepper Motor
Rotor
    Permanent Magnet Rotor – uses a permanent magnet, simple construction.
    Variable Reluctance Rotor – made of soft iron with teeth to provide a low reluctance path for magnetic flux.
    Hybrid Rotor – combines both permanent magnet and reluctance features for high precision.

## Slide 23: Construction of Stepper Motor
Shaft
  Connected to the rotor, transmits motion to the external load.
Bearings
  Support the shaft and allow smooth rotation.
Driver Circuit
  An electronic driver is used to energize stator windings sequentially according to input pulses from a controller (like a microcontroller or computer).

## Slide 24: Working Principle of Stepper Motor
The stepper motor works on the principle of electromagnetism and stepwise excitation:
    When an electrical pulse is applied to a stator winding, it creates a magnetic field in that pole.
    The rotor aligns itself with the energized stator pole due to magnetic attraction.
    When the next winding is energized (as per sequence), the magnetic field shifts, and the rotor moves a fixed angular distance (step angle) to align with the new pole.
    By applying pulses in a specific sequence, the rotor continues to rotate step by step.
    The step angle depends on the number of stator and rotor teeth and defines the resolution of movement (e.g., 1.8° per step means 200 steps per revolution).
    The speed of the motor is controlled by the frequency of input pulses, and the position is controlled by the number of pulses applied.

## Slide 25: Types of Stepper Motor Operation (Modes of Excitation)
Single-phase excitation – only one winding is energized at a time (less torque).
Two-phase excitation – two windings energized simultaneously (more torque).
Half-step mode – alternates between single and double excitation for smoother motion.
Micro-stepping mode – divides current in windings to achieve very fine angular resolution.
In summary:
A stepper motor has a stator with multiple windings and a toothed or magnetized rotor. When stator windings are energized in sequence, the rotor moves in small, precise steps, making it highly useful in applications like CNC machines, robotics, 3D printers, and disk drives.

## Slide 26: STEPPER MOTOR

## Slide 27: ADVANTAGES & LIMITATIONS OF ELECTRIC ACTUATORS
ADVANTAGES
Wide spread availability of power supply.
The basic dive element in an electric motor is usually lighter than that for fluid power.
High power conversion efficiency.
No pollution of working environment
The accuracy and repeatability of electric power driven robots are normally better than fluid power robots in relation to cost.
Easily maintained and repaired.
The drive system is well suited to electronic control.
LIMITATIONS
Electric actuators often require some sort of mechanical transmission system this increases the unwanted movement, additional power and may complicate control.
Due to increased complexity of the transmission system additional cost is incurred for their procurement and maintenance.
Electric motors are not intrinsically safe. They cannot therefore be used in for example explosive atmospheres.

## Slide 28: APPLICATIONS
Stepper motors can be a good choice whenever controlled movement is required.
They can be used to advantage in applications where you need to control rotation angle, speed, position d synchronism. These include :
  printers
  plotters
  medical equipment
  fax machines
  automotive and scientific equipment etc.

## Slide 29: Comparison of actuating systems
Hydraulic
+ Good for large robots and heavy payload
+Highest Power/Weight Ratio
+Stiff system, High accuracy, better response
+No reduction gear needed
+Can work in wide range of speeds without difficulty
+Can be left in position without any damage
Electric
+ Good for all size of Robots
+Better control, good for high precision robots
+Higher Compliance that Hydraulics
+Reduction gears used reduce inertia on the motor
+does not leak, good for clean room
+Reliable, low maintenance
Pneumatic
+ Many components are usually off-the-shelf
+Reliable components.
+No leaks or sparks
+Inexpensive and simple
+Low pressure compared to hydraulics
+ Good for on-off applications and for pick and place

## Slide 30: Comparison of actuating systems
Hydraulic
- May leak. Not fit for clean room application
-Requires pump, reservoir, motor, hoses etc.
-Can be expensive and noisy, requires maintenance.
-Viscosity of oil changes with temperature
-Very susceptible to dirt and other foreign material in oil
-Low compliance
-High torque, High pressure, large inertia on the actuator.
Electric
+Can be spark-free. Good for explosive environment.
-Low stiffness
-Needs reduction gears, increased backlash, cost, weight, etc.
-Motor needs braking device when not powered. Otherwise, the arm will fail.
-
-
-
Pneumatic
+Complaint systems.
-Noisy systems.
- Require air pressure, filter, etc.
-Difficult to control their linear position
-Deform under load constantly
-Very low stiffness. Inaccurate response.
-Lowest power to weight ratio