## Slide 1: E – WASTE MANAGEMENT
Course Outcomes:
CO1: Understand the environmental impacts of e-waste. (L2)
CO2: Apply concepts of e-waste management hierarchy.(L3)
CO3: Distinguish the role of various national and internal act and laws applicable for e-waste management and handling.(L4)
CO4: Analyze the e – waste management measures proposed under national and global legislations. (L4)

## Slide 2: E – WASTE MANAGEMENT
Introduction:
E- waste Composition and generation
Global context in E- waste
E-waste pollutants
E waste hazardous properties
Effects of pollutant (E- waste) on human health and surrounding environment
Domestic e-waste disposal
Basic principles of E-waste management
Component of E waste management
Technologies for recovery of resources from electronic waste
Resource recovery potential of e-waste
Steps in recycling and recovery of materials-mechanical processing
Technologies for recovery of materials
Occupational and environmental health perspectives of recycling e-waste in India.

## Slide 3: UNIT-I
Introduction:
E-waste or Electronic waste broadly describes discarded, surplus, obsolete, broken, electrical or electronic devices which are at the end of their useful life and need to be disposed or dismantled to recover some valuable components. this e-waste stream as ‘Waste Electrical and Electronic Equipment’ (WEEE).

## Slide 4: Definition
Electronic waste or E-waste describes discarded electrical or electronic devices. It is also commonly known as waste electrical and electronic equipment(WEEE) or end-of-life electronics.
"E-Waste is a term used to cover items of all types of electrical and electronic equipment (EEE) and its parts that have been discarded by the owner as waste without the intention of re-use."

## Slide 9: Classification of e-waste

## Slide 14: Composition of E-Waste:
E-waste consists of all waste from electronic and electrical appliances which have reached their end- of- life period or are no longer fit for their original intended use and are destined for recovery, recycling or disposal.
It includes computer and its accessories monitors, printers, keyboards, central processing units; typewriters, mobile phones and chargers, remotes, compact discs, headphones, batteries, LCD/Plasma TVs, air conditioners, refrigerators and other household appliances.
The composition of e-waste is diverse and falls under ‘hazardous’ and ‘non-hazardous’ categories.
Broadly, it consists of ferrous and non-ferrous metals, plastics, glass, wood and plywood, printed circuit boards, concrete, ceramics, rubber and other items.

## Slide 16
Iron and steel constitute about 50% of the waste
Plastics - 21%
Non-ferrous metals - 13% and other constituents.
Non-ferrous metals consist of metals like copper, aluminum and precious metals like silver, gold, platinum, palladium and so on.
The presence of elements like lead, mercury, arsenic, cadmium, selenium, hexavalent chromium, and flame retardants beyond threshold quantities make e-waste hazardous in nature.
It contains over 1000 different substances, many of which are toxic, and creates serious pollution upon disposal.
Obsolete computers pose the most significant environmental and health hazard among the e-wastes

## Slide 17: E-waste generation:
All over the world, the quantity of electrical and electronic waste generated each year, especially computers and televisions, has assumed alarming proportions.
In 2006, the International Association of Electronics Recyclers (IAER) projected that 3 billion electronic and electrical appliances would become WEEE or e-waste by 2010. That would tantamount to an average e-waste generation rate of 400 million units a year till 2010.
Globally, about 20-50 MT (million tonnes) of e-wastes are disposed off each year, which accounts for 5% of all municipal solid waste.

## Slide 18
According to the Comptroller and Auditor- General’s (CAG) report, over 7.2 MT of industrial
hazardous waste, 4 lakh tonnes of electronic waste, 1.5 MT of plastic waste, 1.7 MT of
medical waste, 48 MT of municipal waste are generated in the country annually.
In 2005, the Central Pollution Control Board (CPCB) estimated India’s e-waste at 1.47 lakh tonnes or 0.573 MT per day.
A study released by the Electronics Industry Association of India (ELCINA) at the electronics industry expo – “Componex Nepcon 2009” had estimated the total e-waste generation in India at a whopping 4.34 lakh tonnes by end 2009.
The CPCB has estimated that it will exceed the 8 lakh tonnes or 0.8 MT mark by 2012.
The main sources of electronic waste in India are the government, public and private (industrial) sectors, which account for almost 70 per cent of total waste generation.
The contribution of individual households is relatively small at about 15 per cent; the rest being contributed by manufacturers. Though individual households are not large contributors to waste generated by computers, they consume large quantities of consumer durables and are, therefore, potential creators of waste.
An Indian market Research Bureau (IMRB) survey of ‘E-waste generation at Source’ in 2009 found that out of the total e-waste volume in India, televisions and desktops including servers comprised 68 per cent and 27 per cent respectively.
Imports and mobile phones comprised of 2 per cent and 1 per cent respectively.

## Slide 19: Electronic waste in the global context:
As the fastest growing component of municipal waste across the world, it is estimated that more than 50 MT of e-waste is generated globally every year.
A report of the United Nations predicted that by 2020, e-waste from old computers would jump by 400 per cent on 2007 levels in China and by 500 per cent in India.
Additionally, e-waste from discarded mobile phones would be about seven times higher than 2007 levels and, in India, 18 times higher by 2020.
China already produces about 2.3 million tonnes of e-waste domestically, second only to the U.S. with about three million tonnes.
The EU and the U.S. would account for maximum e-waste generation during this current decade.
As per the Inventory Assessment Manual of the UNEP, 2007, it is estimated that the total e-waste generated in the EU is about 14-15 kg per capita or 5MT to 7MT per annum.
In countries like India and China, annual generation per capita is less than 1kg.

## Slide 21: Projected electronic waste generation worldwide from 2019 to 2030 (in million metric tons)

## Slide 22
In Europe, e-waste contributes up to 6 million tonnes of solid waste per annum.
The e-waste generation in the EU is expected to grow at a rate of 3 per cent to 5 per cent per year.
In the past, e-waste had increased by 16 per cent to 28 per cent every five years which is three times faster than average annual municipal solid waste generation.
In the U.S., e-waste accounts for 1 to 3 per cent of the total municipal waste generation.
As per the United States Environmental Protection Agency (USEPA), it generated 2.6 MT of e-waste in 2005, which accounted for 1.4 per cent of total wastes.
Electronic waste is generated by three major sectors in the U.S.:
Individuals and small businesses;
Large businesses, institutions and governments; and
Original equipment manufacturers (OEMs)

## Slide 23: E-waste pollutants:
Pollutants or toxins in e-waste are typically concentrated in circuit boards, batteries, plastics, and LCDs (liquid crystal displays). Pollutants and their occurrence in waste electrical and electronic equipment are:
Pollutants | Occurrence
Arsenic | Semiconductors, diodes, microwaves, LEDs (Light-emitting diodes), solar cells
Barium | Electron tubes, filler for plastic and rubber, lubricant additives
Brominated flame-proofing agent | Casing, circuit boards (plastic), cables and PVC cables
Cadmium | Batteries, pigments, solder, alloys, circuit boards, computer batteries, monitor cathode ray tubes (CRTs)
Chrome | Dyes/pigments, switches, solar

## Slide 24
Pollutants | Occurrence
Cobalt | Insulators
Copper | Conducted in cables, copper ribbons, coils, circuitry, pigments
Lead | Lead rechargeable batteries, solar, transistors, lithium batteries, PVC (polyvinyl chloride) stabilizers, lasers, LEDs, thermoelectric elements, circuit boards
Liquid crystal | Displays
Lithium | Mobile telephones, photographic equipment, video equipment (batteries)
Mercury | Components in copper machines and steam irons; batteries in clocks and pocket calculators, switches, LCDs
Nickel | Alloys, batteries, relays, semiconductors, pigments
PCBs (polychlorinated biphenyls) | Transformers, capacitors, softening agents for paint, glue, plastic
Selenium | Photoelectric cells, pigments, photocopiers, fax machines
Silver | Capacitors, switches (contacts), batteries, resistors
Zinc | Steel, brass, alloys, disposable and rechargeable batteries, luminous substances

## Slide 25: E waste hazardous properties

## Slide 27: Effects of pollutant (E- waste) on human health and surrounding environment

## Slide 30
Mercury is mobile and poisonous in any form - inorganic, organic or elemental. Its organic compound methyl mercury has been scientifically proved to be a neuro-toxicant that damages the brain.
Mercury is known to cause severe and permanent damage to the central nervous system, lungs and kidneys.
It can trigger depression and suicidal tendencies and cause paralysis, Alzheimer’s disease, speech and vision impairment, allergies.

## Slide 33: Basic principles of E waste management

## Slide 34: REDUCTION
Product reuse
Material volume reduction
Toxicity reduction
Increased product lifetime
Decreased consumption

## Slide 35: . REUSE
Containers can be reused at home or for school projects
Reuse wrapping paper, plastic bags, boxes, and lumber.
Give outgrown clothing to friends or charity
Buy beverages in returnable containers
Donate broken appliances to charity or a local vocational school, which can use them forart classes or for students to practice repairing.
Offer furniture and household items that are no longer needed to people in need, friends or charity.

## Slide 36: RECYCLE
lessens reliance on landfills and incinerators
protects human health and the environment by removing harmful substances from the waste stream
conserves natural resources by reducing the demand for raw materials.

## Slide 38: Component of E waste management

## Slide 39
The components of recycling and resource recovery in e-waste management are seen as a process of ‘problem to resources’, bringing circular economy (CE) and resource efficiency (RE) to centre-stage along with safe environment and human health.
The CE and RE are associated with social and economic benefts including job creation, investment in technology development and infrastructure building.
Higher rates of e-waste generation are caused by shorter life cycles of e-products, and fewer repair options.
Thus, introducing resource recovery, REs and CE link with recy- cling/treating e-waste.
Spreading awareness among users of e-products, user roles in minimising e-waste, and contribution to tax regime/fees for recycling also have become the agenda of e-waste management.
The dominant discourse on governance of e-waste includes increasing e-waste collection and recycling; generating and harmonising statistics on e-waste across the world; existing regulatory/legislative framework, expansion of legal net and legal compliance; urban mining; economic potentials – resource recovery and reduc- ing use of virgin materials; and protecting health of workers exposed to hazard- ous e-waste in improper working conditions; adhering environmental concerns.

## Slide 40: Resource recovery potential of e-waste
E-waste consists of materials that can be recovered and reused in the manufacturing process.
Figure 1 shows the percentage composition of various useful components present in the computer waste.
The composition of mobile phones also indicate the possibility of recovery of plastics, aluminum, copper, ferrous metals, gold, palladium, and platinum.
It is possible to recover 90% of the materials present in mobile phones, which can be used as raw materials for other products (Table 2).
Stainless steel can be made from nickel and cobalt, and new batteries can be manufactured from cadmium obtained from old batteries; gold and silver recovered from circuit boards can be used for various applications, and new plastics and metals products can result from plastics and metals
Though the percentage of precious metals and other non-ferrous metals in mobile phone is less than that in computer waste, there is a possibility of recovering the available resources by efficient mechanical processing techniques.
Due to the fraction of the non ferrous and precious metals in TV scraps compared to personal computer, efficient methods of disassembling and recovery process is necessary for cost effective recycling.

## Slide 41: Resource recovery potential of e-waste

## Slide 44
The resource recovery potential has led to the increase in demand of e-waste in the recycling business in various countries including India.
In developed countries ,the recycling process is carried out in an organized sector, while in developing countries like India, this is done primarily in an unorganized sector.
It is necessary to have simple, environment-friendly, and economically viable management practices.
Efficient collection mechanisms coupled with appropriate equipment and technological interventions would help in improving the profitability of the business and the quality of life of the workers who are part of the recycling chain.

## Slide 45: Steps in recycling and recovery of materials-mechanical process
Collection, dismantling, mechanical processing, and metal extraction are the major steps in recyling

## Slide 46
Mechanical processlng

## Slide 47
As e-waste is a complex mix of substances, it is characterized by heterogeneity, with the presence of materials with varying physical and chemical characteristics. This property facilitates the easy separation of the materials based on the magnetic properties and particle size. During this stage, adequate care should be taken for achieving high recycling targets, and safe and efficient removal of hazardous substances from the useable materials.
The components that should be removed before further processing, because of their hazardous nature, include capacitors containing printed circuit boards, CRTs (cathode ray tubes), toner cartridges, mercury switches, batteries, plastics containing halogenated flame retardants, and fluorescent lamps.
After the separation of components containing hazardous materials and reusable parts, the electronic components and the assemblies undergo mechanical processing, which involves shredding and grinding to reduce the particle size.
The next stage separates the ferrous materials based on their magnetic properties

## Slide 49: Steps in recycling and recovery of materials-mechanical processing
THE PROCESS E-Waste recycling process should be a balance between disassembly, mechanical separation of complex materials and metallurgical treatment.
First Stage - Manual segregation of components, where different parts of E-waste are separated.
Second Stage - The mechanical separation process is applied. In this process, ferrous, aluminum, plastic and non ferrous material are initially separated.
Third Stage - The plastics are then recycled by plastics recycling process which further processes the plastic.
Fourth Stage - The non-ferrous metals are sent to metallurgical treatment plant where the nonferrous metals are separated into constituent metals.

## Slide 50
Schematic Diagram of Mechanical Recycling Process of WEEE

## Slide 51
Mechanical processes, such as screening, shape separation, magnetic separation, Eddy current separation, electrostatic separation, and jigging have been widely utilized in recycling industry.
Disassembly Selective disassembly or dismantling has been an indispensable step in waste recycling because of reuse priority, removal of selective hazardous components and separation of precious/desirable parts such as printed circuit boards, cables, and plastics. It is also crucial for simplification of subsequent steps in pursuit of recovery of materials. Dismantling remains a manual process with application of various tools for increased efficiency and lower time. However, it may be a costly affair to perform manual dismantling of products containing lowgrade precious metals and copper like TV sets, video etc.

## Slide 52
Screening and Shape Separation:
Screening is very significant step for size uniformity as well as upgrading metal content. As the particle size-shape properties of metals differ from plastics and ceramics, this process can play a crucial role in making metal rich streams. Rotating screens have been significantly used for metal recovery. Rotating screen shows high resistance to blinding, which helps in the process as the particle shapes and sizes are highly varying in electronic waste. Another widely accepted technique is vibratory screening specifically for non-ferrous recovery sites. Shape separation has played an important role in controlling particle properties. Tilted plate and sieves are the most common approach while inclined conveyor and vibrating plate have also been used to recover metals from waste cable, printed circuit boards, TV and personal computers

## Slide 53
Magnetic Separation:
Magnetic separators have been extensively used for separation of ferromagnetic materials. Low-intensity drum separators separates ferromagnetic metals from non-ferrous/nonmagnetic materials in waste stream.
With latest advancements in High-intensity magnetic separators, it is now possible to separate copper alloys from the waste matrix.
Electric Conductivity based Separation:
Based on different electric conductivity of materials, it is possible to separate them through Electric conductivity-based separation.
Eddy current separation, Corona electrostatic separation, and Triboelectric separation are major techniques based on this concept.
Eddy current separators have been highly successful in the recovery non-ferrous metals from shredded coarse size electronic scrap.
Electrostatic separator with application of corona charging separates raw materials into conductive and non-conductive fractions. The extreme difference in the electric conductivity of metals and non-metals forms the basis of corona electrostatic separation electronic waste recycling.
Recovery of copper, aluminum and precious metals from electronic scrap has been performed using this technique.
Triboelectric separation separates plastics based on the difference in electric properties, which has been highly desirable for plastic recovery and refining.

## Slide 54
Density/Gravity based Separation:
Heavy materials can be separated from lighter ones based on their density difference. This serves as the principle for density based separation and has been extensively applied for the separation of metals from non-metals.
Gravity concentration works on the fact that materials of different specific gravity have different relative movement in response to the force of gravity and other forces like resistance by fluid (air/water). Particle motion in a fluid is affected by multiple factors including particle’s density, size as well as shape so size control of feed determines the effectiveness of gravity/density processes.
Jigging is one of the widely used methods of gravity concentrations in mineral processing industry for concentrating relatively coarse materials.
With a fairly uniform feed size, good separation of a narrow gravity range can be achieved, acting as an efficient way for sorting small pieces of metals.
Heterogeneity and high complexity of electronic waste makes it difficult to be separated by jigging process

## Slide 55: Magnetic separator

## Slide 56
An eddy current separator (ECS) is a machine that uses a powerful magnetic field to separate non-ferrous metals from an input waste or ore stream.

## Slide 57: Density separator

## Slide 58: Technologies for recovery of materials
Pyro-metallurgy
Hydrometallurgy
Bio-metallurgy

## Slide 59
PROCESSES FOR RECYCLING
Mechanical-physical separation
Liberation of materials from their interlocked state physically by comminution
and separation of valuable materials into concentrates.
Comminution - shredding and screening
Separation - shape separation, density separation, magnetic separation,
eddy current separation and electrostatic separation
Pyrometallurgical processes
Extraction and purification of metals by processes involving the application of heat.
Smelting, incineration, combustion, pyrolysis, molten salt, and pyrochemical processes.
Hydrometallurgical processes
Selective leaching of metallic compounds to form a solution from which the metals can be precipitated and recovered.
Leaching, precipitation, solvent extraction, and resin ion exchange.
Notes: Mechanical treatment and physical separation processes are widely used for recycling. Comminution involves size reduction and size-wise classification. Shredding and screening is used prior to separation of metals and plastics for the physical liberation of materials (such as plastics, different metals, etc.) from their interlocked state. Once the materials are well liberated and particle size is suitable, separation technologies are applied resulting in production of concentrates.
Adapted separation techniques such as shape separation, density separation, magnetic separation, eddy current separation and electrostatic separation are then used to prepare concentrates of valuable materials contained in the WEEE streams.
Pyrometallurgy defined as a process of extraction and purification of metals by processes involving the application of heat was proven an efficient method for recovery of metallic fractions. The main pyrometallurgical methods used for recycling of electronic equipment include smelting, incineration, combustion, pyrolysis, molten salt, and pyrochemical processes.
Hydrometallurgical processes are bysed on chemical leaching of metals to form a solution. Metals are then precipitated and recovered.

## Slide 60
PRE-TREATMENT (HYDROMETALLURGY)
Disassembly
  Manual (labor intensive),
  automated (melting of solder joints).
Size reduction (optional) :
  Shredding, crushing and grinding.
Enrichment (optional) – separation:
  Size and shape, magnetism, electric conductivity (eddy current, corona electrostatic or triboelectric separation), density.
Chemical pre-treatment
  Solder mask dissolving, solder dissolving, organic swelling, supercritical depolymerization, resin dissolving.
Disassembly
Crushing
Grinding
Magnetic separation
Ferrous metals
Electric separation
Shredding
Electronic components
Base board
Non-metals
Non-ferrous metals
Source: https://www.sciencedirect.com/science/article/pii/S092134491830288X
Pre-treatment
Leaching
Purification
Recovery
Notes: Generally, the process for the hydrometallurgical recycling of waste printed circuit board can be divided into pre-treatment, leaching, purification and recovery. First stage of the pre-treatment is the disassembly of electronic components (resistors, capacitors, chips, batteries etc.), leaving the actual stripped circuit board. Electronic components with a high content of metals are usually recycled separately. Dismantling can be either done manually, which is very labor intensive, or using new automated methods which are based on destroying solder joints between electronic components and boards and then separating them by an external force. Usually, heat is applied to melt the solder.
Next step is size reduction – shredding, crushing and grinding is used to enhance the contact of metals during leaching (because most of the metals are laminated in resin layer by layer).
Various separation methods based on physical properties can be used for the enrichment of metals. These methods include size and shape separation, separation based on electric conductivity, magnetic properties or density.
Also chemical pre-treatment methods can be used. Chemicals are used to dissolve solder mask (sodium hydroxide), dissolve solder (using acids such as methanesulforic acid, hydrochloric acid or dilute nitric acid), dissolve resin or other purposes.

## Slide 61
LEACHING OF METALS (HYDROMETALLURGY)
Transfer of metals from solid materials to a solution
Traditional leaching methods
  Leaching of base and precious metals using mineral acids.
    Mineral acids only - H2SO4, HNO3, HCl and aqua regia (HCl:HNO3 = 3:1, v/v).
    Using mineral acid and oxidant - metals with high reduction potentials.
    Multi-stage leaching – selective leaching of metals.
  Cyanide-based leaching of precious metals
Mild leaching methods
  Thiourea leaching of precious metals – acid or alkaline thiourea
  Thiosulfate leaching of precious metals (S2O32−)
  Thiocyanate leaching of precious metals
  Halide leaching of precious metals
  Ammonia-ammonium leaching of base metals
Novel leaching methods
  Chelating leaching of base metals
  Ionic liquid leaching of base metals
  Supercritical leaching of base and precious metals
Source: https://www.sciencedirect.com/science/article/pii/S092134491830288X
Pre-treatment
Leaching
Purification
Recovery
Notes: The purpose of leaching is the transfer of solid metals into a solution. Traditional leaching methods include leaching with mineral acids and cyanide based leaching. Their advantage is relatively low cost. And a well investigated mechanism usually with predicable results. Acids used for this purpose include sulphuric acid, nitric acid, hydrochloric acid or aqua regia. Generally, method of using only mineral acids can be used for leaching of metals like zinc, tin, iron and aluminium. On the other hand, copper and precious metals are dissolved only partially. If also oxidant is used (such as hydrogen peroxide or chlorine) recovery of metals with reduction potentials is improved, accelerating the leaching efficiency. Selective leaching of metals can be achieved if multi-stage approach is used.
Cyanide based leaching is used for more than a century for leaching of precious metals. While cyanide is highly toxic it is very efficient and low cost and thus still preferred in industrial applications if the legislation is not a problem.
Mild leaching methods replace these solvents in favor of solvents which are considered less harmful to environment. This is also expected as solving one environmentally related problem and by creating another is not advisable. Thio-systems (thiourea – both alkaline and acidic, thiocyanate and thiosulfate) and halide leaching were investigated for leaching of precious metals and ammonia-ammonium system for leaching of base metals.
Scientists also study novel leaching methods to overcome the limitations in traditional and mild leaching methods. These novel methods include chelating leaching (EDTA) of base metals, ionic leaching of base metals or supercritical leaching which can be used for base and precious metals. However, they are yet to be apllied in industrial scale.

## Slide 62
PURIFICATION AND RECOVERY (HYDROMETALLURGY)
Purification – removal of harmful substances from solutions
Recovery – precipitation of the dissolved metals and their recovery in solid form.
Various methods:
  Chemical precipitation – displacement reaction (more active metal replaces less active metal in solution)
    Cementation – Fe replaces Cu; base metals replace precious metals.
    pH adjustment, using other chemicals for precipitations
  Solvent extraction (metals are passed from the leach solution into extraction solution and the two phases are then separated).
  Activated carbon adsorption - Au and Ag recovery from cyanide leaching solutions.
  Ion exchange by resin – comparable to adsorption with activated carbon often with higher adsorption and recovery rates
  Electrodeposition – utilization of simple electric device with minimal chemicals input – environmental point of view.
Source: https://www.sciencedirect.com/science/article/pii/S092134491830288X
Pre-treatment
Leaching
Purification
Recovery
Notes: Through the leaching process, metals in WPCBs are transferred into solution. To make final metal products, the leaching solution needs to be further treated for purification and recovery. Pregnant solution from leaching and purification operations is treated in a variety of ways to precipitate the dissolved metal values and recover them in solid form. These methods include cementation, chemical precipitation other than cementation, solvent extraction, activated carbon adsorption, ion exchange by resin and electrolytic deposition also called electrowinning.
There are several ways of chemical precipitation of metals. Cementation is a widely used method for recovery of copper. Iron replaces copper ions in solution (iron is thus dissolved into solution), while solid particles of copper precipitate (and copper is removed from the solution). More generally, base metals such as iron, zinc, aluminium and copper are used to replace precious metals in solution during cementation precipitation. Other chemical precipitation methods include pH adjustment by introducing alkali such as sodium hydroxide. Different metals precipitate at different pH levels and this way some selectivity can be achieved. For example tin is precipitated from solution at pH 1.5, iron at pH 3, copper at pH 6 and zinc at an alkaline pH of 8. Alternatively, other chemical substances can be used to precipitate metals from solution based on the properties of the solution.
Solvent extraction is used to concentrate metals. Small amount of solvent is added to dilute leaching solution. Metals pass from the leaching solution to solvent which and phases are then separated resulting in more concentrated solution suitable for another processing step.
Large adsorption capacity of activated carbon is utilized in another method used for recovery of gold and silver from cyanide leaching solutions. Adsorption using activated carbon is fast and with relatively high selectivity. Since activated carbon can also partially adsorb base metal ions (such as copper, zinc, iron, and nickel), a previous step is often required before using it for gold and silver recovery.
Similarly to carbon adsorption, ion exchange can be utilized with some advantages such as higher adsorption rates and gold recovery rates, desorption and regeneration under ambient pressures and temperatures.
Last mentioned is electrodeposition. Insoluble anodes, and cathodes made of either a strippable inert material or a thin sheet of the deposited metal, are inserted into a tank containing leach solution. As current is passed, the solution dissociates, and metal ions deposit at the cathode. From environmental point of view this method is superior as it only uses minimum chemical inputs.

## Slide 63
PYROMETALLURGY (PCBs)
Pre-treatment (dismantling of electronic components, grinding)
Incineration
  Aerobic conditions – organic components are thermally decomposed and combusted at high temperature.
  Glass-fibers and metal oxides (recycled by physical separation methods).
Pyrolysis
  Thermochemical decomposition of organic resins in anaerobic conditions.
  Pyrolysis products (oil and gasses) and residues (glass fibers and metals)
Plasma
  Decomposition of organic matter to gasses and melting of glass fibers.
  Gasses, vitreous body (molten glass fibers), metals.
Molten salt
  Molten salt (stable and inert) is used to separate liquid or solid-state metal products at high temperature.
Source: https://www.sciencedirect.com/science/article/pii/S0921344917302409
Pre-treatment
Pyrometallurgical processing
Physical separation
Notes: Prior to pyrometallurgical processing, pre-treatment – in most cases only dismantling of electronic components and some grinding might be required. Once the waste printed circuit boards are stripped of electronic components and ground to required size, one of several methods is utilized. Incineration is considered a traditional process which is simple, low-cost and effective with a benefit of possible energy recovery. Circuit boards are fed into high temperature furnaces under aerobic conditions. Organic components are thermally decomposed, leaving a residue composed of glass-fibers (and possibly other non-volatile non-metallic materials such as ceramics) and metal oxides. These residues are then separated by using physical separation methods to prepare concentrates of non-ferrous metals, ferrous-metals and tailings composed of the non-metallic materials.
Pyrolysis uses a temperature of between 350 and 900 degrees Celsius in anaerobic conditions (in the presence of inert gasses) for a thermochemical decomposition of organic resins. Products of pyrolysis are then condensed leaving pyrolysis oil and gasses which can be used as a fuel. Residues are non-metal materials (glass fibers) and metals which can be again effectively separated by physical methods.
Plasma treatment also uses decomposition of organic resins, similar to incineration. However, temperature in the furnaces by using high efficiency arc plasma is high enough to also melt glass fibers into a vitreous body. The resulting gases, vitreous body and remaining metals can be effectively separated.
In the molten salt method, molten salt is used to separate liquid or solid-state metal products at high temperature in a u-shaped reactor filled with liquid. The salt must be stable and inert - usually sodium hydroxide or potassium hydroxide eutectics used to dissolve glasses, oxides and to destruct plastics present in wastes without oxidizing the most valuable metals.. This method can effectively recycle copper-rich metal fractions and remove the glass fiber and resin components in waste printed circuit boards.

## Slide 64
Biometallurgy has been utilised in the form of bioleaching for metal extraction and biosorption for metal recovery in mineral processing.
Bioleaching has been tested for potential metal recovery from electronic scrap material yet it remains at naïve state for lab scale operations

## Slide 65: occupational and environmental health perspectives of recycling e-waste in India.