## Slide 1: ROBOT PROGRAMMING
Programming is the identification and specification of a series of basic actions which, when executed in the specified order, achieve some specific task or realize some specific process.
Robot Programming is the defining of desired motions so that the robot may perform them without human intervention.
According to the consistent performance by the robots in industries, the robot programming can be divided in two common types such as:
        Lead through Programming Method ( online Programming)
        Off-line Programming
  Lead through Programming Method:
  During this programming method, the traveling of robots is based on the desired movements, and it is stored in the external controller memory. There are two modes of a control system in this method such as a run mode and teach mode. The program is taught in the teach mode, and it is executed in the run mode.

## Slide 2: ROBOT PROGRAMMING
The lead through programming method can be done by two methods.
  Powered Lead through Method:
    The powered lead through is the common programming method in the industries. A teach pendant is incorporated in this method for controlling the motors available in the joints. It is also used to operate the robot wrist and arm through a sequence of points.
    The playback of an operation is done by recording these points.
    The control of complex geometric moves is difficult to perform in the teach pendant.
    As a result, this method is good for point to point movements. Some of the key applications are spot welding, machine loading & unloading, and part transfer process.

## Slide 3: ROBOT PROGRAMMING
  Manual Lead through Method
    In this method, the robot’s end effector is moved physically by the programmer at the desired movements.
    Sometimes, it may be difficult to move large robot arm manually.
    To get rid of it a teach button is implemented in the wrist for special programming.
    The manual lead through method is also known as Walk Through method.
    It is mainly used to perform continuous path movements. This method is best for spray painting and arc welding operations.

## Slide 4: ROBOT PROGRAMMING
  Lead through programming is not readily compatible with modern computer based technology.
Advantages:
  Easy
  No special programming skills or training
Disadvantages:
  Robot cannot be used in production, while it is being programmed.
  not practical for large or heavy robots
  High accuracy and straight-line movements are difficult to achieve, as are any other kind of geometrically defined trajectory, such as circular arcs, etc.
  difficult to edit out unwanted operator moves
  difficult to incorporate external sensor data
  Synchronization with other machines or equipment in the work cell is difficult
  A large amount of memory is required

## Slide 5
Robot Offline Programming Methods
Definition: Offline programming is a method of programming industrial robots on a computer workstation without stopping production or physically teaching the robot with a pendant. The program is created, tested, and simulated offline, and then transferred to the robot controller for execution.
This is widely used in industries such as automobile, aerospace, painting, welding, assembly, and machining where downtime is very costly.

## Slide 6
Methods of Offline Programming
Manual Coding (Text-based Programming)
  The programmer writes the robot’s movements and logic using a robot programming language (such as VAL, RAPID, KRL, or TRL).
  Motion commands (MOVE, APPROACH), I/O control (ON/OFF signals), and logic statements are written as text.
  Requires deep knowledge of robot kinematics and coordinate systems.
  Advantage: Very flexible, precise control.
  Limitation: Time-consuming and prone to errors if not verified with simulation.

## Slide 7
Methods of Offline Programming
CAD-based Programming
  The robot program is generated directly from a CAD (Computer-Aided Design) model of the workpiece and workspace.
  The software automatically extracts tool paths from the CAD geometry (e.g., surface paths for painting, cutting, or welding).
  The robot trajectory is then simulated in 3D.
  Advantage: Fast generation of complex paths.
  Limitation: Requires accurate CAD models and calibration.

## Slide 8
Methods of Offline Programming
Simulation-based Programming
  Uses dedicated robot simulation software (e.g., RoboDK, ABB RobotStudio, FANUC ROBOGUIDE, Siemens Process Simulate).
  The entire robot cell (robot, tools, fixtures, conveyors) is modelled in a virtual environment.
  The programmer defines the path, speed, and process in the simulator, checks for collisions, reachability, and cycle time, and then downloads the program to the real robot.
  Advantage: No production stoppage, safe testing.
  Limitation: Requires powerful software and calibration to match real-world accuracy

## Slide 9
  The benefits of this form of programming are:-
        Reduced down time for programming.
        Programming tools make programming easier.
        Simplification of complex tasks
        Optimization of robot programs
        Access control
        Reduction of the robot operating time
        Single robot programming system
        Integration of CAD / CAM systems
        Cycle time analysis
        Verification of robot programs

## Slide 10: ROBOT PROGRAMMING
Programming Languages for Robotics:
There are many programming languages which will use while building Robots, a few programming languages which are always prefer to use in designing.
Actually the programming languages which can be used mainly depend on the hardware used to the building robots.
URBI : URBI stands for Universal Real-time Behaviour Interface.
It is a client/server based interpreted language in which Robot works as a client and controller as a server.
It makes us to learn about the commands which we give to Robots and receive messages from them.
The interpreter and wrapped server are called as "URBI Engine". The URBI Engine uses commands from Client and receives messages to it.
This language allows user to work on basic Perception-action principle. The users just have to write some simple loops on the basis of this principle directly in URBI.

## Slide 11: ROBOT PROGRAMMING
Programming Languages for Robotics:
PYTHON : There is another language which is used in designing Robots.
Python is an object-oriented language which is used to access and control Robots.
Python is an interpreted language; this language has an application in working with mobile robots, particularly those manufactured by different companies.
With python it is possible to use a single program for controlling many different robots. However Python is slower than C++ but it has some good sides as well as it proved very easy to interact with robots using this language, it is highly portable and can be run in windows and MAC OSX plus it can easily be extendable using C and C++ language.
Python is a very reliable language for string manipulation and text processing.
ROBOTC is another programming language which is C-based.
It is actually a text based programming language.
The commands which we want to give to our Robot, first written on the screen in the form of simple text, now as we know that Robot is a kind of machine and a machine only understands machine language. So these commands need to be converted in machine language so that robot can easily understand and do whatever it is instructed to do.

## Slide 12: ROBOT PROGRAMMING
Programming Languages for Robotics:
Microsoft Robotics Developer Studio is an environment given for simulation purpose of Robots.
It is based on a .net library concurrent implementation. This environment has support so that we can add other services as well.
It has features which not only include creating and debugging Robot Applications but also it becomes easy to interact with sensors directly.
C programming language is used as a primary language in it.
If we want to graphics and visual effects in our programming, we use VPL.
Visual Programming language is a programming language which allows us to create programs by doing manipulations in programming languages graphically.
We use boxes and arrows in this kind of programming while we want to show dataflow kind of things.

## Slide 13: ROBOT PROGRAMMING
Textual Robot Languages:
In 1973, WAVE language was developed, and it is the first textual robot language as well. It is used to interface the machine vision system with the robot.
Trajectory calculations through coordination of joint movements, end-effector positions and touch sensing were some of the new features of WAVE. But the algorithm was too complex and not user-friendly.
Then AL language was introduced in 1974 for controlling multiple robot arms during arm coordination.
VAL was invented in 1979, and it is the common textual robot language. Later, this language was updated in 1984, and called as VAL II.
The IBM Corporation has established their two own languages such as AML and AUTOPASS, which is used for the assembly operations.
AML is very useful for assembly operations as different user—robot programming interfaces are possible. The programming language AML is also used in other automated manufacturing systems.
Other important textual robot languages are Manufacturing Control Language (MCL), RAIL, and Automatic Programmed Tooling (APT) languages.

## Slide 14: ROBOT PROGRAMMING
Textual Robot Languages:
Other important textual robot languages are Manufacturing Control Language (MCL), RAIL, and Automatic Programmed Tooling (APT) languages.
US Air force ICAM project led to the development of another manufacturing control language known as MCL by McDonnel—Douglas. This is a modification of the popular APT (Automatically Programmed Tooling) language used in CNC machine tools as many similar commands are used to control
RAIL Was developed by Automatic for robotic assembly, inspection, arc Welding and machine vision.
A variety of data types as used in PASCAL can be used. It uses Motorola 68000 type microcomputer system; It supports many commands and control of the vision system.
HELP was developed by General Electric Company. It acts more or less like RAIL. It has the capability to control two robot arms at the same time. The structure of the language is like PASCAL.
JARS was developed by NASA JPL. The base of the language is PASCAL. JARS can be interfaced with PUMA 6000 robot for running robotic programs.

## Slide 15: ROBOT PROGRAMMING
Textual Robot Languages:
RPL was developed at SRI International. A compiler is used to convert a program into the codes that can be interpreted by an interpreter. Unimation PUMA 500 can be controlled with the help of RPL. The basic ideas of LISP (an Al language) have been organized into a FORTRAN-like syntax in RPL. It is modular and flexible.
Besides these, there are some other languages like PAL, ADA etc. PAL has been written by Richard Paul by modifying WAVE and incorporating features of PASCAL. But the representations of syntaxes used in the program are difficult to handle. ADA developed by the Department of Defense (DOD) in USA is a real-time system that can be run on several microcomputers like Zilog, VAX, Motorola 68000, etc. ADA is convenient for controlling the robots used in a manufacturing cell.
Different textual robot languages have different attributes. Far example, VAL, HELP and MC though powerful for many simple tasks, do not have the same structured modular programming capability like AL, AML, JARS and ADA or VAL II. In a manufacturing cell, multiple robots or robotic equipment work in unison. Control of two or more operations done by the robots in a coordinated manner is complex .

## Slide 16
PROGRAM PICK_PLACE
; Define positions
POINT P1 = (100, 200, 300) ; Pick-up location
POINT P2 = (150, 250, 300) ; Place location
POINT HOME = (0, 0, 500) ; Home position (safe)
; Start program
MOVE HOME ; Move robot to home position
APPROACH P1, 50 ; Move near pick-up point (50 mm above)
MOVE P1 ; Move to pick-up point
CLOSE GRIPPER ; Close gripper to hold the object
DEPART P1, 50 ; Move away safely from pick point
APPROACH P2, 50 ; Move near place location (50 mm above)
MOVE P2 ; Move to place location
OPEN GRIPPER ; Release the object
DEPART P2, 50 ; Move away safely
MOVE HOME ; Return to home position
END PROGRAM
Explanation
POINT P_PICK / P_PLACE / P_HOME → predefined Cartesian coordinates of pick, place, and home positions.
MOVE → moves the robot arm to a specific point.
APPROACH / DEPART → safe approach and retreat motions above/below a target location.
GRIP ON / OFF → activates/deactivates the end effector (gripper).
BEGIN / END → marks the start and end of the program.

## Slide 17
Write a Program for machine loading and unloading
Task Assumptions
The robot picks a raw part from a tray (location P_TRAY).
It loads the part into a CNC machine chuck (location P_MACHINE_LOAD).
After machining (simulated by a wait), it unloads the finished part from the machine (location P_MACHINE_UNLOAD).
It places the finished part onto an output tray (location P_OUTPUT_TRAY).

## Slide 18
PROGRAM MACHINE_LOAD_UNLOAD
; Move to tray and pick raw part
MOVE P_TRAY
CLOSE GRIPPER
DEPART 50 ; Move back by 50 mm for clearance
; Load part into machine
MOVE P_MACHINE_LOAD
OPEN GRIPPER
DEPART 50
; Wait for machining to finish (simulation)
WAIT 30 ; 30 seconds machining time
; Unload finished part
MOVE P_MACHINE_UNLOAD
CLOSE GRIPPER
DEPART 50

## Slide 19
; Wait for machining to finish (simulation)
WAIT 30 ; 30 seconds machining time
; Unload finished part
MOVE P_MACHINE_UNLOAD
CLOSE GRIPPER
DEPART 50
; Place finished part on output tray
MOVE P_OUTPUT_TRAY
OPEN GRIPPER
DEPART 50
END PROGRAM
Explanation
MOVE P_TRAY → robot moves to tray position.
CLOSE GRIPPER → grips the raw part.
DEPART 50 → backs away from current position by 50 mm for safety.
WAIT 30 → waits 30 seconds (representing machine cycle time).
MOVE P_OUTPUT_TRAY → places the finished part on the output tray.
OPEN GRIPPER → releases the part.

## Slide 20
a simple Textual Robot Language (TRL) program for a palletizing operation.
Task Assumptions
The robot picks boxes from an infeed conveyor (P_PICK).
It places them on a pallet, row by row.
The pallet has 3 rows × 3 columns (9 boxes total).
Positions are pre-defined as P_PALLET(ROW, COL).

## Slide 21
PROGRAM PALLETIZING
; Loop through 3 rows
FOR ROW = 1 TO 3
; Loop through 3 columns
FOR COL = 1 TO 3
; Pick box from conveyor
MOVE P_PICK
CLOSE GRIPPER
DEPART 50
; Move to pallet position
MOVE P_PALLET(ROW, COL)
OPEN GRIPPER
DEPART 50
NEXT COL
NEXT ROW
END PROGRAM
Explanation
FOR ROW / COL → Nested loops place boxes in rows and columns automatically.
MOVE P_PICK → Robot goes to conveyor pickup point.
CLOSE GRIPPER → Grips the box.
MOVE P_PALLET(ROW, COL) → Robot places the box at the correct pallet location.
OPEN GRIPPER → Releases the box.

## Slide 22
; Define painting path points
POINT P_HOME = (0, 0, 200)
POINT P_START = (100, 50, 150)
POINT P_END = (300, 50, 150)
POINT P_TOP = (100, 100, 150)
POINT P_BOTTOM = (300, 100, 150)
; Start program
BEGIN
MOVE P_HOME ; Move robot to home position
; Move to start position
APPROACH P_START, 50 ; Approach painting start point from 50 mm above
MOVE P_START ; Move to start point
SPRAY ON ; Turn ON spray gun
; Perform first stroke
MOVE P_END ; Paint along straight line
; Move to next stroke
MOVE P_BOTTOM
MOVE P_TOP ; Paint back stroke
SPRAY OFF ; Turn OFF spray gun
DEPART P_TOP, 50 ; Move away from painted surface
MOVE P_HOME ; Return to home position
END
Explanation
POINTS → define the Cartesian coordinates of painting path.
MOVE → robot moves along the programmed path.
APPROACH / DEPART → ensures safe entry/exit without hitting the surface.
SPRAY ON / OFF → controls the paint spray gun.
Robot moves in a zig-zag / raster pattern, which is common in spray painting to cover a surface uniformly.