## Slide 1: UNIT-III (Decoders, Encoders)

## Slide 2: Contents
Topics :
  Decoders
  Encoders

## Slide 3: DECODER
Discrete quantities of information are represented in digital systems by binary codes.
A decoder is a combinational circuit that has ‘n’ input lines and maximum of 2n output lines.
While decoding, the decoder generally places a logic 1 at one of its outputs to create the exact code.
The general structure of a decoder is shown below. It also has an enable input. When it is set to logic HIGH, the coded output will be seen depending on the binary data input.

## Slide 4: Contd..
Applications
Code converters
Used in the memory system of computers to access a particular memory location based on the address produced by a computing device.
To carry out the operations in the Arithmetic Logic Unit of CPU, decoders are used to decode the program instructions to activate the control lines.

## Slide 5: Contd..
There are different type of decoders based on the number of inputs and its coded output.

## Slide 6: 2 to 4 Line Decoder
In the 2 to 4 line decoder, there is a total of three inputs, i.e., A0, and A1 and E and four outputs, i.e., Y0, Y1, Y2, and Y3.
For each combination of inputs, when the enable 'E' is set to 1, one of these four outputs will be 1.
The block diagram and the truth table of the 2 to 4 line decoder are given below.

## Slide 7: Contd..
Some binary decoders have an additional input pin labelled “Enable” that controls the outputs from the device.
This extra input allows the decoders outputs to be turned “ON” or “OFF” as required.
These types of binary decoders are commonly used as “memory address decoders” in microprocessor memory applications.
Each output represents one of the minterms of the 2 input variables, (each output = a minterm).

## Slide 8: Contd..
By the use of Data Lines it represents the address of memory locations.
Truth Table:
The output values will be: Qo=A’B’ Q1=A’B Q2=AB’ Q3=AB

## Slide 9: Contd..

## Slide 10: 3 to 8 Line Decoder
Block Diagram:
A Decoder with 3 inputs and it gives 8 outputs.

## Slide 11: Contd..
Truth Table:

## Slide 12: Contd..
The logicial expresión of the term Y0, Y1, Y2, Y3, Y4, Y5, Y6, and Y7 is as follows:
Y0=A0'.A1'.A2' Y1=A0.A1'.A2' Y2=A0'.A1.A2' Y3=A0.A1.A2' Y4=A0'.A1'.A2 Y5=A0.A1'.A2 Y6=A0'.A1.A2 Y7=A0.A1.A2

## Slide 13: Contd..
Circuit Diagram:

## Slide 14: Implementing High Order Decoder to Low Order Decoder
Now, let us implement the following two higher-order decoders using lower-order decoders.
1. 3 to 8 decoder
2. 4 to 16 decoder
1. 3 to 8 Decoder: let us implement 3 to 8 decoder using 2 to 4 decoders. We know that 2 to 4 Decoder has two inputs, A1 & A0 and four outputs, Y3 to Y0. Whereas, 3 to 8 Decoder has three inputs A2, A1 & A0 and eight outputs, Y7 to Y0.

## Slide 15: Contd..

## Slide 16: Contd..
We can find the number of lower order decoders required for implementing higher order decoder using the following formula.

## Slide 17: Contd..
Block Diagram:
Step-1:
Step-2:

## Slide 18: Contd..
Step-3:

## Slide 19: Contd..
Step-4: Both the decoders have the enable line for the 3rd input Z.

## Slide 20: Contd..
For Example

## Slide 21: 4 to 16 Decoder
Here, 4 to 16 decoder using 3 to 8 decoders.
We know that 3 to 8 Decoder has three inputs A2, A1 & A0 and eight outputs, Y7 to Y0.
Whereas, 4 to 16 Decoder has four inputs A3, A2, A1 & A0 and sixteen outputs, Y15 to Y0:

## Slide 22: Contd..
Therefore, we require two 3 to 8 decoders for implementing one 4 to 16 decoder. The block diagram of 4 to 16 decoder using 3 to 8 decoders is shown in the following figure.

## Slide 23: Contd..
The parallel inputs A2, A1 & A0 are applied to each 3 to 8 decoder.
The complement of input, A3 is connected to Enable, E of lower 3 to 8 decoder in order to get the outputs, Y7 to Y0. These are the lower eight min terms.
The input, A3 is directly connected to Enable, E of upper 3 to 8 decoder in order to get the outputs, Y15 to Y8. These are the higher eight min terms.

## Slide 24: Combinational Logic Implementation
Example-1: we obtain the functions for the combinational circuit in sum-of-minterms form:
S(x, y, z) = (1, 2, 4, 7)
C(x, y, z) = (3, 5, 6, 7)

## Slide 25: Contd..

## Slide 26: ENCODER
An Encoder is a Digital Circuit that performs the reverse operation of the Decoder.
It has maximum of 2n input lines and ‘n’ output lines.
At a time, only one input line is activated for simplicity.
It is optional to represent the enable signal in encoders.
There are various types of Encoders .
  4- 2 Encoder
  8- 3 Encoder
  10- 4 Encoder and many more

## Slide 27: Contd..
Block Diagram:

## Slide 28: 4 – 2 Encoder
In 4 to 2 line encoder, there are total of four inputs, i.e., Y0, Y1, Y2, and Y3, and
In 4-input lines, one input-line is set to true at a time to get the respective binary code in the output side.
Below are the block diagram and the truth table of the 4 to 2 line encoder.

## Slide 29: Contd..
Truth Table:
From Truth table, we can write the Boolean functions for each output as: A1=Y3+Y2
A0=Y3+Y1

## Slide 30: Contd..
Circuit Diagram:
The above Circuit Diagram contains Two OR Gates.

## Slide 31: 8-3 Encoder or (Octal to Binary)
The 8 to 3 Encoder or octal to Binary encoder consists of 8 inputs : Y7 to Y0 and 3 outputs : A2, A1 & A0. Each input line corresponds to each octal digit and three outputs generate corresponding binary code.
In 8-input lines, one input-line is set to true at a time to get the respective binary code in the output side.

## Slide 32: Contd..
Truth Table:
From Truth table, we can write the Boolean functions for each output as
A2=Y7+Y6+Y5+Y4
A1=Y7+Y6+Y3+Y2
A0=Y7+Y5+Y3+Y1

## Slide 33: Contd..
Circuit Diagram:

## Slide 34: Decimal to BCD Encoder
The Octal to Binary Encoder is also known as 10 to 4 line Encoder. In 10 to 4 line encoder, there are total of ten inputs, i.e., Y0, Y1, Y2, Y3, Y4, Y5, Y6, Y7, Y8, and Y9 and four outputs, i.e., A0, A1, A2, and A3.
In 10-input lines, one input-line is set to true at a time to get the respective BCD code in the output side

## Slide 35: Contd..
Truth Table:

## Slide 36: Contd..
From Truth table, we can write the Boolean functions for each output as
A3 = Y9 + Y8 A2 = Y7 + Y6 + Y5 +Y4 A1 = Y7 + Y6 + Y3 +Y2 A0 = Y9 + Y7 +Y5 +Y3 + Y1

## Slide 37: Contd..
Circuit Diagram: