## Slide 1: Outline of today’s session
Conversion of flip-flop
  Procedure
  Conversions
    SR JK,T,D
    JK SR,T,D
    T SR,JK,D
    D SR,JK,T

## Slide 2: Necessity of conversion
JK flip – flops and D flip – flops are the most widely used flip – flops. And so their availability in the form of integrated circuits (IC’s) is abundant. Numerous varieties of JK flip – flop and D flip – flop are available in the semiconductor market.
The less popular SR flip – flop and T flip – flop are not available in the market as integrated circuits (IC’s) (even though a very few number of SR flip – flops are available as IC’s, they are not frequently used). There might be a situation where the less popular flip – flops are required in order to implement a logic circuit.
In order use the less popular flip – flops, we will convert one type of flip – flop into another.

## Slide 3: Procedure to convert one flip flop into other
Step 1: Identify available and required Flip flop.
Step 2: Make the characteristic table for required Flip flop.
Step 3: Make the excitation table for available Flip flop.
Step 4: Make the conversion table
Step 5: Write the Boolean expression for inputs of available Flip flop.
Step 6: Draw the circuit.

## Slide 4: SR Flip – flop to JK Flip – flop
Write the characteristic table for the two inputs J and K. For two inputs along with the Qt, we get 8 possible combinations in characteristic table.
For every combination of J, K ,Qt , we find the corresponding Qt+1 state.
Using these Qt and Qt+1 , we write the values of S and R, using Excitation table
This table is called Conversion table.

## Slide 5: Conversion table : SR JK

## Slide 6: K-Maps: SR JK
The K – map for S is shown below:
The K – map for R is shown below:
S=JQ1t
R=KQt

## Slide 7: SR JK, D, T
SR FF to JK FF(Flipflop) conversion equation
S = J*Qt' R = K*Qt
SR FF to D FF(Flipflop) conversion equation
S = D R =D'
SR FF to T FF(Flipflop) conversion equation
S = T*Qt' R = T*Qt

## Slide 8: JK SR, D, T
JK FF to SR FF(Flipflop) conversion equation
J = S K = R
JK FF to D FF(Flipflop) conversion equation
J = D K = D'
JK FF to T FF(Flipflop) conversion equation
J = K = T

## Slide 9: D SR, JK, T
D FF to SR FF(Flipflop) conversion equation
D = S + R'*Qt
D FF to JK FF(Flipflop) conversion equation
D = J*Q‘t + K'*Qt
D FF to T FF(Flipflop) conversion equation
D = T (ex-or) Qt

## Slide 10: T SR, JK, D
T FF to JK FF(Flipflop) conversion equation
T = J*Q't + K*Qt
T FF to SR FF(Flipflop) conversion equation
T = S*Q't + R*Qt
T FF to D FF(Flipflop) conversion equation
T = D (ex-or) Qt

## Slide 11: Flip-Flop With Asynchronous Inputs (Preset And Clear)
Asynchronous inputs on a flip-flop have control over the outputs (Q and Q1) regardless of clock input status.
These inputs are called the preset (PRE) and clear (CLR).
The preset input drives the flip-flop to a set state while the clear input drives it to a reset state.
PRESET Set state
CLEAR Reset state

## Slide 12: Asynchronous Inputs (Preset And Clear)
Asynchronous inputs, just like synchronous inputs, can be engineered to be active-high or active-low.
If they’re active-low, there will be an inverting bubble at that input lead on the block symbol, just like the negative edge-trigger clock inputs.
Active HIGH
Active LOW

## Slide 13: Asynchronous Inputs (Preset And Clear)
When the preset input is activated, the flip-flop will be set (Q=1, not-Q=0) regardless of any of the synchronous inputs or the clock.
When the clear input is activated, the flip-flop will be reset (Q=0, not-Q=1), regardless of any of the synchronous inputs or the clock.
If both preset and clear inputs are activated we get an invalid state on the output.

## Slide 14
THANK YOU